## Slide 1
Research on Factors Influencing the Use of Rail Transit
CHEN Qi
Graduate School of Human-Environment Studies,
Kyushu University, Japan
May 22, 2018

## Slide 2
General flowchart of the dissertation
0.0

## Slide 3
Chapter 1
Introduction
Background
Research purpose
Literature review
Primary research questions
Dissertation organization

## Slide 4
Chapter 1 - Introduction
Background
1.1
How is the research topic proposed?
Current situation
Requirement according to the situation
Measures for the requirement
Developed countries
Developing countries
Rapid urbanization, severe congestion, pollution.
lack of resources
Aged society, low birthrate, high public financial expenditure
fiscal burden
sustainability
Increase supply
Improve financial situation
Topic
explore the determinants of rail transit ridership
Increase public transportation utilization

## Slide 5
Chapter 1 - Introduction
Purpose
1.2
How to encourage people to take rail transit?
What explains rail transit ridership?
How to increase the rail transit ridership?
What we want to do?
explore the determinants of rail transit ridership
Main purpose
1. What determines catchment area?
2. What factors explain transit ridership at station level?
3. What factors influence transit ridership among stations?
Subject topics to discussion

## Slide 6
Year |  | 2004 | 2004 | 2009 | 2010 | 2011 | 2012 | 2013 | 2013 | 2015
Author |  | Chu | Kuby et al. | Taylor et al. | Sohn and Shim | Gutiérrez et al. | Cardozo et al. | Chakraborty et al. | Zhao et al. | Jun et al.
Catchment (walking distance) |  | 400m walking distance | 800m walking distance | N/A | N/A | Distance-decay 800m buffer | 800m walking distance | N/A | 800m radius | 300m,600m,900m radius
Method |  | Poisson Regression | WLS | 2SLS | OLS/SEM | OLS | OLS/GWR | OLS/SEM | OLS | OLS/MGWR
Sample Size |  | 2568 | 268 | 265 | 251 | 158 | 190 | 900 | 55 | 442
Number of Valid Indicator |  | 15 | 11 | 8 | 7 | 9 | 4 | 9 | 11 | 11
Coefficient of determination (Adjusted R2) |  | 0.54 | 0.71 | 0.91 | 0.60 | 0.73 | 0.56 | 0.69 | 0.95 | 0.77
Building environment | Built environment |  |  |  | ● | ● |  | ● | ● | ●
 | Hospital |  |  |  |  |  |  |  | ● | 
 | School/University |  |  |  | ● |  |  |  | ● | 
 | CBD |  | ● |  |  |  |  |  | ● | 
 | Land use mix |  |  |  | ● | ● | ● |  |  | ●
 | Other infrastructures |  | ● |  |  |  |  |  | ● | ●
Transportation Accessibility | Accessibility of pedestrian | ● |  |  |  |  |  | ● |  | 
 | Accessibility of transfer |  | ● |  | ● | ● | ● | ● | ● | ●
 | Road coverage |  |  | ● | ● |  |  |  | ● | 
 | Parking |  | ● |  |  |  |  |  | ● | 
 | Service level of public transit | ● | ● | ● |  | ● | ● |  | ● | ●
 | Locational factor |  | ● |  | ● |  |  |  | ● | 
Demographic and Socioeconomic Environment | Population |  | ● | ● | ● |  | ● | ● | ● | ●
 | Employment | ● | ● | ● | ● | ● | ● | ● | ● | ●
 | Age | ● |  | ● |  |  |  |  |  | ●
 | Tenant proportion |  | ● |  |  |  |  |  |  | ●
 | Race | ● | ● | ● |  | ● |  |  |  | 
 | Income | ● |  |  |  |  |  | ● |  | 
 | Vehicles holdings | ● |  |  |  |  | ● | ● |  | 
 | Fare |  |  | ● |  |  |  |  |  | 
Chapter 1 - Introduction
Review
1.3

## Slide 7
Chapter 1 - Introduction
Questions
1.4
Exploring the relationship between walking distance and walking preference, and trying to explain the catchment area.
Analyzing the characteristics in the variation of transit ridership.
Exploring the approach for screening effective influencing factors.
Shifting the research perspective, trying to describing the relationship between stations and stations.
Specific research questions based on the research purpose and paper review

## Slide 8
Chapter 1 - Introduction
Organization
1.5
Chapter 1
Introduction
Chapter 2
Analyzing the Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Chapter 3
Analysis on the characteristics of transit ridership and land use
Chapter 4
Influencing Factors on Transit Ridership at Station Level
Chapter 5
Influencing Factors on Transit Ridership at Station-to-Station Level
Chapter 6
Conclusion

## Slide 9
Chapter 2
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
Methods
Data description
Selection for Valid Features
Estimation of Features
Result and Discussion
Conclusion

## Slide 10
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Catchment area
objective
Influencing factor
Built-environment
Facilities
Behaviors
Research Point
(This Study)
Personal Socio-Demographic Characteristics
(abbreviated as PSDC)
Walking duration to transit stations
Relationship
Research position
Acceptable walking distance/duration

## Slide 11
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Realistic issue
As an example, for one person who has the attributes:
8 min
4 min
OK
I can accept a walking duration less than 8 minutes
0 min
Reflected in questionnaire
This time I walked 6 minutes to the station
0 min
6 min
Problem description

## Slide 12
In a general way
Walking duration obtained from questionnaire
Acceptable walking duration
Where the minutes is the reflection of the duration between departures and stations
Where the minutes is the acceptable walking duration for the people with those factors
Deviation is appeared
The general expression can be:
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1

## Slide 13
The work of this study
Explorer how the PSDC can affect the acceptable walking duration to transit stations.
Threshold of walking duration
Continuous value of Walking duration
Research purpose
Research object
Entry point
Try to explain the acceptable walking duration using probability.
Examine the probability at the given threshold of walking duration
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1

## Slide 14
6 min
If considering the threshold of 6 minutes
Group 1
Group 2
All Samples
minute
Probability
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Assuming the walking duration distribution of the passengers with the same attributions subject to the normal distribution.
If the survey result obtained from the questionnaire showed one group of passengers with a specific PSDC tend to walk longer, it means this group of passengers can accept a longer walking duration.
In this graph it can be considered that Group 1 can accept a longer walking duration than Group 2
Important assumption

## Slide 15
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Where: means the given threshold of walking duration
represents the probability of accepting or not at the threshold of minutes.
Model construction
Abstract form of the model
PSCD

## Slide 16
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data description
2.3
Distribution of the transit stations
data in this study
Study case: Fukuoka

## Slide 17
Data description
2.3
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data disposal
Source: Person Trip Survey

## Slide 18
Data description
2.3
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
The age distribution of passengers
Distribution of walking duration
Distribution verification
Subject to normal distribution, the samples can be viewed valid.
People are inclined to reply a looser answer when they are being asked some questions about details.
There are peak values at 5, 10, 15 min

## Slide 19
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Selection for Valid Features
2.4
Selection of thresholds
The thresholds selected in this study is 5, 8, 13 minutes.
According to the existing studies, the acceptable walking duration mainly range from 5 – 13 minutes.
In this study, the average walking duration is about 8 minutes.
Analysis of variance
L : tend to spend Less than the threshold
M: tend to spend more than the threshold
Valid Features at each threshold

## Slide 20
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Selection for Valid Features
2.4
Analysis of variance
L : tend to spend Less than the threshold
M: tend to spend more than the threshold
Valid Features at each threshold

## Slide 21
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Estimation of Features
2.5
The rationality of model selection
Decision tree and forest random models
Binary choice issue
Good generalization for different forms of data
Forest random model is constructed by random selection of features and samples based on decision tree model.
The result is obtained by the average value of multiple decision trees.
Decision tree
Bayesian model
Support vector machine
Artificial neural networks
…
Logistic regression

## Slide 22
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Estimation of Features
2.5
Individual Value |  | Group Trend | 
Actual | Predicted | Actual | Predicted
1 | 1.000 | 0.654 | 0.637
1 | 0.897 | 0.653 | 0.636
1 | 0.897 | 0.651 | 0.635
… | … | … | …
0 | 0.621 | 0.581 | 0.580
1 | 0.621 | 0.581 | 0.579
1 | 0.621 | 0.580 | 0.579
… | … | … | …
0 | 0.498 | 0.435 | 0.411
1 | 0.496 | 0.437 | 0.411
1 | 0.496 | 0.434 | 0.410
… | … | … | …
Prediction
The predicted result is probabilities of accepting the giving threshold of walking duration.
The accuracy of results are evaluated by using the method of simple moving average.
Simple moving average

## Slide 23
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of prediction
Evaluation of 5 minutes threshold
Possible explanation: The threshold of 5 minute is a commonly acceptable walking duration, some one who cannot accept this threshold can be considered to have some specific characteristics. The features are significant at this threshold.
High precision

## Slide 24
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of prediction
Evaluation of 8 minutes threshold
Possible explanation: There may be some randomness in making the decision of whether walking to transit stations at the 8 minutes threshold. People may have some ambiguity in choosing whether to accept or not. The features are not significant at this threshold.
Low precision

## Slide 25
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of prediction
Evaluation of 13 minutes threshold
Possible explanation: The threshold of 13 minute is not a commonly acceptable walking duration, some one who can accept this threshold can be considered to have some specific characteristics. The features are significant at this threshold.
Slightly high precision

## Slide 26
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Achievement in this study
Probability of accepting the given threshold of walking duration
Station
A
C
B
13 min
8 min
5 min
Block
Application of this achievement
Superior Topic
Exploring the use tendencies of urban rail transit
Model
The trend (probability) of using this station in the blocks can be grasped.
PSDC data in the blocks (e.g. A/B/C)
input
output

## Slide 27
Chapter 3
Analysis on the characteristics of transit ridership and land use
Introduction
Data
Characteristics of transit ridership and land use
Influencing factors of transit ridership
Conclusion

## Slide 28
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problem
Aging population
Reduction in share rate of public transit
Traffic congestion
Demand
Promoting the use of rail transit
Alleviating the pressure on government finances
Making a better living environment for residents
Background

## Slide 29
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Research position
Master the characteristics
Preliminary study
Transit ridership
Influencing factor
Station level
Station-to-station level
Explore the influence
Relationship
Chapter 4
Chapter 5
Provide foundation for estimating the influence

## Slide 30
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
To describe the characteristics of transit stations in terms of both transit ridership and land use
To explore the relationship between transit ridership and land use on the base of intensive description on the characteristics of transit stations.
Purpose

## Slide 31
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
Fukuoka subway
3 Lines
35 Stations
30km operating distance
600, 000 passengers per day
20% of total motorized travel
Study case

## Slide 32
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
Data collection

## Slide 33
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
Data collection
1. Matching the region of data.
2. Matching the time points of data.
3. Extracting the data within the catchment area.

## Slide 34
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Three line carries more than 0.5 million passengers per day
Line 1 accounts for the most reaching about 0.5 million
Transit ridership characteristics
Line 3 had a much higher growth rate at the first few years of the opening
The growth rate of three lines tend to be stable after the year of 2009

## Slide 35
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership | Total | Line 1 | Line 2 | Line 3
Hub | 2 | 2 | 0 | 0
Large | 4 | 3 | 0 | 1
Medium | 11 | 8 | 1 | 2
Small | 18 | 0 | 4 | 4
Growth rate | Total | Line 1 | Line 2 | Line 3
0-2.5 | 12 | 8 | 4 | 0
2.5-4.5 | 11 | 5 | 2 | 4
4.5-6.0 | 6 | 0 | 0 | 6
6.0- | 6 | 0 | 0 | 6
Transit ridership characteristics

## Slide 36
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics

## Slide 37
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics

## Slide 38
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
Factor 1: Ofﬁce & commerce
This factor represents the land use mainly including ofﬁce area, large commercial area, and some commercial supporting facilities.
Factor 2: Mixed residence
The indicators of apartment, residence, and culture mainly attribute to this factor, which can reﬂect the attribute of residence with supporting facilities.
Factor 3: Education
Except for the indicator of education, the indicator of government also at tributes a large part of this factor. It means that the land use of education and government have a relatively strong correlation.

## Slide 39
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use - classification
Type | Station | Population-density | Business | Commerce | Residence | Government | Education
Low-density residence | 30 | 33 | 1.70% | 41.50% | 44.95% | 0.01% | 0.18%
 | 26 | 54 | 2.81% | 1.23% | 58.26% | 0.00% | 2.85%
 | 29 | 78 | 3.02% | 5.40% | 75.86% | 0.00% | 6.94%
 | 27 | 79 | 4.30% | 4.24% | 75.87% | 0.07% | 0.77%
 | 28 | 81 | 3.55% | 3.42% | 73.46% | 0.03% | 6.24%
 | 3 | 91 | 4.01% | 8.58% | 59.97% | 3.04% | 6.25%
 | 33 | 101 | 1.74% | 2.10% | 81.71% | 0.00% | 7.84%
 | 24 | 103 | 2.14% | 2.17% | 66.82% | 0.10% | 8.30%
 | 34 | 109 | 2.38% | 3.28% | 86.12% | 0.01% | 0.86%
 | Average | 81 | 2.85% | 7.99% | 69.23% | 0.36% | 4.47%
This factor represents the land use mainly including ofﬁce area, large commercial area, and some commercial supporting facilities.

## Slide 40
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use - classification
Type | Station | Population-density | Business | Commerce | Residence | Government | Education
High-density residence | 19 | 121 | 2.17% | 3.15% | 76.63% | 2.77% | 0.12%
 | 13 | 125 | 11.11% | 6.48% | 46.08% | 1.29% | 4.51%
 | 16 | 142 | 4.59% | 5.03% | 72.75% | 1.43% | 2.68%
 | 18 | 142 | 2.27% | 1.96% | 64.58% | 4.81% | 6.80%
 | 31 | 143 | 4.14% | 2.26% | 54.17% | 0.51% | 18.28%
 | 17 | 144 | 6.02% | 7.28% | 55.45% | 0.74% | 10.60%
 | 12 | 145 | 4.16% | 1.77% | 66.22% | 0.19% | 4.39%
 | 32 | 170 | 1.17% | 1.28% | 73.54% | 0.73% | 9.93%
 | 23 | 193 | 10.00% | 6.18% | 44.52% | 0.04% | 2.56%
 | Average | 151 | 5.43% | 4.03% | 59.66% | 1.22% | 7.47%
The indicators of apartment, residence, and culture mainly attribute to this factor, which can reﬂect the attribute of residence with supporting facilities.

## Slide 41
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use - classification
Type | Station | Population-density | Business | Commerce | Residence | Government | Education
Education | 25 | 35 | 1.38% | 2.31% | 30.04% | 0.00% | 39.83%
 | 1 | 56 | 8.70% | 1.91% | 48.01% | 0.53% | 17.89%
 | 35 | 58 | 5.63% | 3.78% | 55.18% | 0.07% | 21.37%
 | 4 | 67 | 4.93% | 3.49% | 33.52% | 13.55% | 14.63%
 | 2 | 77 | 4.03% | 11.75% | 44.03% | 0.81% | 23.24%
 | 5 | 89 | 11.53% | 7.26% | 30.51% | 8.90% | 7.30%
 | Average | 64 | 6.03% | 5.08% | 40.22% | 3.98% | 20.71%
Except for the indicator of education, the indicator of government also attributes a large part of this factor. It means that the land use of education and government have a relatively strong correlation.

## Slide 42
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use - classification
Type | Station | Population-density | Business | Commerce | Residence | Government | Education
Downtown commerce | 9 | 64 | 44.97% | 20.55% | 10.62% | 2.17% | 0.70%
 | 20 | 67 | 34.60% | 36.74% | 11.34% | 3.01% | 1.26%
 | 8 | 67 | 42.97% | 27.86% | 12.23% | 0.16% | 0.59%
 | 11 | 79 | 37.12% | 17.38% | 18.47% | 2.50% | 1.89%
 | 10 | 92 | 30.76% | 26.26% | 15.72% | 2.55% | 1.74%
 | Average | 74 | 38.08% | 25.76% | 13.68% | 2.08% | 1.24%
The type of downtown commerce includes 5 stations, which constituted the CBD area of Fukuoka. These stations have the highest proportion of ofﬁce and commerce, while proportion of residence is the lowest and population
density is relatively lower.

## Slide 43
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use - classification
Type | Station | Population-density | Business | Commerce | Residence | Government | Education
Business | 15 | 64 | 31.63% | 7.80% | 25.80% | 4.39% | 5.73%
 | 6 | 96 | 34.56% | 17.29% | 21.61% | 0.10% | 1.75%
 | 14 | 105 | 26.97% | 17.27% | 17.61% | 3.74% | 2.80%
 | 21 | 136 | 22.86% | 16.12% | 33.66% | 0.16% | 2.70%
 | 22 | 167 | 21.38% | 12.53% | 36.79% | 0.04% | 2.50%
 | Average | 114 | 27.48% | 14.20% | 27.09% | 1.69% | 3.10%
Airport | 7 | 19 | 3.55% | 1.45% | 33.45% | 0.03% | 1.25%
This type includes 5 stations, of which the main land use is ofﬁce. These stations mainly distribute around the CBD area, mixed land use is one of the main characteristics.

## Slide 44
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Influencing factors of transit ridership
3.4

## Slide 45
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Influencing factors of transit ridership
3.4

## Slide 46
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Conclusion
3.4
provided references for selecting more valid indicator to make a prediction in the future research.
Implications for next stage
The determination of catchment area needs more investigation. Since the 800-meter circle catchment does not consider the differences in the form of the road network, the same 800 meters catchment area may represent different walking distance reﬂecting on the real road network.
The selection of indicators explaining the transit ridership needs more exploration. The other categories of indicators about such as facilities, socio-economic, and urban design should also have inﬂuence on the transit ridership.
The selection and usage of estimation model need more investigation. The issue of transit ridership is not only a simple regression problem, but it also relates to the location of stations. A model which is suitable for spatial analysis may be better than an ordinary regression model.
The approach of dealing with small sample case should be considered. Statistical analysis needs a certain sample size, otherwise, it cannot say the estimation result is credible. The problem led by small sample also reﬂects on the procedure of selecting the valid explanatory variables.

## Slide 47
Chapter 4
Influencing Factors on Transit Ridership at Station Level
Introduction
Influencing factors
Identification of valid factors
Model estimation
Residual analysis
Conclusion

## Slide 48
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Weakness in population growth
Tendency of using private transport
The financial pressure of public transport operator
Research Purpose
Explore and explain the factors influencing subway ridership
Explore the handling of small samples in this kind of issue
Research Content
Build the index framework based on prior study;
Identify the valid variables that do affect subway ridership
Estimate the Mix Geographically Weighted Regression model.
Present Situation

## Slide 49
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
 | Walking |  | Bicycle | 
 | Proportion | Ave time | Proportion | Ave time
Average | 78% | 7.2 | 9% | 9.0
median | 85% | 7.0 | 8% | 9.5
Max | 22% | 4.8 | 0% | 0.0
Mix | 100% | 9.2 | 33% | 20.0
Catchment Area of Stations
Range for general
Rang in Fukuoka
Catchment area: walking distance accessing the subway station.
(Pedestrian Catchment Area, PCA)
Thresholds range: 400m ~ 1000m
Most adopted: 800m
Walking speed: about 4.8km/h
Average walking distance is about 600m
It can be inferred that most trips can be included in the range of 800 meters in Fukuoka

## Slide 50
Influencing factors
4.2
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Expected sign | Min Value | Max Value | Average | Unit
Built environment | Commerce | + | 2,921 | 811,281 | 114,353 | m2
 | Office | + | 2,614 | 839,956 | 167,088 | m2
 | Residence | + | 110,748 | 1,067,523 | 528,533 | m2
 | Education | + | 294 | 305,559 | 59,691 | m2
 | Government | + | - | 128,471 | 20,878 | m2
 | Transportation Facility Area | + | 197 | 132,777 | 21,204 | m2
 | Land use Aggregation | + | 0.09 | 0.75 | 0.31 | -
Transportation Accessibility | Transfer Dummy | + | 1 | 4 | 1.34 | -
 | Bicycle Parking | Unknown | 64 | 4,375 | 778 | -
 | Bus Capacity | Unknown | 3 | 260 | 58.48 | -
 | Bus Accessibility | Unknown | 4 | 455 | 89.71 | -
 | Road Density | - | 191 | 479 | 299 | m/ha2
Demographic and Socioeconomic Environment | Population | + | 1,908 | 19,393 | 9,813 | -
 | House Member | - | 1.86 | 2.79 | 2.18 | -
 | Job-Resident Balance | Unknown | 1.27 | 2.61 | 1.80 | -
 | Tenant Proportion | - | 0.15 | 0.65 | 0.43 | %
Dependent variable: average daily subway ridership
Variable Summary

## Slide 51
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable Interpretation
: the average proportion of type land use.
: the type of land use (respectively government, commercial, residence and education)
: the floor area of land use type within catchment area of subway station
Land-use Aggregation
Range of PCA | Residence | Office | Commerce | Education | Total
600 | 51.8% | 19.3% | 13.8% | 5.5% | 90.5%
800 | 55.3% | 17.5% | 12.0% | 6.2% | 90.9%
1000 | 57.6% | 16.5% | 10.8% | 6.0% | 90.9%
1200 | 59.2% | 15.5% | 10.2% | 5.9% | 90.8%
Ave | 62.8% | 10.1% | 7.5% | 5.3% | 85.7%
The indicator of land-use mix is re-defined into the aggregation of land-use.
Average
Influencing factors
4.2

## Slide 52
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Influencing factors
4.2
Variable Interpretation
: is the number of bus lines passing through the th bus station.
: the number of bus stations within catchment area of subway station
: the number of lines in one bus station and
: is the frequency of NO. line at NO. station.
Bus capacity
Bus Accessibility

## Slide 53
Identification of Valid Factors
4.3
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Statistical Information |  |  |  |  | 
 |  | VIF | Validity | stability | times | + | -
 | Total |  |  |  | 367 | 253 | 114
Built environment | Commerce Area | 8.8 | 32.1% | 100.0% | 25 | 25 | 0
 | Office Area | 10.4 | 9.0% | 71.4% | 7 | 5 | 2
 | Residence Area | 27.5 | 12.8% | 70.0% | 10 | 7 | 3
 | Education Area | 1.8 | 7.7% | 100.0% | 6 | 6 | 0
 | Government Area | 1.8 | 42.3% | 100.0% | 33 | 33 | 0
 | Transportation Facility | 3.0 | 67.9% | 100.0% | 53 | 53 | 0
 | Land use Aggregation | 2.5 | 50.0% | 100.0% | 39 | 39 | 0
Transportation Accessibility | Transfer Dummy | 3.0 | 34.6% | 100.0% | 27 | 27 | 0
 | Bicycle Parking | 4.5 | 44.9% | 100.0% | 35 | 35 | 0
 | Bus Capacity | 6.6 | 37.2% | 96.6% | 29 | 1 | 28
 | Bus Accessibility | 6.8 | 19.2% | 100.0% | 15 | 15 | 0
 | Road Density | 2.3 | 1.3% | 100.0% | 1 | 1 | 0
Demographic Socioeconomic Environment | Population | 23.9 | 12.8% | 60.0% | 10 | 6 | 4
 | Household Members | 3.0 | 39.7% | 100.0% | 31 | 0 | 31
 | Job-Resident Balance | 3.0 | 37.2% | 100.0% | 29 | 0 | 29
 | Tenant Proportion | 2.2 | 21.8% | 100.0% | 17 | 0 | 17
Exploratory Regression – Stage 1
The cell marked with dark color means that it doesn’t meet the judgment.

## Slide 54
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Identification of Valid Factors
4.3
Independent variables | Test model |  | 
 | Beta | Sig | VIF
Government Area | 0.10 | 0.02 | 1.36
Transportation Facility Area | 0.20 | 0.00 | 2.31
Land use Aggregation | 0.10 | 0.03 | 1.42
Bicycle Parking | 0.46 | 0.00 | 2.60
Bus Capacity | -0.20 | 0.01 | 3.56
Bus Accessibility | 0.26 | 0.00 | 4.71
Transfer Dummy | 0.26 | 0.00 | 2.79
Job-Resident Balance | -0.10 | 0.05 | 1.94
Tenant Proportion | -0.09 | 0.03 | 1.32
Household Members | - | - | -
Residual sum of squares | 337744990 |  | 
Adjusted R2 | 0.96 |  | 
AICc | 694.39 |  | 
Jarque-Bera test (Sig) | 0.61 * |  | 
Koenker (BP) test (Sig) | 0.85 ** |  | 
SA test (Sig) | 0.27 *** |  | 
* No biased standard errors due to heteroscedasticity
** Not deviating from a normal theoretical distribution
*** Not spatial autocorrelated
Exploratory Regression – Stage 2

## Slide 55
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Moran's Index | Z-score | P-value* | Pattern | DIFF of Criterion** | Type
Government Area | 0.04 | 0.66 | 0.51 | Random | - | Global
Transportation Facility | 0.29 | 3.33 | 0.00 | Clustered | -1.95 | Local
Land use Aggregation | -0.01 | 0.20 | 0.84 | Random | - | Global
Transfer Dummy | 0.13 | 1.58 | 0.12 | Random | - | Global
Bicycle Parking | -0.12 | -0.92 | 0.36 | Random | - | Global
Bus Capacity | 0.70 | 7.57 | 0.00 | Clustered | 0.18 | Local
Bus Accessibility | 0.45 | 5.04 | 0.00 | Clustered | 0.04 | Local
Job-Resident Balance | 0.77 | 7.61 | 0.00 | Clustered | -0.17 | Local
Tenant Proportion | 0.24 | 2.54 | 0.01 | Clustered | 1.02 | Local
Identification for Global/Local Variable
* Statistical significance means autocorrelation
** More than or equal to the value of 2, means the local term is better to be assumed as global

## Slide 56
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
MGRW Parameter Setting
Fixed Gaussian kernel function
Chart: AICc
5.7km
Golden-section search
Kernel Type
Bandwidth selection method

## Slide 57
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Type | OLS model |  |  |  | MGWR model |  | 
 |  | B | SE | t |  | B | SE | t
Government Area | Global | 0.05 | 0.02 | 2.41 |  | 0.05 | 0.02 | 2.59
Land use | Global | 11,832.53 | 5323.15 | 2.22 |  | 13,384.34 | 5,408.81 | 2.48
Transfer Dummy | Global | 6,578.09 | 1216.82 | 5.41 |  | 5,968.65 | 1,198.72 | 4.98
Bicycle Parking | Global | 7.51 | 0.93 | 8.11 |  | 7.72 | 0.90 | 8.59
Transport Area | Local | 0.11 | 0.03 | 3.58 |  | 0.10 | 0.02 | -
Bus Capacity | Local | -59.21 | 20.71 | -2.86 |  | -55.14 | 5.94 | -
Bus Accessibility | Local | 50.71 | 14.64 | 3.46 |  | 48.61 | 2.43 | -
Job-Resident Balance | Local | -2,762.24 | 1,079.33 | -2.56 |  | -2,411.17 | 364.44 | -
Tenant Proportion | Local | -9,987.81 | 4,380.30 | -2.28 |  | -10,304.66 | 756.09 | -
Best bandwidth |  |  |  |  |  | 5.7km |  | 
AICc |  | 694.39 |  |  |  | 690.60 |  | 
Residual sum of squares |  | 337,744,989 |  |  |  | 296311499 |  | 
Coefficient

## Slide 58
Residual Analysis
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Z-score in MGWR is less than that in OLS
Moran’s index in MGWR is more closer to the expected index than that in OLS
Indicator | OLS | MGWR
Moran’s index | 0.08 | 0.03
Expected index | -0.03 | -0.03
Variance | 0.01 | 0.01
z-score | 1.09 | 0.61
p-value | 0.27 | 0.54
Distribution of Local R2
0.960 - 0.965
0.965 – 0.970
0.970 – 0.975
0.975 – 0.980
Local R2
Distribution of Residuals

## Slide 59
Residual Analysis
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Significance Map
Transportation Facility Area
Bus Capacity
Bus Accessibility
Population Job Balance
Tenant Proportion
Not Significance
P = 0.01
P = 0.05
P = 0.1
Significance Map

## Slide 60
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Main Work
Reclassified and reorganized the indicator framework.
Proposed the approach of selecting variables from candidates using the tool of exploratory regression in ArcGIS.
Provided a method for judging whether a variable is global or local used in estimating the MGWR model.

## Slide 61
Chapter 5
Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
Research object
Method
Methods
Results Discussion

## Slide 62
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
The urban rail transit has become one of the most important travel modes in modern cities.
Development of urban rail transit
The policy of giving priority to the development of public transport has widely been adopted around the world.
Public transit goes first
How to master the relationship between land-use and passenger volume has become an important issue.
Coordination between urban planning and urban rail transit

## Slide 63
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
 | Scale | Objective
Station-Level | single station | Passenger volume of station
Station-to-Station-Level | station network | OD passenger volume
Some References
[1] Taylor, B.D. et al., (2003). Analyzing the determinants of transit ridership using a two-stage least squares regression on a national sample of urbanized areas. University of California Transportation Center.
[2] Choi, J. et al., (2012). An analysis of Metro ridership at the station-to-station level in Seoul. Transportation, 39(3), 705–722.
[3] Gutiérrez, J., Cardozo, O.D. & García-Palomares, J.C., (2011). Transit ridership forecasting at station level: An approach based on distance-decay weighted regression. Journal of Transport Geography, 19(6), 1081–1092.
To describe the connectivity between different stations using OD ridership.
To explain how the connectivity is determined by land-use factors.
Research Questions

## Slide 64
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Index framework
Dependent variable
Independent variable
Conversion of realistic issue
Discrete choice issue
Logistic regression
Model estimation
Result and Discussion
Probability of getting off at a specific destination station

## Slide 65
Research object
5.2
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
1
k
2
3
4
5
……
Boarding
Alighting
Station
Station k
Other
Stations
Passenger Volume
Passenger Volume
Description for Connectivity —— dependent variable

## Slide 66
Research object
5.2
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Residence proportion
Office proportion
Commerce proportion
Education proportion
Operation distance of subway
Bus accessibility
Bus capacity
Land-use aggregation
Determinants for transit ridership —— independent variables
Land-use
Impedance

## Slide 67
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Boarding
Alighting
……
Other
Stations
Station 1
……
Station 2
Station k
land-use feature of boarding station
Choice of whether to get off at station k
Affect
Impedance between boarding and alighting station
Realistic issues
Independent variable
Dependent variable

## Slide 68
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
: probability of getting off
: result of choice
: vector of explanatory variable
: residual item.
Logistic regression model
Discrete choice issue
Mathematical problems

## Slide 69
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Select sample station
Station type | Station name | Population density | Commerce proportion | Office proportion | Residence proportion | Education proportion
Medium-density residence | Kamo | 98 Person/Ha | 4% | 3% | 83% | 4%
High-density residence | Fujisaki | 173 Person/Ha | 5% | 7% | 76% | 6%
Education | Hakozakikyudai | 83 Person/Ha | 5% | 6% | 51% | 22%
Office | Gofukumachi | 135 Person/Ha | 8% | 31% | 49% | 3%
Commerce | Tenjin | 69 Person/Ha | 34% | 32% | 24% | 1%
Airport | Fukuoka Airport | 36 Person/Ha | 1% | 3% | 45% | 2%
Note:
The highlighted cells refer to the representative values that having much higher percentage than other land-use types.

## Slide 70
Results and discussion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Type | Destination Station | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Medium-density residence | Kamo | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | Fujisaki | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | Hakozakikyudai | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | Gofukumachi | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | Tenjin | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | Airport | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Note: full name of the abbreviation
C: Commerce, O: Office, R: Residence, E: Education, L-A: Land-use Aggregation, D: Distance, B-C: Bus Capacity, B-A: Bus Accessibility.
Result of estimation

## Slide 71
Results and discussion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Type | Destination Station | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Medium-density residence | Kamo | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | Fujisaki | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | Hakozakikyudai | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | Gofukumachi | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | Tenjin | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | Airport | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Result: Medium-density residence have weak connectivity with all other types.
Discussion: The private traffic ratio is higher.
Discussion for results

## Slide 72
Results and discussion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Type | Destination Station | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Medium-density residence | Kamo | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | Fujisaki | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | Hakozakikyudai | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | Gofukumachi | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | Tenjin | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | Airport | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Result: Education type have strong connectivity with most of other types.
Discussion: Students are more inclined to use subway.
Discussion for results

## Slide 73
Results and discussion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Type | Destination Station | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Medium-density residence | Kamo | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | Fujisaki | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | Hakozakikyudai | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | Gofukumachi | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | Tenjin | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | Airport | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Result: Similar types have weak connectivity
Discussion: Traffic demand is generated by different trip purpose
Discussion for results

## Slide 74
Chapter 6
Conclusion
Summary
Contributions
Recommendations

## Slide 75
Summary
6.1
Chapter 6 - Conclusion
Taking explaining the rail transit ridership as the overall goal analyzed the inﬂuence of various factors on ridership from station level and station-to-station level respectively.
Provided new explanations for the catchment area of rail transit stations.
Provided an approach for selecting the valid indicators;
Proposed a ridership forecasting method with the consideration of interaction among stations and stations
showed a way to accurately estimate the catchment area.

## Slide 76
Contributions
6.2
Chapter 6 - Conclusion
Chapter 2
Reinterpreted the implication of surveyed walking distance/duration to transit stations, that it has no linear relation with people willingness but just the reﬂection of the distance between departures and stations.
Described the correlation between surveyed walking duration and people’s individual characteristics from the view of probability, which can be further applied to the estimation of catchment area of rail transit stations.

## Slide 77
Contributions
6.2
Chapter 6 - Conclusion
Chapter 3
Analyzed the trend of variations in transit ridership, and classiﬁed the sub-way stations of Fukuoka into 5 types in terms of land use. Conﬁrmed the correlations between transit ridership and land use.

## Slide 78
Contributions
6.2
Chapter 6 - Conclusion
Chapter 4
Considered the inﬂuence of bus on rail transit ridership from both the sides of bus capacity and bus accessibility, and veriﬁed that the effect of bus capacity is positive to rail transit ridership, while the effect of bus accessibility is negative.
Proposed the approach of screening valid indicators by introducing the exploratory regression, and conﬁrmed its effectiveness in a small sample case.
Distinguished the local and global variables in MGWR model by examining the spatial distribution of each variable, and the effectiveness was conﬁrmed in the estimation of MGWR model

## Slide 79
Contributions
6.2
Chapter 6 - Conclusion
Chapter 5
By examining the probability of selecting the destination station from all the stations, established a logistic regression model for describing the correlation between stations and stations.
Quantitatively validated the impact of land use types on the selection of destination stations.

## Slide 80
Recommendations
6.3
Chapter 6 - Conclusion
recommendations for helping increase the
use of rail transit
People’s walking preferences have signiﬁcant inﬂuence on the use of rail transit. It is suggested that the design for pedestrian accessibility should also consider the individual characteristics of resident, thus helping increase the use of rail transit.
With the development of rail transit, if viewing from the whole transit system, the positioning of bus system is gradually inclining to be the connection between departures and rail transit. Rather than planning higher capacity for bus transport, it is suggested to plan more accessible bus routes which can help people use rail transit more convenient.
According to the ﬁndings, the more aggregation in land use functions the more demand in rail transit. Thus suggesting to connect more functional regions as possible when making rail transit planning.

## Slide 81
Recommendations
6.3
Chapter 6 - Conclusion
recommendations for helping increase the
use of rail transit
Surveys of income and occupation, exploring the effect on travel behavior.
Integer of the whole process of estimating the catchment area of rail transit stations based on the achievements of this dissertation.
Joint of the estimation of catchment area and ridership forecasting, improving the accuracy.
Analysis of the inﬂuence on land use affected by the use of rail transit, exploring the interaction between land use and transit.
Analysis of balance condition among various elements in the catchment area of transit stations, including human, resource, land use, transportation etc. achieving the goal of sustainable development.