## Slide 1
Research on Determinants of Rail Transit Ridership
CHEN Qi
Graduate School of Human-Environment Studies,
Kyushu University, Japan
November 27, 2018
Notes: Hello everyone, I’m Chen Qi, the doctor candidate from Zhao laboratory.
The title of my dissertation is Research on Determinants of Rail Transit Ridership.
Now I will give my presentation.

## Slide 2
Introduction
Chapter 1

## Slide 3
Chapter 1 - Introduction
Background
1.1
Current situation
Reduction in share rate of public transit
1
Traffic congestion
2
Chart: Traffic mode share rate of Fukuoka
| 1972 | 1983 | 1993 | 2005 | 2025
rail transit | 0.066 | 0.098 | 0.134 | 0.141 | 0.133
bus | 0.173 | 0.118 | 0.08 | 0.083 | 0.096
texi | 0.033 | 0.02 | 0.015 | 0.011 | 0.012
pravite car | 0.306 | 0.308 | 0.378 | 0.422 | 0.481
bycicle | 0.049 | 0.155 | 0.151 | 0.156 | 0.116
walk | 0.373 | 0.301 | 0.241 | 0.185 | 0.162
Notes: This research uses the Fukuoka public rail transit as the study case to examine the influencing factors on ridership.
Now Fukuoka is facing a problem of reduction in public transit share.
The private car share rate keeps on increasing, while the rail transit share has begun to decline.

## Slide 4
Chapter 1 - Introduction
Background
1.1
Current situation
Chart: Average travel speed during crowded time in major cities
| Tokyo | Saitama | Osaka | Kawasaki | Nagoya | Sakaishi | Fukuoka | Yokohama | Kyoto | Sagamihara | Chiba | Sapporo | Kitakyushu | Kobe | Shizuoka | Hiroshima | Okayama | Sendai | Hamamatsu | Niigata
speed | 16.8 | 17.8 | 18.6 | 18.6 | 18.9 | 19.4 | 20.4 | 20.7 | 22.7 | 23.6 | 24.4 | 26.7 | 27.3 | 28.1 | 29 | 29.9 | 29.9 | 30.2 | 30.8 | 32.6
Reduction in share rate of public transit
1
Traffic congestion
2
Notes: Another problem the traffic congestion, which we are experiencing every day.
At present, the average travel speed during crowed time has almost fallen under 20 kilometers per hour, and it keeps on getting worse now.

## Slide 5
Chapter 1 - Introduction
Background
1.1
Exploring the determinants on the utilization of rail transit
Reduction in share rate of public transit
Promoting the use of public rail transit
Current situation
Demand
Theme
Subtopic
Walking duration to rail transit stations
Ridership of a single station
Ridership transfer between station and station
Traffic congestion
Notes: With these transportation problems, it’s clear that we have the demand to promote the use of public transit.
And that is what I want to talk about in this dissertation.
The theme is to explore the influencing factors of rail transit ridership.

## Slide 6
Chapter 1 - Introduction
Background
1.1
Problems
1
Walking is the most important travel modes in accessing transit stations, also one of the most key determinants on the utilization of rail transit. A quantitative method for describing walking duration preference to rail transit stations is necessary.
2
The rail transit ridership, land use, and population have their own distribution characteristics in space. These characteristics in the case of Fukuoka City need to be further and objectively understood.
3
Rail transit ridership is considered to be mainly affected by the environmental factors surrounding the station. For the rail transit station in Fukuoka City, the influencing factors need to be explored and estimated.
3
The rail transit station is in a network. When the ridership is affected by the environmental factors around the station, it is also influenced by the environmental factors around the other stations in the same network. How to describe and estimate the ridership transfer between station and station is an important issue.
Notes: With these transportation problems, it’s clear that we have the demand to promote the use of public transit.
And that is what I want to talk about in this dissertation.
The theme is to explore the influencing factors of rail transit ridership.

## Slide 7
Chapter 1 - Introduction
Purpose
1.2
Exploring the factors influencing rail transit ridership from multiple perspectives and estimating the influence.
Utilization of rail transit
Main purpose
Exploring the factors influencing the ridership at station level
Problem 3
Chapter 4
Exploring the factors influencing the ridership transfer between station and station
Problem 4
Chapter 5
Clarifying the characteristics of ridership and land use
Problem 2
Chapter 3
Secondary purposes
Exploring the factors influencing Walking duration
Problem 1
Chapter 2
Notes: With these transportation problems, it’s clear that we have the demand to promote the use of public transit.
And that is what I want to talk about in this dissertation.
The theme is to explore the influencing factors of rail transit ridership.

## Slide 8
Chapter 1 - Introduction
Organization
1.2
Chapter 1
Introduction of the dissertation including background, purpose, literature review.
Chapter 2
Walking duration
Exploring the factors influencing walking duration to transit stations from the perspective of passengers’ attributes.
Chapter 3
Characteristics analysis. Preliminary research for chapter 4, 5
Clarify the characteristics of transit ridership and land use
Chapter 6
Summarizing the findings achieved in each chapter, and giving the conclusion for this dissertation
Chapter 4
Transit ridership at station level
Exploring the factors influencing transit ridership at station level
Chapter 5
Transit ridership at station-to-station level
Exploring the factors influencing transit ridership at station-to-station level
Notes: With these transportation problems, it’s clear that we have the demand to promote the use of public transit.
And that is what I want to talk about in this dissertation.
The theme is to explore the influencing factors of rail transit ridership.

## Slide 9
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Chapter 2

## Slide 10
distance to destinations is widely thought to be an important predictor of active travel
Introduction
2.1
Background
Exploring the factors influencing walking duration to transit stations from the perspective of passengers’ attributes.
Main purpose
Walking is the most important travel modes in accessing transit stations.
Walking duration to transit station is widely accepted to be an important determinants on the utilization of rail transit.
Walking duration to rail transit stations is mainly obtained by survey statistics, which is limited by the individual and regional characteristics of survey objects that the preference of walking duration cannot be generalized to other cases.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Notes: Because Walking is the most important travel modes in accessing transit stations. The Walking duration to transit station is also widely thought to be an important determinants on the use of public transit.
This research mainly focuses on Identifying the correlation between walking duration to stations and the probability of accepting this walking duration.

## Slide 11
 | Study | Type 1 | Type 2 | Type 3 | This
Research object | Walking distance | ● |  | ● | 
 | Walking duration |  | ● |  | ●
Method | Statistical description | ● |  |  | 
 | Regression |  | ● | ● | 
 | Nonlinear fitting |  |  |  | ●
Method | Qualitative | ● |  |  | 
 | Quantitative |  | ● | ● | ●
Result |  | Survey result description | Some factors were found, but prediction and verification were not given | No relationship found | Having relationship with travel purpose, travel time period, age, and occupation
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Review

## Slide 12
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Most studies use qualitative methods. Few quantitative analysis obtained the significant result on estimating walking duration. The reason of that may be in the data processing, the model constructing, also model estimating.
Research focus
Research focus
1
  Describe walking duration
Using probability but not the linear relationship to describe the walking duration preference of passengers with different attributes.
Identify valid indicators
2
Using variance analysis to identify the valid influencing factors.
Problem 1
Problems in previous studies
Notes: Because Walking is the most important travel modes in accessing transit stations. The Walking duration to transit station is also widely thought to be an important determinants on the use of public transit.
This research mainly focuses on Identifying the correlation between walking duration to stations and the probability of accepting this walking duration.

## Slide 13
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Although many studies have summarized some factors affecting the walking duration through qualitative methods, none of them quantitatively verified the effect of the influencing factors.
Research focus
Research focus
Problems in previous studies
To estimate and predict the relationship between identified influencing factors and walking duration. Then evaluating the prediction to judge the effectiveness of identified influencing factors.
3
  Predict and evaluate
Problem 2
Notes: Because Walking is the most important travel modes in accessing transit stations. The Walking duration to transit station is also widely thought to be an important determinants on the use of public transit.
This research mainly focuses on Identifying the correlation between walking duration to stations and the probability of accepting this walking duration.

## Slide 14
Walking duration preference
Threshold value of walking duration
Identify valid feature
Verify the extracted features
Conclusion
Construct the indicator system
Random forest decision tree
Predict
evaluation
Variance analysis
Dependent variable
Exploratory variable
Data cleaning
Passengers’ attributes
Valid travel chain info
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Prediction for individual
Prediction for group
Research focus
1
Research focus
2
Research focus
3

## Slide 15
Walk longer than the given threshold of walking duration
Explanatory variables
Behavior
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data
2.2
Indicators
Dependent variable
Probability
Trip chain info
Other personal attributes
Personal socio-demographic characteristics
Notes: On the base of interpreting the problems in this research topic, the research object in this study is carried out.
The dependent variable is the probability of accepting the given threshold of walking duration
The explanatory variables are passengers’ behaviors including Personal socio-demographic characteristics, some other personal attributes, and also the trip chain information.

## Slide 16
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data
2.2
Distribution of the transit stations
Data in this study
Study case: Fukuoka
Notes: After introducing the methods, I’m going to give an overview of the study case and dataset in this study.
The study case is the rail transit stations in Fukuoka, there are 78 stations in total, including JR Kyushu, Fukuoka subway, and West Japan Railway.
The main data source used in this study is from the 4th nationwide person trip survey, mainly including the information about trip chaining behavior and some socio-demographic attributes.

## Slide 17
Data
2.2
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Source: Person Trip Survey
Data processing
Notes: The original data covers all the main cities in Kitakyushu.
I set the filter with city area of Fukuoka, rail transit trip chain, without null record, the remaining valid dataset has 4000 records.

## Slide 18
Data
2.2
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
The age distribution of passengers
Distribution of walking duration
The passengers aged between 25-55 who are still at production age account for the majority
People tend to reply a looser answer when they are being asked some questions about details.
Peak values at 5, 10, 15 min
Distribution verification
Notes: This is the data description. The left part is the age distribution of passengers.
As we can see in this figure, the passengers aged between 25-55 who are still at production age account for the majority.
The right part is the distribution of walking duration, we can clearly see 3 peak values in this figure, they are 5, 10, 15 minutes, respectively.
Here are some reasons for this result. That is if people were asked some questions about details like how much did you spend, how long did you take, for such kinds of questions, people tend to reply a looser answer, some general number like 5, 10, or something.
This is also considered as one of the reasons that using the continuous value of walking duration cannot get a good result.
In this study, since this research investigate the threshold of walking duration, even the obtained loose answer can be viewed that the passenger has accepted.
We can thing that the peak values will not cause anomaly in this study.

## Slide 19
Give an example, for one person who has the attributes:
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.3
Realistic issue
8 min
4 min
OK
I can accept a walking duration less than 8 minutes
0 min
Reflected in person trip survey
I walked 6 minutes to the station
0 min
6 min
Problem description
Notes: There has been a lot of studies on the relationship between walking duration and personal attributes, however, the problem of walking duration is not well solved.
So, at first, I’m going to give an example to explain what I want to do in this research.
Think about a people who has the attributes like this, we suppose he can accept a walking duration less than 8 minutes for accessing transit stations.
But if it is reflected in a person trip survey, it will be like “I walked 6 minutes to the station”. Obviously, it cannot represent how long he are willing to walk to stations.
Here I will give an example to explain what I want to do in this research. There has been a lot of studies on the relationship between walking duration and personal attributes, however, a common problem is still not well addressed. Think about a people who has the attributes like this, (𝑀𝑎𝑙𝑒, 25 𝑦𝑒𝑎𝑟𝑠 𝑜𝑙𝑑, 𝑠𝑡𝑢𝑑𝑒𝑛𝑡, 𝑝𝑒𝑎𝑘 ℎ𝑜𝑢𝑟, 𝑔𝑜 𝑡𝑜 𝑠𝑐ℎ𝑜𝑜𝑙), we suppose a people like him can accept a walking duration less than 8 minutes for accessing transit stations. But if it is reflected in a person trip survey, it may be that “I walked 6 minutes to the station”. Sometimes the passengers even cannot give a clear answer that how long he would like to walk to transit stations. Here the deviation is appeared.

## Slide 20
Real Walking duration obtained from person trip survey
Acceptable walking duration
Where the is the reflection of the walking duration from departures to stations
Where the is the acceptable walking duration for the people with those factors
The general expression can be:
Deviation is appeared
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.3
Mathematical description
Real ≠ Acceptable
Notes: I will change the description to a mathematical way.
According to the previous research, walking duration to transit station should have a relationship with personal attributes.
The general expression should be like this. The walking duration is a function of personal attributes.
However, the walking duration obtained from questionnaire is just a reflection of walking duration from the departure to the station. It should not have relationship with personal attributes.
But, as we know, the personal attributes should have influence on the travel behaviors including the walking duration to stations. In fact, what the personal attributes can influence is the acceptable walking duration.

## Slide 21
Assuming the distribution of walking duration of the passengers with the same attributions subject to the normal distribution.
If the survey result obtained from the questionnaire showed one group of passengers with specific attributes tend to walk longer, it means this group of passengers can accept a longer walking duration.
In this graph it can be considered that Group 1 can accept a longer walking duration than Group 2.
6 min
If considering the threshold of 6 minutes
Group 1
Group 2
All Samples
minute
Probability
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.3
Important assumption
Notes: Then I’m going to explain the methods.
Firstly, An important assumption is necessary in this research.
Think about an example, as shown in this figure, we assume two groups of passengers, the passengers in each group have the same characteristics in personal characteristics, but group 1 is different from group 2.
The passengers in the two groups may have different preference of walking duration.
Now we give the assumption that the distribution of walking duration with the same personal attributes should subject to the normal distribution.
If the survey result obtained from the questionnaire showed group 1 tend to walk longer, it means this group of passengers can accept a longer walking duration.
As expressed in this figure, if investigating the threshold of 6 minutes, Group 1 can accept a longer walking duration than Group 2.

## Slide 22
Attributes
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.3
Abstract form of the model
Model construction
Where:
the given threshold of walking duration
the probability of accepting or not at the threshold of minutes.
Continuous value of Walking duration
Threshold of walking duration
Notes: Then I will give the abstract model for this problem.
Different from that in previous studies, the dependent variable is the probability of accepting or not at the threshold of y minutes.
Note it, the investigated walking duration is not a continuous value but some specific thresholds.

## Slide 23
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Selection of valid features
2.4
The thresholds selected in this study is 5, 8, 13 minutes.
According to the existing studies, the acceptable walking duration mainly range from 5 – 13 minutes.
In this study, the average walking duration is about 8 minutes.
L : tend to spend Less than the threshold
M: tend to spend more than the threshold
Valid Features at each threshold
Selection of thresholds
Analysis of variance
Notes: It has been said in the former slides, the research objects are some specific threshold of walking durations.
According to the previous research and the investigation of Fukuoka, the acceptable walking duration mainly range from 5-13 minutes, and the average duration is about 8 minutes in Fukuoka.
Therefore, the threshold of walking duration to be investigated are set to 5, 8. 13 minutes.
Regarding the three thresholds, I picked the valid factors at each threshold, by using the analysis of variance.
For this table, in the column of effect, the cell marked with L means people with this attributes tend to accept a longer time than this threshold, M is the opposite.
For example, at the 5 minutes threshold, we can see that passengers who has the attributes of peak hour, and purpose of commuting to work tend to walk a less time than the given threshold of 5 minutes.

## Slide 24
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Prediction
2.5
Decision tree and forest random
Reason for choosing decision tree
Reason for adding forest random
Used as an exploratory method for the dataset with unknown feature distribution
Reduce the possibility of over-fitting of data which is easily occurred in the decision tree model.
50% training set
50% testing set
Train the model
Get the rule
Verify the model
Input
Flow
Notes: Now we have got the valid features, the next step is to estimate the model to obtain the influence of the features on the acceptable walking duration.
I used the forest random decision tree model in this study.
Forest random model is constructed by random selection of features and samples based on decision tree model.
The result is obtained by the average value of multiple decision trees.

## Slide 25
Evaluation
2.6
Index: Kappa indicator
Object: Group of 200 individuals
Predictive power of group trends
Predictive power of individual
Object: Individual
Index: Coefficient of determination
-1
1
Worse
Better
Range
Predictive power
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
0
1
Worse
Better
Range
Predictive power

## Slide 26
Valid Features at each threshold
Kappa index
0.284
0.033
0.118
Evaluation
2.6
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Coefficient of determination
0.843
0.221
0.426

## Slide 27
The effect of influencing factors is predicted, the results are evaluated from the perspective of both individual and group.
Describe passengers' walking duration preferences by examining the probability that passengers with different attributes walk longer than a given threshold.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Summary
Problems
Little quantitative relationship between walking duration and passengers’ attributes was found.
Few of the existing studies quantitative verified the effect of influencing factors
1
2
Achievements
Notes: Now we get the conclusion of chapter 2.
The main findings of this study can be summarized into 4.
1. 5 minutes is a widely accepted walking duration to rail transit.
2. Whether accepting the 8 minutes walking duration is ambiguous in passenger’s practical behaviors.
3. Passengers with the private travel purpose tend to accept the longest walking duration.
4. Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.
This is the chapter 2.

## Slide 28
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Findings
Peak hour
Commuting to work
Age between 25-44
Female
Peak hour
Commuting to work
Business purpose
Private purpose
Going home purpose
Age between 45-64
Peak hour
Commuting to work
Private purpose
Walk less than the threshold
Walk more than the threshold
Business purpose
Private purpose
Going home purpose
Older than 65
No occupation
5 minutes threshold
Individual: Slight
Group trend: High
8 minutes threshold
Individual: Low
Group trend: Low
13 minutes threshold
Individual: Low
Group trend: Moderate
Notes: Now we get the conclusion of chapter 2.
The main findings of this study can be summarized into 4.
1. 5 minutes is a widely accepted walking duration to rail transit.
2. Whether accepting the 8 minutes walking duration is ambiguous in passenger’s practical behaviors.
3. Passengers with the private travel purpose tend to accept the longest walking duration.
4. Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.
This is the chapter 2.

## Slide 29
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Recommendations
Encourage office buildings to move close to stations
Results from the factors of business purpose and going home purpose. Office workers tend to access rail transit station in a less time.
The individual prediction is still not accurate enough for predicting individual behavior.
Results from the evaluation of individual prediction
The group prediction can be used for mastering the overall trend of rail transit utilization in a block.
Results from the evaluation of group prediction
Notes: Now we get the conclusion of chapter 2.
The main findings of this study can be summarized into 4.
1. 5 minutes is a widely accepted walking duration to rail transit.
2. Whether accepting the 8 minutes walking duration is ambiguous in passenger’s practical behaviors.
3. Passengers with the private travel purpose tend to accept the longest walking duration.
4. Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.
This is the chapter 2.

## Slide 30
Chapter 3
Analysis on the characteristics of transit ridership and land use

## Slide 31
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Research position
Ridership Estimation
Purpose
To grasp the characteristics of transit stations in terms of both transit ridership and land use in Fukuoka.
Preliminary study
Chapter 4
Station-to-station
Chapter 5
Station level
Characteristics
Relationship
Chapter 3
Land use
Ridership
Notes: This chapter is a preliminary study for estimating the influence on transit ridership, mainly focus on the characteristics of transit ridership and land use, also give a simple exploration on the relationship between them.
The purposes of chapter 3 is to grasp the characteristics of transit stations in terms of both transit ridership and land use.

## Slide 32
Summary the characteristics of rail transit ridership in spatial and temporal distribution
Introduction
3.1
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Problem 1
The characteristics of rail transit ridership and land use in Fukuoka needs to be clarified.
Research focus
Problems in previous studies
1
  Characteristics of transit ridership
Analyze the characteristics of land use around the subway in terms of the type of land use
2
  Characteristics of land use
Preliminary explore the relationship between rail transit ridership and land use
3
  Characteristics of land use

## Slide 33
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
Study case
Fukuoka subway
35 subway stations
3 operating subway lines
29.8 km operating mileage
20% share of motorized travel
Data source
Notes: This is the overview of study case and data source.
This study uses the Fukuoka subway stations as the study case.
The main data source in this study is the subway transit ridership, statistic of population, and land use.

## Slide 34
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
1. Matching the region of data.
2. Matching the time points of data.
3. Extracting the data within the catchment area.
Data extraction
Notes: This is the procedure of data extraction.

## Slide 35
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership characteristics
Growth trend.
More than 600,000 passengers per day.
Significant difference in ridership among the three lines.
Trends of variation in transit ridership
Chart: Transit ridership of subway in Fukuoka
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
line 1 | 408641 | 420811 | 424076 | 427402 | 417222 | 426908 | 442126 | 454504 | 471578 | 491838
line 2 | 38887 | 39429 | 39145 | 40394 | 40015 | 41347 | 42583 | 43727 | 45848 | 47704
line 3 | 77007 | 88969 | 95886 | 100822 | 98519 | 102808 | 107775 | 110471 | 115163 | 120410
total | 524535 | 549209 | 559107 | 568618 | 555756 | 571063 | 592484 | 608702 | 632589 | 659952
Notes: Next is the transit ridership characteristics.
This is the trends of variation in transit ridership.
The ridership keeps a growth trend
Also we can see that there are significant differences in ridership among the three lines.

## Slide 36
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Line 3 had a much higher growth rate at the first few years of the opening
The growth rate of three lines tend to be stable after the year of 2009
Transit ridership characteristics
Annual growth rate of transit ridership
Chart: Annual change rate of transit ridership
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
line 1 | 0.029782 | 0.0077588 | 0.0078429 | -0.023818 | 0.023215 | 0.035647 | 0.027997 | 0.037566 | 0.042962
line 2 | 0.013938 | -0.0072028 | 0.031907 | -0.0093826 | 0.033288 | 0.029893 | 0.026865 | 0.048506 | 0.040482
line 3 | 0.15534 | 0.077746 | 0.051478 | -0.022842 | 0.043535 | 0.048313 | 0.025015 | 0.042473 | 0.045562
total | 0.04704 | 0.018022 | 0.017011 | -0.02262 | 0.027543 | 0.037511 | 0.027373 | 0.039243 | 0.043256
Notes: This is the annual growth rate of transit ridership.
Line 3 had a much higher growth rate at the first few years of the opening.
The growth rate of three lines tend to be stable after the year of 2009.

## Slide 37
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership characteristics
Terminal
Terminal
Hub
Airport
Hub
Newly opened
Spatial distribution of transit ridership
Notes: This is the characteristics of spatial distribution.
Fukuoka subway has two terminal stations, two hub stations, and one station serving for the airport.
We can see that, most stations located in the central area have higher ridership.

## Slide 38
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership | Total | Line 1 | Line 2 | Line 3
Hub | 2 | 2 | 0 | 0
Large | 4 | 3 | 0 | 1
Medium | 11 | 8 | 1 | 2
Small | 18 | 0 | 4 | 4
Growth rate | Total | Line 1 | Line 2 | Line 3
0-2.5 | 12 | 8 | 4 | 0
2.5-4.5 | 11 | 5 | 2 | 4
4.5-6.0 | 6 | 0 | 0 | 6
6.0- | 6 | 0 | 0 | 6
Transit ridership characteristics
Small scale
High growth rate
Line 3
Small scale
Low growth rate
Line 2
Large scale
Low growth rate
Line 1
Classification based on transit ridership
Notes: Regarding the transit ridership and their growth rate, the two cross tables are given to help understand the characteristics.
From the two tables, the three lines represent significant differences.

## Slide 39
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
800m-radius region
Extracting data
ArcGIS
Business
Commerce
Hotel
Entertainment
Residence
Apartment house
Dwelling with shop
Government
Education
Culture
Main land use
Data extraction
Notes: Next is the analysis on the land use characteristics.
The information of land use is extracted using an 800 meters radius region around the stations.

## Slide 40
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
High correlation ( >0.7)
Correlation analysis for indicators
Notes: Then is the land use characteristics.
A correlation analysis is conducted to master the relationship among all the indicators.
The cells marked with grey color represent a strong linear correlation between the two indicator.

## Slide 41
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
Factor analysis
Purpose
To deal with the strong collinearity among indicators
Further explore the internal relationship
Test for factor analysis
Suggested value
> 0.7
Suggested value
< 0.05
KMO and Bartlett’s Test
PASSED the test
Notes: To deal with this linear correlation, the factor analysis is conducted to make a further exploration on the internal relationship.
According to the test for factor analysis, this dataset is thought to be suitable to do factor analysis.

## Slide 42
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
Component Matrix
Factor extraction
Factor 1: Ofﬁce & commerce
Office
Hotel
Commerce
Entertainment
Dwelling with shop
Culture
Factor 2: Residence
Apartment house
Residence
Culture
Factor 3: Education
Education
Government
Notes: As a result, three factors are extracted by the factor analysis, they are office & commerce, Residence, and education.

## Slide 43
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
Land use characteristics
Station classification based on land use
Chart: Land Use Constitution for each type
| Office | Commerce | Residence | Education | Other
Low-density residence | 0.028504 | 0.0799 | 0.69225 | 0.044717 | 0.15463
High-density residence | 0.05432 | 0.040303 | 0.59665 | 0.074697 | 0.23403
Education | 0.060316 | 0.050842 | 0.40217 | 0.20709 | 0.27958
Downtown commerce | 0.38084 | 0.25757 | 0.13678 | 0.012363 | 0.21244
Office | 0.27482 | 0.14201 | 0.27095 | 0.030956 | 0.28127
Notes: This is the summary for each type of stations.

## Slide 44
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
General relationship
Summary for each type of station
Cross table of land use and transit ridership
Large differences in different types
Low density = Low ridership
Commercial center = High ridership
Notes: Combining with the cross table of land use and transit ridership, we can get some information.
They are, different land use characteristics have different scales in transit ridership.
The density of both population and land use have significant influence on transit ridership.
Commercial land use produces more ridership.

## Slide 45
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
Statistical relationship - quantiﬁcation method I
Transit ridership per day
Dependent variable
Population density
Commerce & office
Residence
Education
Explanatory variables
0.513
Coefficient of determination
Commerce area
Office area
Key factors
Part 1
Notes: After the general understanding of the relationship between ridership and land use, the quantification method one is used to make a further exploration.
In the first part of quantification method one, the dependent variable is transit ridership per day.
The result showed two key factors of commerce area and office area. But it did not show a good fitness.

## Slide 46
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
Statistical relationship - quantiﬁcation method I
Part 2
Growth rate of transit ridership
Dependent variable
Population density
Commerce & office
Residence
Government
Education
Explanatory variables
0.537
Coefficient of determination
Population density
Key factors
Notes: In the part 2, the same indicator set is used for estimating growth rate of transit ridership.
The same with part 1, the result did not show a good fitness as well.

## Slide 47
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Conclusion
3.5
Through the summary and analysis, we got a comprehensive understanding of rail transit utilization and land use status in the case of Fukuoka City.
Provided foundation and references for the further exploration on the determinants on transit ridership
Pedestrian area should be considered.
Explanatory variables should be enriched.
Model should be improved.
The approach of dealing with small sample case should be considered.
Summary
Implications
Notes: This is the content of this chapter, here gives a summary.
This study provided foundation and references for the further exploration on the determinants on transit ridership
Also the experiences obtained from this study gave some implications for the next.
Pedestrian area should be considered.
Explanatory variables should be enriched.
Model should be improved.
The approach of dealing with small sample case should be considered.

## Slide 48
Chapter 4
Influencing Factors on Transit Ridership at Station Level

## Slide 49
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Background
Rail transit ridership is considered to be mainly affected by the environmental factors surrounding the station.
The influencing factors are different in cities with different urban form and travel preference. Few studies focus on such a city like Fukuoka with only tens rail transit stations.
Explore and explain the factors influencing subway ridership at station level using a small sample case
Main purpose
Notes: The main purpose of chapter 4 is to explore and explain the factors influencing subway ridership at station level using a small sample case.
Around this purpose, this study focuses on three specific topics.
The first one is to propose and reconstruct indicators to improve the index system
Second is to find an approach of identifying the valid indicators for small sample case.
The third one is to consider the different spatial distribution of indicators in the spatial regression model to improve accuracy in estimation.

## Slide 50
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Study type |  | Type 1 | Type 2 | Type 3 | This
Sample size | Tens |  |  |  | ●
 | Hundreds | ● | ● | ● | 
Method | Linear regression | ● | ● | ● | 
 | Mixed spatial regression |  |  |  | ●
Catchment area | Circle buffer | ● | ● |  | 
 | Walking distance |  |  | ● | ●
Indicators | Land use |  | ● | ● | ●
 | Transit-relation | ● | ● | ● | ●
 | Demographic-relation | ● |  |  | ●
Review

## Slide 51
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Research focus
Problem 1
Problem 2
Few studies work on the selection of valid indicators using small sample case.
The consideration of spatial correlation among the explanatory variables is inadequate.
Problem 3
Index system need to be enriched
1
  Improve index system
Propose and reconstruct indicators to improve the index system
Identify valid indicators
2
Propose effective index screening method for small samples
Improve accuracy in estimation
3
Consider the different spatial distribution of indicators in the spatial regression model by identifying global/local variables.
Research focus
Problems in previous studies
Notes: The main purpose of chapter 4 is to explore and explain the factors influencing subway ridership at station level using a small sample case.
Around this purpose, this study focuses on three specific topics.
The first one is to propose and reconstruct indicators to improve the index system
Second is to find an approach of identifying the valid indicators for small sample case.
The third one is to consider the different spatial distribution of indicators in the spatial regression model to improve accuracy in estimation.

## Slide 52
Determine the catchment area
Construct the indicator system
Select valid indicators on explaining ridership
MGWR
Determine local/global variables in MGWR
Estimate MGWR
Residual analysis
Conclusion
Extract indicator from the catchment area
Select valid indicators
Select optimal combination of valid indicators
Explanatory variables
Dependent variable
800m pedestrian area
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Research focus
1
Research focus
2
Research focus
3

## Slide 53
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
 | Walking |  | Bicycle | 
 | Proportion | Ave time | Proportion | Ave time
AVG | 78% | 7.2 | 9% | 9.0
Mid | 85% | 7.0 | 8% | 9.5
Max | 22% | 4.8 | 0% | 0.0
Min | 100% | 9.2 | 33% | 20.0
Catchment area: walking distance accessing the subway station. (Pedestrian Catchment Area, PCA)
Pedestrian area range: 400m ~ 1000m
Most adopted: 800m
Walking speed: about 4.8km/h
Average walking distance: about 600m
1. Walking is the main method of accessing transit station.
2. Most walking distances are within 800m
In general
Catchment area of stations
In the case of Fukuoka
Notes: As to the catchment area, this study uses the 800 meters pedestrian area.
Summarized from the previous studies, the catchment area ranges from 400 meters to 1 kilometer in general, and the most accepted pedestrian area is 800 meters.
Back to our study case Fukuoka, according to the subway survey report, the average walking distance in Fukuoka will be about 600 meters.
We can think that 800 meters covers most of the passengers in Fukuoka.
Based on the above, it can be viewed that 800 meters pedestrian area is reasonable in this study.

## Slide 54
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Catchment area of stations
Separated along the river
The walking distances along the real road network are equal from any point on the boundary line to both the station on both sides.
Notes: As to the catchment area, this study uses the 800 meters pedestrian area.
Summarized from the previous studies, the catchment area ranges from 400 meters to 1 kilometer in general, and the most accepted pedestrian area is 800 meters.
Back to our study case Fukuoka, according to the subway survey report, the average walking distance in Fukuoka will be about 600 meters.
We can think that 800 meters covers most of the passengers in Fukuoka.
Based on the above, it can be viewed that 800 meters pedestrian area is reasonable in this study.

## Slide 55
Indicators system
4.2
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Expected sign | Min Value | Max Value | Average | Unit
Built environment | Commerce | + | 2,921 | 811,281 | 114,353 | m2
 | Office | + | 2,614 | 839,956 | 167,088 | m2
 | Residence | + | 110,748 | 1,067,523 | 528,533 | m2
 | Education | + | 294 | 305,559 | 59,691 | m2
 | Government | + | - | 128,471 | 20,878 | m2
 | Transportation Facility Area | + | 197 | 132,777 | 21,204 | m2
 | Land use Aggregation | + | 0.09 | 0.75 | 0.31 | -
Transportation Accessibility | Transfer Dummy | + | 1 | 4 | 1.34 | -
 | Bicycle Parking | Unknown | 64 | 4,375 | 778 | -
 | Bus Capacity | Unknown | 3 | 260 | 58.48 | -
 | Bus Accessibility | Unknown | 4 | 455 | 89.71 | -
 | Road Density | - | 191 | 479 | 299 | m/ha2
Demographic and Socioeconomic Environment | Population | + | 1,908 | 19,393 | 9,813 | -
 | House Member | - | 1.86 | 2.79 | 2.18 | -
 | Population/Job Balance | Unknown | 1.27 | 2.61 | 1.80 | -
 | Tenant Proportion | - | 0.15 | 0.65 | 0.43 | %
Dependent variable: average daily subway ridership
Variable summary
Notes: This is the data description.
In this study, the dependent variable is average daily ridership.
The candidate independent variables are summarized into 3 categories: 1. built environment; 2. transportation accessibility; 3. demographic and socioeconomic environment.
In the column of expected sign, plus sign means the increase in this indicator is expected to cause an increase in transit ridership, while the minus sign is expected to have an opposite effect.

## Slide 56
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
: the type of land use (respectively government, commercial, residence and education)
: the floor area of land use type within catchment area of subway station
: the average proportion of type land use.
Describing the variety of land use
Indicators system
4.2
Variable interpretation
Land-use Aggregation
Range of PCA | Residence | Office | Commerce | Education | Total
800 | 55.3% | 17.5% | 12.0% | 6.2% | 90.9%
Average
0
1
More
Less
Range
Variety
Notes: Then I will give some interpretation for some of the indicators in details.
First one is the indicator of land-use aggregation.
This indicator is used to describe the variety of land use.
The indicator A ranges from 0 to 1, the higher the indicator A is, the land use variety is lower. On the contrary, the land use variety is higher.

## Slide 57
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators system
4.2
Variable interpretation
Bus capacity
Share passengers from rail transit. Negative effect on rail transit ridership
Bus Accessibility
Bring passengers to rail transit. Positive effect on rail transit ridership
Indicators of bus system
Bus system has both positive and negative effect on rail transit ridership
Supposition
Share ridership from rail transit
Bring ridership to rail transit
VS
Notes: In this study, the indicator of bus system is considered from two aspects.
Like shown in the figure, bus should have two effect on the rail transit, one is bringing passengers to rail transit, and another one is share passengers from rail transit.
The indicator of bus capacity is expected to share passengers from rail transit, having negative effect on rail transit.
The indicator of bus accessibility is expected to bring passengers to rail transit, having positive effect on rail transit.

## Slide 58
Identification of valid factors
4.3
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Flowchart of screening valid factors with small sample
Candidate indicators
Valid indicators
Optimal combination
16
10
9
Multicollinearity
Validity
Stability
Judgement
Number of
indicators
Flow
Model estimation
Test indicators for linear regression
Notes: This part is for identifying the valid factors with small sample.
This is the flowchart of screening valid factors with small sample.
This identification is conducted by two procedures, using the exploratory regression and linear regression, respectively.
At beginning, there were 16 candidate indicators, after running the exploratory regression, 10 valid indicators are left. At last, the optimal combination contains 9 valid indicators.
As to the procedure of screening valid factors, simply speaking, three judgments are used to identify the valid variables, they are multicollinearity, validity, and stability.

## Slide 59
Identification of valid factors
4.3
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Statistical Information |  |  |  |  | 
 |  | VIF | Validity | stability | times | + | -
 | Total |  |  |  | 367 | 253 | 114
Built environment | Commerce Area | 8.8 | 32.1% | 100.0% | 25 | 25 | 0
 | Office Area | 10.4 | 9.0% | 71.4% | 7 | 5 | 2
 | Residence Area | 27.5 | 12.8% | 70.0% | 10 | 7 | 3
 | Education Area | 1.8 | 7.7% | 100.0% | 6 | 6 | 0
 | Government Area | 1.8 | 42.3% | 100.0% | 33 | 33 | 0
 | Transportation Facility | 3.0 | 67.9% | 100.0% | 53 | 53 | 0
 | Land use Aggregation | 2.5 | 50.0% | 100.0% | 39 | 39 | 0
Transportation Accessibility | Transfer Dummy | 3.0 | 34.6% | 100.0% | 27 | 27 | 0
 | Bicycle Parking | 4.5 | 44.9% | 100.0% | 35 | 35 | 0
 | Bus Capacity | 6.6 | 37.2% | 96.6% | 29 | 1 | 28
 | Bus Accessibility | 6.8 | 19.2% | 100.0% | 15 | 15 | 0
 | Road Density | 2.3 | 1.3% | 100.0% | 1 | 1 | 0
Demographic Socioeconomic Environment | Population | 23.9 | 12.8% | 60.0% | 10 | 6 | 4
 | Household Members | 3.0 | 39.7% | 100.0% | 31 | 0 | 31
 | Population/Job Balance | 3.0 | 37.2% | 100.0% | 29 | 0 | 29
 | Tenant Proportion | 2.2 | 21.8% | 100.0% | 17 | 0 | 17
The cell marked with dark color means that it doesn’t meet the judgment.
Valid factors
Suggested value
VIF< 7.5; Validity > 10%; Stability >90%
Valid Variable
Notes: The procedure of the first step is as shown in this table.
The indicators with the VIF less than 7.5, the validity more than 10%, and the stability more than 90% is viewed as valid.

## Slide 60
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Identification of valid factors
4.3
Independent variables | Test model |  | 
 | Beta | Sig | VIF
Government Area | 0.10 | 0.02 | 1.36
Transportation Facility Area | 0.20 | 0.00 | 2.31
Land use Aggregation | 0.10 | 0.03 | 1.42
Bicycle Parking | 0.46 | 0.00 | 2.60
Bus Capacity | -0.20 | 0.01 | 3.56
Bus Accessibility | 0.26 | 0.00 | 4.71
Transfer Dummy | 0.26 | 0.00 | 2.79
Population/Job Balance | -0.10 | 0.05 | 1.94
Tenant Proportion | -0.09 | 0.03 | 1.32
Household Members | - | - | -
Residual sum of squares | 337744990 |  | 
Adjusted R2 | 0.96 |  | 
AICc | 694.39 |  | 
Jarque-Bera test (Sig) | 0.61 |  | 
Koenker (BP) test (Sig) | 0.85 |  | 
SA test (Sig) | 0.27 |  | 
No biased standard errors due to heteroscedasticity
Optimal combination of factors
Not deviating from a normal theoretical distribution
Not spatial autocorrelated
Notes: In the second step, the linear regression is conducted again to select an optimal combination of valid explanatory variables.
The judgement is the statistical test for regression.
As shown in this table, there are 9 valid variables entering the model at last.

## Slide 61
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Moran's Index | Z-score | P-value* | Pattern | DIFF of Criterion** | Type
Government Area | 0.04 | 0.66 | 0.51 | Random | - | Global
Transportation Facility | 0.29 | 3.33 | 0.00 | Clustered | -1.95 | Local
Land use Aggregation | -0.01 | 0.20 | 0.84 | Random | - | Global
Transfer Dummy | 0.13 | 1.58 | 0.12 | Random | - | Global
Bicycle Parking | -0.12 | -0.92 | 0.36 | Random | - | Global
Bus Capacity | 0.70 | 7.57 | 0.00 | Clustered | 0.18 | Local
Bus Accessibility | 0.45 | 5.04 | 0.00 | Clustered | 0.04 | Local
Population/Job Balance | 0.77 | 7.61 | 0.00 | Clustered | -0.17 | Local
Tenant Proportion | 0.24 | 2.54 | 0.01 | Clustered | 1.02 | Local
* Statistical significance means autocorrelation
** More than or equal to 2.00, means the local term is better to be assumed as global
Identification for global/local variable
Notes: Before estimating the model, we should determine whether the indicator is a local or global indicator.
This procedure is conducted by using Moran’s index to examine if the variable is spatial autocorrelation or not.
The indicators with clustered pattern are selected as the local variable.

## Slide 62
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Type | OLS model |  |  |  | MGWR model |  | 
 |  | B | SE | t |  | B | SE | t
Government Area | Global | 0.05 | 0.02 | 2.41 |  | 0.05 | 0.02 | 2.59
Land Use Aggregation | Global | 11,832.53 | 5323.15 | 2.22 |  | 13,384.34 | 5,408.81 | 2.48
Transfer Dummy | Global | 6,578.09 | 1216.82 | 5.41 |  | 5,968.65 | 1,198.72 | 4.98
Bicycle Parking | Global | 7.51 | 0.93 | 8.11 |  | 7.72 | 0.90 | 8.59
Transport Area | Local | 0.11 | 0.03 | 3.58 |  | 0.10 | 0.02 | -
Bus Capacity | Local | -59.21 | 20.71 | -2.86 |  | -55.14 | 5.94 | -
Bus Accessibility | Local | 50.71 | 14.64 | 3.46 |  | 48.61 | 2.43 | -
Population/Job Balance | Local | -2,762.24 | 1,079.33 | -2.56 |  | -2,411.17 | 364.44 | -
Tenant Proportion | Local | -9,987.81 | 4,380.30 | -2.28 |  | -10,304.66 | 756.09 | -
Best bandwidth |  |  |  |  |  | 5.7km |  | 
AICc |  | 694.39 |  |  |  | 690.60 |  | 
Residual sum of squares |  | 337,744,989 |  |  |  | 296,311,499 |  | 
Estimation of Mix Geographically Weighted Regression
Notes: This is the result of estimation.
As a result, the indicators of building area have a positive effect on the subway ridership.
The indicator of land-use aggregation shows land use variety can lead to decrease in ridership.
As the expectation, the indicator of bus capacity has a negative effect on the subway ridership, and the bus accessibility has a positive effect.
The factor of resident/job balance and tenant proportion tells that working people and tenants are more willing to use subway.

## Slide 63
Model estimation
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Z-score in MGWR is lower than that in OLS
Moran’s index in MGWR is closer to the expected index than that in OLS
Indicator | OLS | MGWR
Moran’s index | 0.08 | 0.03
Expected index | -0.03 | -0.03
Variance | 0.01 | 0.01
z-score | 1.09 | 0.61
p-value | 0.27 | 0.54
Distribution of residuals
Closer to the expected value is better
Less is better
Notes: This part is the residual analysis.
From the residual distribution, Moran’s index in MGWR is closer to the expected index than that in OLS, Z-score is also lower than that in OLS.
We can say the result of MGWR is better than that of OLS.
The lower part is the distribution of residuals of both linear regression and geographically weighted regression, to have a look if the accuracy increased. The Moran’s index in MGWR is closer to the expected index than that in OLS, and the Z-score in MGWR is less than that in OLS, the accuracy did increase.

## Slide 64
Indicators system are constructed from 3 categories. Redefine the indicators of land use variety. The indicators of bus system are defined into bus capacity and bus accessibility.
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Summary
Identified global/local indicator in MGWR using the spatial autocorrelation of indicators.
Problems
Indicator system need to be enriched
1
Selection of effective indicators under small sample
2
Achievements
Insufficient consideration of spatial relevance of indicators
3
To reduce the possibility of statistical 1,2 errors in small samples, use exploratory regression to screen effective indicators and the most metric combinations.
Summary
Notes: For a conclusion, this study reorganized the indicator framework, and proposed a method of selecting valid variables for small sample.
The main findings of this study are
High diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 65
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Findings
Government Area
Land Use Aggregation
Transfer Dummy
Bicycle Parking
Transport Area
Bus Accessibility
Increasing ridership
Decreasing ridership
Bus Capacity
Population/Job Balance
Tenant Proportion
Notes: For a conclusion, this study reorganized the indicator framework, and proposed a method of selecting valid variables for small sample.
The main findings of this study are
High diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 66
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Conclusion
4.6
Recommendation
Increase bicycle parking
- Results from the indicator of bicycle parking
From the perspective of bus lines and frequency, reduce the overlap rate between bus lines and rail transit lines, strengthen the transfer function of bus system
- Results from the indicator of bus accessibility and bus capacity
Encourage new construction of apartments around the rail transit station
- Results from the indicator of tenant proportion
Notes: For a conclusion, this study reorganized the indicator framework, and proposed a method of selecting valid variables for small sample.
The main findings of this study are
High diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 67
Chapter 5
Influencing Factors on Transit Ridership at Station-to-Station Level

## Slide 68
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
Background
Main purpose
Exploring the factors influencing transit ridership at station-to-station level
The variation of land use in the catchment B can affect the probability that passengers boarding from station A choose station B as the destination
Catchment B
Station A
Station B
Ridership will vary in both the stations
If the elements varied in catchment B
Notes: At the beginning, I want to repeat it once again that why I focus on the ridership between station and station.
There is a station A, if the ridership of station A varied because of the variation in the elements within the catchment area of station A, it is obvious, the transit ridership of station B will also vary, because station A is connecting with station B, the variation of transit ridership in Station A must bring new variation in Station B.
With this issues, the purpose of this study is proposed, Exploring how the factors of land-use influence the choice of destination station for passengers from the perspective of TOD

## Slide 69
Previous study |  | Type 1 | Type 2 | Type 3 | This
Perspective | Station | ● |  |  | 
 | Station-to-station |  | ● | ● | ●
Research object | Dependent variable | Transit ridership | Transit ridership | Transportation Impedance | Destination selection probability
 | Explanatory variable | Single station | Both O and D stations | Both O and D stations | Both O and D stations
Method | Linear Regression | ● | ● |  | 
 | Gravity model |  |  | ● | 
 | Probability regression |  |  |  | ●
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Review

## Slide 70
On the research object, the ridership between ODs should be produced by the origin station, and then transferred to the destination station. Direct model for OD transit ridership is lack of this process on estimating the transfer between OD stations.
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Research focus
Problem 1
1
  Describe the transfer between station and station
To find an indicator to describe the passenger transfer between station and station
Research focus
Problems in previous studies

## Slide 71
In terms of method, the issue of analyzing the transfer of ridership between station and station usually adopt the gravity model, however, the gravity model is not used for estimating the influence of indicators.
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Research focus
Problem 2
2
  Estimate the influencing factors on the transfer of ridership between station and station
Convert this issue into the mathematical problem, then estimate the effect of influencing factors.
Research focus
Problems in previous studies

## Slide 72
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Flowchart
Influencing factors
Convert to mathematical problems
Binary choice problem
Model estimation
Result and Discussion
Choice of destination
Land use
Independent variable
impedance
Dependent variable
Probability of getting off at a specific destination station
Logistic regression
Research focus
1
Research focus
2
Notes: This is the research flow of this study.
First, I will construct the index framework, and then convert this realistic issue into a mathematical problem.
Finally, estimate the logistic regression model, and give discussion for the result.

## Slide 73
Research object
5.2
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
1
k
2
3
4
5
……
Boarding
Alighting
Station
Station k
Other
Stations
Passenger Volume
Passenger Volume
Dependent variable
Probability of choosing the destination
For the passengers boarding from station 1
The probability of getting off at station
Notes: I will give an interpretation for the research object.
With this figure, the dependent variable in this study is the probability of getting off at station k for the passengers boarding from station 1.
As is shown in this formula

## Slide 74
Research object
5.2
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Operation distance of subway
Bus accessibility
Bus capacity
Residence proportion
Office proportion
Commerce proportion
Education proportion
Land-use aggregation
Independent variables
Land use
Impedance
Notes: Here are the independent variables in this study.
The factors are selected from two aspects, land-use and impedance.
There are 8 indicators in total.

## Slide 75
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Mathematical problems
Conversion
Binary discrete model
Logistic regression model
Explanatory variable for making the choice of whether getting off
Probability of getting off at the investigated station
Notes: Now the research objects have been given, we have to convert this issue into a mathematical problems.
As the interpretation before, this issue is converted into a binary discrete problem.
I choose the logistic regression to estimate this binary discrete problem.

## Slide 76
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Station type | Station name | Population density | Commerce proportion | Office proportion | Residence proportion | Education proportion
Low-density residence | 賀茂 | 98 Person/Ha | 4% | 3% | 83% | 4%
High-density residence | 藤崎 | 173 Person/Ha | 5% | 7% | 76% | 6%
Education | 箱崎九大前 | 83 Person/Ha | 5% | 6% | 51% | 22%
Office | 呉服町 | 135 Person/Ha | 8% | 31% | 49% | 3%
Commerce | 天神 | 69 Person/Ha | 34% | 32% | 24% | 1%
Note:
The highlighted cells refer to the representative values that having much higher proportion than other land-use types.
Selecting sample station
Notes: In this problem, what we want to know is how the independent variables determine the choice of where to get off.
To master the significant features of choosing destination regarding different type of land-use, I will select some typical stations as research objective.
I chose one station from each of the land use type.
The six stations are Kamo station of medium-density residence
Fujisaki station of high-density residence
Hakozakikyudai station of education
Gofukumachi station of office
Tenjin station of commerce
and airport station.

## Slide 77
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | 0.88 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Result of estimation
Full name of the abbreviation
B-C: Bus Capacity
B-A: Bus Accessibility
L-A: Land-use Aggregation
D: Distance
R: Residence
E: Education
C: Commerce
O: Office
Increase in this type of land use will lead to an increase in the probability of choosing this station as the destination
Increase in this type of land use will lead to a decrease in the probability of choosing this station as the destination
Note
Meaning of the coefficients
1% increase in the proportion of land use will lead to a corresponding variation in the probability of getting off at the destination
Notes: This is the result of estimation.
In this table, the values less than 1 means Increase in this type of land use will lead to a decrease in the probability of choosing this station as the destination
The values larger than 1 means Increase in this type of land use will lead to an increase in the probability of choosing this station as the destination
For the meaning of the coefficients, 1% increase in the proportion of land use will lead to a corresponding variation in the probability of getting off at the destination
. The blank means this value does not pass the statistical significance test.

## Slide 78
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Discussion for results
Chart: Office
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Office 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 | 1 | 1
Chart: Commerce
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Commerce 天神 | 1 | 0.99 | 1.01 | 1.03 | 1.02 | 1.06 | 1
Chart: Airport
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Airport 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 | 0.92 | 1 | 1
Commerce
Office
Residence
Education
Land use aggregation
Distance
Bus capacity
Bus accessibility
Chart: Low-density residence
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Low-density residence 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 | 1.07 | 1.01 | 1
Chart: High-density residence
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
High-density residence 藤崎 | 1.01 | 0.99 | 1.01 | 0.98 | 0.95 | 1 | 1
Chart: Education
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Education 箱崎九大前 | 1.02 | 1.02 | 1.03 | 0.99 | 0.88 | 1 | 1
Commerce
Office
Residence
Education
Land use aggregation
Distance
Bus capacity
Bus accessibility
Odd ratio, increase in probability of choosing the destination station
Odd ratio, decrease in probability of choosing the destination station
Notes: Then I will give some details for the results.
Look at the values marked with frame.
It means the any type of Land use increased in departure station
The Probability of choosing the destination station belong to low-density residence type will decrease

## Slide 79
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Summary
Described the passenger transfer using the probability of choosing a specific destination station.
Problems
Description for the process of passenger transfer needs to be clear.
1
The model should be able to reflect the influence extent of the indicators.
2
Achievements
The problem is converted into a binary choice question. Logistic regression is used to estimate the influence of land use on the probability of passenger destination selection, also taking into account the influence of inter-station impedance.
Notes: This is the chapter 5, the main findings of this chapter is as belowpp, Defined the “connectivity” between station and station. The influence of land use on the connectivity was estimated.
Also we got some implications for the future, Further enrich the indicator system. The share of different transportation modes should be considered. The indicators belong to impedance should be improved. The influence of bus system also should be considered at the station-to-station level

## Slide 80
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Findings
The probability of choosing a destination has a trend of decreasing between the same type of land use.
The probability of choosing a destination belong to low-density residence type has no tend to raise regarding to the variation of land use in the departure station.
Increase in the education land use tends to lead increase in the ridership between station and station.
Notes: This is the chapter 5, the main findings of this chapter is as belowpp, Defined the “connectivity” between station and station. The influence of land use on the connectivity was estimated.
Also we got some implications for the future, Further enrich the indicator system. The share of different transportation modes should be considered. The indicators belong to impedance should be improved. The influence of bus system also should be considered at the station-to-station level

## Slide 81
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Recommendations
It is recommended to pay more attention to the location of rail transit stations while judging the site selection of a newly planned school.
- Results from finding 3
For low-density residence type stations, it is recommended that promoting the utilization of rail transit could start with other measures than land use, such as fare adjustment.
  - Results from finding 2
Combined with the achievement from chapter 4, a complete forecasting model for rail transit ridership is possible to be established.
  - Results from chapter 4 and chapter 5
Notes: This is the chapter 5, the main findings of this chapter is as belowpp, Defined the “connectivity” between station and station. The influence of land use on the connectivity was estimated.
Also we got some implications for the future, Further enrich the indicator system. The share of different transportation modes should be considered. The indicators belong to impedance should be improved. The influence of bus system also should be considered at the station-to-station level

## Slide 82
Chapter 6
Conclusion

## Slide 83
Conclusion
6.1
Chapter 6 - Conclusion
Summary
Chapter 2 discussed how the walking duration to rail transit station is affected by passengers’ attributes. Centering with this problem, 3 specific research questions are proposed according to the previous studies, then the answers to each question were given.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
One

## Slide 84
Conclusion
6.1
Chapter 6 - Conclusion
Summary
Chapter 3 summarized the characteristics of rail transit ridership and land use in the case of Fukuoka, which helped to make a comprehensive understanding of the research object in this dissertation. This chapter also gave some important reference and implication for the next research.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Two

## Slide 85
Conclusion
6.1
Chapter 6 - Conclusion
Summary
Chapter 4 explored and estimated the influencing factors on rail transit ridership at the station level. With the focus on the case of Fukuoka with small sample size, this chapter proposed improved approach from indicator system, valid indicator selection, and model estimation three aspects, and the results are proved effective and improved.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Three

## Slide 86
Conclusion
6.1
Chapter 6 - Conclusion
Summary
Chapter 5 gave a description for the transfer of ridership between station and station that use the land use type around a station to explain the probability of choosing that station as the destination station. Then ran logistic regression to estimate the influence of land use on the probability of getting off at the destination station. The influence of land use on the transfer of ridership between station and station is confirmed in this chapter.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Four

## Slide 87
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Recommendations
6.2
Station
A
C
B
11 min
7 min
5 min
Block
Achievement from Chapter 2
Combination with the achievements
Model
The trend (probability) of using this station in the blocks can be mastered.
PSDC data in the blocks (e.g. A/B/C)
input
output
Using the estimated catchment area to make prediction of transit ridership
Using the results of ridership transfer between station and station to correct the prediction of ridership at single station
Application of the achievements
Estimating the catchment area
Notes: Now we get the conclusion of this study.
In summary, this study estimated the probability of accepting the given threshold of waling duration to rail transit stations.
Well, what can we do with this achievement?
As this figure, for example we have a station in the center, and three blocks around this station, the distances to this station are not the same for the 3 stations. Now if we have the data of personal attributes in each block, we can input this dataset into the model discussed in this study, and then get the trend of using this station in each block.
With this output, obviously, the catchment area of the station can be estimated.
This is the contents of chapter 2.

## Slide 88
Organization
0.0
Introduction
Chapter 1
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Analysis on the characteristics of transit ridership and land use
Influencing Factors on Transit Ridership at Station Level
Influencing Factors on Transit Ridership at Station-to-Station Level
Conclusion
Chapter 6
Chapter 5
Chapter 4
Chapter 3
Chapter 2
Notes: At the first, I want to give an overview for the organization.
This dissertation is organized by 6 chapters.
Chapter 1 is introduction….

## Slide 89
Chapter 1 - Introduction
Background
1.1
Problems
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3
Chart: Population estimation of Fukuoka
| 1985 | 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
0-14 years old | 252 | 231 | 205 | 191 | 188 | 192 | 201 | 204 | 201 | 189 | 176 | 168 | 165 | 164
15-64 years old | 816 | 886 | 933 | 968 | 984 | 998 | 1002 | 996 | 996 | 993 | 975 | 937 | 901 | 870
65 and older | 91 | 113 | 142 | 178 | 213 | 254 | 322 | 367 | 395 | 422 | 454 | 497 | 524 | 539
unknown | 1 | 7 | 5 | 4 | 16 | 20 | 0 | 1 | 0 | 0 | 1 | -1 | 0 | 0
sum | 1160 | 1237 | 1285 | 1341 | 1401 | 1464 | 1525 | 1568 | 1592 | 1604 | 1606 | 1601 | 1590 | 1573
Notes: This research uses the Fukuoka public rail transit as the study case to examine the influencing factors on ridership.
At the very beginning, I’d like to give an introduction of the background in Fukuoka.
Nowadays, even though Fukuoka is still in a rapid growth, there are also many social problems that Fukuoka is facing now.
One of that is the aging population, this figure gives the prediction of Fukuoka’s population in tens years. As we can see, The population of that in production age has reached the peak recently, and the total population will reach the peak in ten years. The population structure is not optimistic in Fukuoka.

## Slide 90
Aged society
Low birthrate
Fiscal burden
Urbanization
Congestion, pollution
Lack of resources
Chapter 1 - Introduction
Background
1.1
Developed Countries
Developing Countries
sustainability
Increasing supply
Improving financial situation
Exploring the determinants of rail transit ridership
Increase public transportation utilization
How is the research topic proposed ?
Status quo
Demand
Measure
Topic
Notes: As we know, nowadays, most of the cities either in developing countries or developed countries, are facing somewhat social problems. I can give a familiar and obvious instance, my country, China, now is still at the period of rapid urbanization, many problems like traffic congestion, air pollution, are not solved yet, while Japan, where now I’m living in, has totally different social problems, like serious aged society, low birthrate, heavy fiscal burden. Therefore, the developing countries like China have more demands on resource and environment protection, while developed countries like Japan need to improve financial situation. However, the demands of both developing and developed country can be viewed as sustainability. For this common demand, promoting public transportation is widely accepted as one of the most important measures.
With the goal of increasing public transportation utilization, the topic was proposed, that is exploring the determinants of rail transit ridership.

## Slide 91
Chapter 1 - Introduction
Research purpose
1.2
Primary questions
What influence the walking duration to transit stations?
1
What factors explain transit ridership at station level?
2
What factors influence the transit ridership between station and station?
3
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: 0. Around this topic, there are 3 primary questions to answer.
1. The first one is what influence the walking duration to transit stations? Since most travel accessing the transit station is walking, the walking duration should be one of the most important factors influencing the ridership.
2. The second is what factors explain transit ridership at station level? As we know, the environment around a station of cause can affect the ridership of this station, so our aim is to find and estimate the influencing factors.
3. Based on the second question, because stations are in the network, the ridership in one of the stations varied, the ridership in other stations must vary as well. Here the third question is proposed, that is what factors influence the transit ridership between station and station.
00. These are the primary questions in this dissertation

## Slide 92
Year |  | 2004 | 2004 | 2009 | 2010 | 2011 | 2012 | 2013 | 2013 | 2015
Author |  | Chu | Kuby et al. | Taylor et al. | Sohn and Shim | Gutiérrez et al. | Cardozo et al. | Chakraborty et al. | Zhao et al. | Jun et al.
Catchment (walking distance) |  | 400m walking distance | 800m walking distance | N/A | N/A | Distance-decay 800m buffer | 800m walking distance | N/A | 800m radius | 300m,600m,900m radius
Method |  | Poisson Regression | WLS | 2SLS | OLS/SEM | OLS | OLS/GWR | OLS/SEM | OLS | OLS/MGWR
Sample Size |  | 2568 | 268 | 265 | 251 | 158 | 190 | 900 | 55 | 442
Number of Valid Indicator |  | 15 | 11 | 8 | 7 | 9 | 4 | 9 | 11 | 11
Coefficient of determination (Adjusted R2) |  | 0.54 | 0.71 | 0.91 | 0.60 | 0.73 | 0.56 | 0.69 | 0.95 | 0.77
Building environment | Built environment |  |  |  | ● | ● |  | ● | ● | ●
 | Hospital |  |  |  |  |  |  |  | ● | 
 | School/University |  |  |  | ● |  |  |  | ● | 
 | CBD |  | ● |  |  |  |  |  | ● | 
 | Land use mix |  |  |  | ● | ● | ● |  |  | ●
 | Other infrastructures |  | ● |  |  |  |  |  | ● | ●
Transportation Accessibility | Accessibility of pedestrian | ● |  |  |  |  |  | ● |  | 
 | Accessibility of transfer |  | ● |  | ● | ● | ● | ● | ● | ●
 | Road coverage |  |  | ● | ● |  |  |  | ● | 
 | Parking |  | ● |  |  |  |  |  | ● | 
 | Service level of public transit | ● | ● | ● |  | ● | ● |  | ● | ●
 | Locational factor |  | ● |  | ● |  |  |  | ● | 
Demographic and Socioeconomic Environment | Population |  | ● | ● | ● |  | ● | ● | ● | ●
 | Employment | ● | ● | ● | ● | ● | ● | ● | ● | ●
 | Age | ● |  | ● |  |  |  |  |  | ●
 | Tenant proportion |  | ● |  |  |  |  |  |  | ●
 | Race | ● | ● | ● |  | ● |  |  |  | 
 | Income | ● |  |  |  |  |  | ● |  | 
 | Vehicles holdings | ● |  |  |  |  | ● | ● |  | 
 | Fare |  |  | ● |  |  |  |  |  | 
Chapter 1 - Introduction
Literature review
1.3
Points discussed in previous studies
Catchment area
Model
Indicator system
Lack of consideration
Small sample case
The ridership between station and station
Notes: With the primary questions, I will give an overview of the previous studies.
Most studies paid the concentration on catchment area, model construction and estimation, and the indicator system.
But very few studies focus on the small sample case and the ridership transfer between station and station.

## Slide 93
Chapter 1 - Introduction
Research contents
1.4
Specific research topic
Exploring the willingness of walking duration to transit stations regarding passengers’ personal attributes.
Chapter 2
Analyzing the characteristics in the variation of transit ridership.
Chapter 3
Exploring the approach of screening effective influencing factors in small sample case
Chapter 4
Shifting the research perspective, trying to describing the variation of ridership between stations and stations.
Chapter 5
1
2
3
4
Notes: Based on the research purpose and previous studies, 4 specific research topics are proposed, corresponding to the chapters from 2 to 5.
Chapter 2 is Exploring the willingness of walking duration to transit stations regarding passengers’ personal attributes.
Chapter 3 is Analyzing the characteristics in the variation of transit ridership.
Chapter 4 is Exploring the approach of screening effective influencing factors in small sample case
Chapter 5 is Shifting the research perspective, trying to describing the variation of ridership between stations and stations.
This is the introduction of my dissertation.

## Slide 94
Chapter 1 - Introduction
Research purpose
1.2
Explore the determinants of rail transit ridership
Giving reference for increasing the rail transit ridership
What factors influence transit ridership among stations?
Main purpose
Subject topics
What determines catchment area?
What factors explain transit ridership at station level?
Notes: With this topic, I will interpreter the research purpose in details. The main purpose of this research can be briefed to exploring the determinants of rail transit ridership, thus giving reference for increasing the rail transit ridership.
In details, the subject topics discussed in this research mainly have 3 parts. They are, what determines catchment area, what factors explain transit ridership at station level, what factors influence transit ridership among stations.

## Slide 95
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 96
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 97
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 98
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3
Demands
Promoting the use of rail transit
Alleviating the pressure on government finances

## Slide 99
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Catchment area
Influencing factor
Research Point
(This Study)
Environment
Behaviors
Personal Socio-Demographic Characteristics
(abbreviated as PSDC)
Walking duration to transit stations
Relationship
The area passengers can accept to walk to the station
Research position
Notes: Before I introduce this research, I want to give a brief position for it. As we know, obviously, the catchment area is a basic determinants for the use of transit station. According to the previous research, catchment area should be determined by various factors, like built-environment, facilities, also people’s behaviors. In this research, we chose the perspective of people’s behaviors to investigate how the catchment area is determined. The walking duration and personal socio-demographic characteristics are used to represent the catchment area and people’s behaviors, respectively.

## Slide 100
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Research position
Behaviors
Acceptable walking duration to rail transit stations
Catchment area
Determine
Walk to the station
How the socio-demographic characteristics influence the acceptable walking duration
Research purpose
Personal attributes
Socio-demographic characteristics
(abbreviated as PSDC)
Walking duration to transit stations
Notes: Since pedestrian accounts most rail transit users, the walking distance and duration can determine the catchment area to a large extent. And the walking duration is thought to be affected by the behavior preference, which should be affected by personal attributes like socio-demographic characteristics.
Now we can carry out the main research purpose, How the socio-demographic characteristics influence the acceptable walking duration?

## Slide 101
Threshold of walking duration
Continuous value of Walking duration
Research object
Examine the probability of accepting the given threshold of walking duration
Explore how the PSDC can affect the acceptable walking duration to transit stations using the data of person trip survey.
Research purpose
Entry point
Try to explain the acceptable walking duration using probability.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
The work of this study
Notes: With the interpretation of the existing problems in previous studies, here the research purpose is proposed, that is to explore how the personal socio-demographic characteristics can affect the acceptable walking duration to transit stations using the data of person trip survey.
And different from the existing studies, I investigate the walking duration by some specific threshold value rather than the continuous value. Moreover, the estimation of relationship is not from the perspective of regression but the probability.
That is to say, I will check the probability of choosing walking to transit stations at some specific threshold.

## Slide 102
Threshold of walking duration
Continuous value of Walking duration
Examine the probability of accepting the given threshold of walking duration
Entry point
Try to explain the acceptable walking duration using probability.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Research object
Acceptable walking duration
Where the is the acceptable walking duration for the people with those factors
Notes: With the interpretation of the existing problems in previous studies, here the research purpose is proposed, that is to explore how the personal socio-demographic characteristics can affect the acceptable walking duration to transit stations using the data of person trip survey.
And different from the existing studies, I investigate the walking duration by some specific threshold value rather than the continuous value. Moreover, the estimation of relationship is not from the perspective of regression but the probability.
That is to say, I will check the probability of choosing walking to transit stations at some specific threshold.

## Slide 103
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Evaluation of features
2.5
Individual Value |  | Group Trend | 
Actual | Prediction | Actual | Prediction
1 | 1.000 | 0.654 | 0.637
1 | 0.897 | 0.653 | 0.636
1 | 0.897 | 0.651 | 0.635
… | … | … | …
0 | 0.621 | 0.581 | 0.580
1 | 0.621 | 0.581 | 0.579
1 | 0.621 | 0.580 | 0.579
… | … | … | …
0 | 0.498 | 0.435 | 0.411
1 | 0.496 | 0.437 | 0.411
1 | 0.496 | 0.434 | 0.410
… | … | … | …
The predicted result is probabilities of accepting the giving threshold of walking duration.
The accuracy of results are evaluated by using the method of simple moving average.
Simple moving average
Prediction
200 records
Average
Notes: The result of decision tree is as shown in the figure. Here I just give a summary of the result to show.
As shown in the table on the right part, column of actual is the actual choice of individual, the prediction column is the value obtained from the estimation of decision tree.
The results are evaluated by using the method of simple moving average.
Sort the result by probability in descending order, the group trend is expressed by the average value of 200 samples.
So the trends between practice and prediction can be compared.

## Slide 104
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of prediction
Evaluation of 13 minutes threshold
Slightly high precision
The threshold of 13 minute is not a commonly acceptable walking duration
Some one who can accept this threshold can be considered to have some specific characteristics.
The features are significant at this threshold.
Notes: Next is the evaluation at 13minutes threshold.
We can see the precision is neither good not bad.
A little like the result at 5 minutes threshold, because the threshold of 13 minute is not a commonly acceptable walking duration. Some one who can accept this threshold can be considered to have some specific characteristics. This significant difference from the other passengers explains this fitness at 13 minutes threshold.

## Slide 105
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 5 minutes threshold
The features are significant at 5 minutes threshold.
The threshold of 5 minute is a commonly acceptable walking duration.
Good fitness
Evaluation of prediction
Notes: Continuously, I will show the trend line of prediction at each threshold of walking duration.
First is the 5 minutes threshold.
As we can see, the prediction trend line fit the actual trend line quite well, the features are significant at this threshold.
The threshold of 5 minute is a commonly acceptable walking duration

## Slide 106
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 8 minutes threshold
The features are not significant at 8 minutes threshold.
There is randomness in choosing whether accepting the 8 minutes walking duration or not.
Low fitness
Evaluation of prediction
Notes: Next is the 8 minutes threshold.
The fitness at 8 minutes is not well, the features are not significant at this threshold.
There is randomness in choosing whether accepting the 8 minutes walking duration or not.

## Slide 107
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 13 minutes threshold
The features are significant at 13 minutes threshold.
The threshold of 13 minute is not a commonly acceptable walking duration
Good fitness
Evaluation of prediction
Notes: The fitness at 13 minutes is not bad.
From the probability we can know the 13 minutes is not a commonly accepted walking duration.

## Slide 108
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Type | Station No. | Population-density | Office | Commerce | Residence | Education
Low-density residence | 30 | 33 | 1.70% | 41.50% | 44.95% | 0.18%
 | 26 | 54 | 2.81% | 1.23% | 58.26% | 2.85%
 | 29 | 78 | 3.02% | 5.40% | 75.86% | 6.94%
 | 27 | 79 | 4.30% | 4.24% | 75.87% | 0.77%
 | 28 | 81 | 3.55% | 3.42% | 73.46% | 6.24%
 | 3 | 91 | 4.01% | 8.58% | 59.97% | 6.25%
 | 33 | 101 | 1.74% | 2.10% | 81.71% | 7.84%
 | 24 | 103 | 2.14% | 2.17% | 66.82% | 8.30%
 | 34 | 109 | 2.38% | 3.28% | 86.12% | 0.86%
Land use characteristics
Station classification based on land use
Low-density residence
Low population-density
High proportion of residence
Notes: According to the analysis of land use indicators, all the 35 stations are classified into several types.
The first is low-density residence, with Low population-density, and High proportion of residence

## Slide 109
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
High-density residence
High population density
High proportion of residence
Type | Station No. | Population-density | Business | Commerce | Residence | Education
High-density residence | 19 | 121 | 2.17% | 3.15% | 76.63% | 0.12%
 | 13 | 125 | 11.11% | 6.48% | 46.08% | 4.51%
 | 16 | 142 | 4.59% | 5.03% | 72.75% | 2.68%
 | 18 | 142 | 2.27% | 1.96% | 64.58% | 6.80%
 | 31 | 143 | 4.14% | 2.26% | 54.17% | 18.28%
 | 17 | 144 | 6.02% | 7.28% | 55.45% | 10.60%
 | 12 | 145 | 4.16% | 1.77% | 66.22% | 4.39%
 | 32 | 170 | 1.17% | 1.28% | 73.54% | 9.93%
 | 23 | 193 | 10.00% | 6.18% | 44.52% | 2.56%
Notes: The second is high-density residence, with high population-density, and High proportion of residence

## Slide 110
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Education
High proportion of education
Type | Station | Population-density | Business | Commerce | Residence | Education
Education | 25 | 35 | 1.38% | 2.31% | 30.04% | 39.83%
 | 1 | 56 | 8.70% | 1.91% | 48.01% | 17.89%
 | 35 | 58 | 5.63% | 3.78% | 55.18% | 21.37%
 | 4 | 67 | 4.93% | 3.49% | 33.52% | 14.63%
 | 2 | 77 | 4.03% | 11.75% | 44.03% | 23.24%
 | 5 | 89 | 11.53% | 7.26% | 30.51% | 7.30%
Notes: The third is education, with high proportion education

## Slide 111
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Downtown commerce
High proportion of business
High proportion of commerce
Type | Station | Population-density | Business | Commerce | Residence | Education
Downtown commerce | 9 | 64 | 44.97% | 20.55% | 10.62% | 0.70%
 | 20 | 67 | 34.60% | 36.74% | 11.34% | 1.26%
 | 8 | 67 | 42.97% | 27.86% | 12.23% | 0.59%
 | 11 | 79 | 37.12% | 17.38% | 18.47% | 1.89%
 | 10 | 92 | 30.76% | 26.26% | 15.72% | 1.74%
Notes: Then is downtown commerce, with high proportion in both business and commerce.

## Slide 112
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Office
High proportion of business
Type | Station | Population-density | Business | Commerce | Residence | Education
Office | 15 | 64 | 31.63% | 7.80% | 25.80% | 5.73%
 | 6 | 96 | 34.56% | 17.29% | 21.61% | 1.75%
 | 14 | 105 | 26.97% | 17.27% | 17.61% | 2.80%
 | 21 | 136 | 22.86% | 16.12% | 33.66% | 2.70%
 | 22 | 167 | 21.38% | 12.53% | 36.79% | 2.50%
Notes: Next is the office type, with high proportion in business.

## Slide 113
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Purpose
Explore and explain the factors influencing subway ridership at station level using a small sample case
1
  Improve index system
Propose and reconstruct indicators to improve the index system
Identify valid indicators
2
Propose effective index screening method for small samples
Improve accuracy in estimation
3
Consider the different spatial distribution of indicators in the spatial regression model
Research questions
Notes: The main purpose of chapter 4 is to explore and explain the factors influencing subway ridership at station level using a small sample case.
Around this purpose, this study focuses on three specific topics.
The first one is to propose and reconstruct indicators to improve the index system
Second is to find an approach of identifying the valid indicators for small sample case.
The third one is to consider the different spatial distribution of indicators in the spatial regression model to improve accuracy in estimation.

## Slide 114
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Bus capacity
Bus Accessibility
: is the number of bus lines passing through the th bus station.
: the number of bus stations within catchment area of subway station
: the number of lines in one bus station and
: is the frequency of NO. line at NO. station.
Notes: There are the two indicators about bus system. In this study, I considered the effect of bus system from two opposite parts, one is the bus capacity, and the other one is bus accessibility.
The indicator of bus capacity represents the ability of how many passengers the bus system can transfer, it relates to the number of bus stops, bus lines and the frequency of bus within the catchment area. It is expected to have negative effect on rail transit ridership, since the large bus capacity may share parts of the passengers from rail transit.
The indicator of bus accessibility represents the areas connecting to the bus system within the catchment area. It only relates to the number of bus lines. This indicator is expected to have positive effect on rail transit ridership, since a better accessibility of bus may take more rail transit passengers.

## Slide 115
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
: the average proportion of type land use.
: the type of land use (respectively government, commercial, residence and education)
: the floor area of land use type within catchment area of subway station
The indicator of land-use mix is re-defined into the aggregation of land-use.
Indicators
4.2
Variable interpretation
Land-use Aggregation
Range of PCA | Residence | Office | Commerce | Education | Total
600 | 51.8% | 19.3% | 13.8% | 5.5% | 90.5%
800 | 55.3% | 17.5% | 12.0% | 6.2% | 90.9%
1000 | 57.6% | 16.5% | 10.8% | 6.0% | 90.9%
1200 | 59.2% | 15.5% | 10.2% | 5.9% | 90.8%
Ave | 62.8% | 10.1% | 7.5% | 5.3% | 85.7%
Average
Notes: Let me go on to interpret some of the indicators. Firstly, the variable of land-use aggregation. This indicator is used to describe the variety of land use. Maybe we usually hear about the word of land-use mix, but not aggregation. Here I redefined it. Look at this formula, it represents the spatial distance between the uppercase P and lowercase p, where the uppercase P means the average proportion of each kind of land use, and the lowercase p represents the proportion in the observing station. The higher the indicator A is, the function of land use is more aggregative, which means the land use variety is lower. The reference value of uppercase P is calculated from the average of all the stations in Fukuoka, using the catchment area of 800 meters walking distance.

## Slide 116
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Bus capacity
Share passengers from rail transit. Negative effect on rail transit ridership
Bus Accessibility
Bring passengers to rail transit. Positive effect on rail transit ridership
Departure
Departure
Destination
Share passengers from rail transit
Bring passengers to rail transit
Indicators of bus system
Notes: In this study, the indicator of bus system is considered from two aspects.
Like shown in the figure, bus should have two effect on the rail transit, one is bringing passengers to rail transit, and another one is share passengers from rail transit.
The indicator of bus capacity is expected to share passengers from rail transit, having negative effect on rail transit.
The indicator of bus accessibility is expected to bring passengers to rail transit, having positive effect on rail transit.

## Slide 117
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Fixed Gaussian kernel function
Chart: AICc
5.7km
Golden-section search
MGRW parameter
Kernel Type
Bandwidth selection method
Ordinary regression
MGRW model
means the weight at the coordinate of
Notes: With these screened indicators, I’m going to estimate the influence on transit ridership quantitively. The transit ridership is not like the common sampling data, it also depends on spatial distribution. Therefore the mix geographically weighted regression is used to deal with the spatial relationship. As we can see the difference between the two formula, beta means the weight at the coordinate of (u, v). The two important parameters in MGRW is set as shown. The bandwidth is set to 5.7 kilometers, which is selected by golden-section search.

## Slide 118
Residual Analysis
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Transportation Facility Area
Bus Capacity
Bus Accessibility
Population Job Balance
Tenant Proportion
Not Significance
P = 0.01
P = 0.05
P = 0.10
Significance Map
Significance Map
Notes: The spatial distribution of significance for each local variable are mapped in Figure 4.4. For the variables of building area of transportation, bus capacity, bus accessibility, job-resident balance and tenant proportion, there are 33, 34, 35, 24 and 32 data points having statistical significance at confidence level 95% respectively. As in the figures, the two indicators for bus that proposed in this study have good performance in terms of significance and stability, while the variable of ‘tenant proportion’ has a little worse stability.

## Slide 119
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Reclassified and reorganized the indicator framework.
Proposed the approach of selecting variables from candidates using the tool of exploratory regression in ArcGIS.
Provided a method for judging whether a variable is global or local used in estimating the MGWR model.
Main works
Main findings
The higher diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.
Notes: For a conclusion, this study reorganized the indicator framework, and proposed a method for selecting valid variables. Also, provided a way for judging whether a variable is global or local in the mix geographically weighted regression model.
Also there are some interesting finding from this study.
The higher diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 120
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
 | Scale | Objective
Station-Level | single station | Passenger volume of station
Station-to-Station-Level | station network | OD passenger volume
To describe the connectivity between different stations using OD ridership.
To explain how the connectivity is determined by land-use factors.
Description for the research
Differences with station-level
Research contents
Notes: This study is at the station-to-station level, but not station-level. Different from station-level, the research scale shift to station network but not a sing station, the research objective is changed to OD passenger volume but not the passenger volume of single station. The emphasis of station-to-station level is not only the prediction of ridership, but also the connectivity between the station and station.
The research contents mainly have two parts, to describe the connectivity between different stations using OD ridership, and to explain how the connectivity is determined by land-use factors.

## Slide 121
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Flowchart
Index framework
Dependent variable
Independent variable
Conversion of realistic issue
Discrete choice issue
Logistic regression
Model estimation
Result and Discussion
Probability of getting off at a specific destination station
Notes: This is the research flow of this study.
First, I will construct the index framework, and then convert this realistic issue into a mathematical problem.
Finally, estimate the logistic regression model, and give discussion for the result.

## Slide 122
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Boarding
Alighting
……
Other
Stations
Station 1
……
Station 2
Station k
Choice of whether to get off at station k
Affect
Independent variable
Dependent variable
Description for the research question
land-use feature of boarding station
Impedance between boarding and alighting station
Notes: Before constructing the mathematical model, I am going to explain how to convert this realistic problem into a mathematical problem. If we examine the case of alighting station k, this probability of getting off at station k is affected by the land-use and impedance of boarding station. Here we can convert this problem into a discrete choice problem. And it can be expressed using logistic regression. In this logistic regression, if we take the alighting station k as an example, the dependent variable is the connectivity between all the boarding stations and alighting station k, it is the probability of getting off at station k. The independent variables are the land-use of departure stations and the impedance between boarding stations and the alighting station k.

## Slide 123
Chart: 
| Commerce | Office | Residence | Education | Land use aggregation
Low-density residence 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97
High-density residence 藤崎 | 1.01 | 0.99 | 1.01 | 0.98
Education 箱崎九大前 | 1.02 | 1.02 | 1.03 | 0.99
Office 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99
Commerce 天神 | 1 | 0.99 | 1.01 | 1.03 | 1.02
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Discussion for results
Commerce
Land use aggregation
Education
Residence
Gray areas represent negative effects
All in the white area
All in the gray area
Office
Notes: Then I will give some details for the results.
Look at the values marked with frame.
It means the any type of Land use increased in departure station
The Probability of choosing the destination station belong to low-density residence type will decrease

## Slide 124
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Main works
In the future
Defined the “connectivity” between station and station
The influence of land use on the connectivity was estimated
The indicator system should be further enriched
The share of different transportation modes should be considered
The indicators belong to impedance should be improved
The influence of bus system also should be considered at the station-to-station level
Notes: This is the chapter 5, the main work of this study includes two parts, Defined the “connectivity” between station and station. The influence of land use on the connectivity was estimated.
Also we got some implications for the future, Further enrich the indicator system. The share of different transportation modes should be considered. The indicators belong to impedance should be improved. The influence of bus system also should be considered at the station-to-station level

## Slide 125
Contributions
6.2
Chapter 6 - Conclusion
Chapter 2
Reinterpreted the implication of surveyed walking distance/duration to transit stations. The surveyed walking distance/duration has no linear relation with people willingness but just the reﬂection of the distance between departures and stations.
Described the correlation between surveyed walking duration and people’s individual characteristics from the view of probability, which can be further applied to the estimation of catchment area of rail transit stations.

## Slide 126
Contributions
6.2
Chapter 6 - Conclusion
Chapter 3
Analyzed the trend of variations in transit ridership, and classiﬁed the sub-way stations of Fukuoka into 5 types in terms of land use. Conﬁrmed the correlations between transit ridership and land use.

## Slide 127
Contributions
6.2
Chapter 6 - Conclusion
Chapter 4
Considered the inﬂuence of bus on rail transit ridership from both the sides of bus capacity and bus accessibility, and veriﬁed that the effect of bus capacity is positive to rail transit ridership, while the effect of bus accessibility is negative.
Proposed the approach of screening valid indicators by introducing the exploratory regression, and conﬁrmed its effectiveness in a small sample case.
Distinguished the local and global variables in MGWR model by examining the spatial distribution of each variable, and the effectiveness was conﬁrmed in the estimation of MGWR model

## Slide 128
Contributions
6.2
Chapter 6 - Conclusion
Chapter 5
By examining the probability of selecting the destination station from all the stations, established a logistic regression model for describing the correlation between stations and stations.
Quantitatively validated the impact of land use types on the selection of destination stations.

## Slide 129
Summary
6.1
Chapter 6 - Conclusion
Analyzed the inﬂuence of various factors on rail transit ridership from station level and station-to-station level respectively.
Provided new explanations for the catchment area of rail transit stations.
Provided an approach for selecting the valid indicators
Proposed a ridership forecasting method with the consideration of interaction among stations and stations
Main findings

## Slide 130
Recommendations
6.2
Chapter 6 - Conclusion
How to increase the use of rail transit
People’s walking preferences have signiﬁcant inﬂuence on the use of rail transit. It is suggested that the design for pedestrian accessibility should also consider the individual characteristics of resident, thus helping increase the use of rail transit.
With the development of rail transit, if viewing from the whole transit system, the positioning of bus system is gradually inclining to be the connection between departures and rail transit. Rather than planning higher capacity for bus transport, it is suggested to plan more accessible bus routes which can help people use rail transit more convenient.
According to the ﬁndings, the more aggregation in land use functions the more demand in rail transit. Thus suggesting to connect more functional regions as possible when making rail transit planning.

## Slide 131
Recommendations
6.2
Chapter 6 - Conclusion
The further research
Enrich indicator system
Combine the estimation of catchment area and the prediction of transit ridership.
Explore how the rail transit affect land use.
Explore the balance condition among various elements in the catchment area of transit stations, including human, resource, land use, transportation etc., providing reference to create the compact city.

## Slide 132
Chapter 1
Introduction
Background
Research contents
Primary research questions
Research purpose
Notes: The chapter 1 is a brief introduction for the whole dissertation

## Slide 133
Chapter 2
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
Methods
Data description
Selection for Valid Features
Estimation of Features
Result and Discussion
Conclusion
Notes: The chapter 2, Analyzing Willingness of Walking Duration to Transit Stations Using passenger’s personal attributes

## Slide 134
Chapter 3
Analysis on the characteristics of transit ridership and land use
Introduction
Data
Characteristics of transit ridership and land use
Exploration the influence on transit ridership
Conclusion
Notes: Next, Chapter 3, Analysis on the characteristics of transit ridership and land use.

## Slide 135
Chapter 4
Influencing Factors on Transit Ridership at Station Level
Introduction
Indicators
Identification of valid factors
Model estimation
Residual analysis
Conclusion
Notes: Next, chapter 4, Influencing Factors on Transit Ridership at Station Level.

## Slide 136
Chapter 5
Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
Research object
Method
Results and Discussion
Conclusion
Notes: Chapter 5, Influencing Factors on Transit Ridership at Station-to-Station Level

## Slide 137
Chapter 6
Conclusion
Findings
Recommendations

## Slide 138
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
The question to answer
What influence the walking duration to transit stations?
1
What factors explain transit ridership at station level?
2
What factors influence transit ridership between station and station?
3
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: This study aims to answer the first primary question that I proposed at the very beginning.
That is, what influence the walking duration to transit stations.

## Slide 139
What factors influence transit ridership between station and station?
3
What influence the walking duration to transit stations?
1
Introduction
4.1
The question to answer
What factors explain transit ridership at station level?
2
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: Chapter 4 aims to answer the second question that I proposed at the very beginning
it is What factors explain transit ridership at station level?

## Slide 140
What influence the walking duration to transit stations?
1
Introduction
5.1
The question to answer
What factors explain transit ridership at station level?
2
What factors influence transit ridership between station and station?
3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: This chapter aims to answer the third question that I proposed at the very beginning, that is What factors influence transit ridership between station and station?

## Slide 141
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: All types
Probability of choosing the destination station belong to low-density residence type: decrease
画成雷达图
Notes: Then I will give some details for the results.
Look at the values marked with frame.
It means the any type of Land use increased in departure station
The Probability of choosing the destination station belong to low-density residence type will decrease

## Slide 142
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: increase in education
Probability of choosing the destination station: increase
Notes: Look at the column of education
It means the Increase in the education land use tends to lead increase in the ridership between station and station.

## Slide 143
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: The same type with the that of the destination station
Probability of choosing the destination station: decrease
Notes: Look at the values with frames.
This represent, the probability of choosing a destination has a trend of decreasing between the same type of land use.

## Slide 144
Conclusion
6.1
Chapter 6 - Conclusion
Walking duration
5 minutes is a widely accepted walking duration to rail transit.
Whether accepting the 8 minutes walking duration is ambiguous in passenger’s practical behaviors.
Passengers with the private travel purpose tend to accept the longest walking duration.
Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.

## Slide 145
Findings
6.1
Chapter 6 - Conclusion
Valid factors selection in small sample case
Approach of screening valid indicator in small sample case is confirmed to be effective.
High diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 146
Findings
6.1
Chapter 6 - Conclusion
Choice of destination regarding land use
Confirmed the influence of land use on the choice of destination.
The probability of choosing a destination has a trend of decreasing between the same type of land use.
The probability of choosing a destination belong to low-density residence type never increase regarding to the variation of land use in the departure station.
Increase in the education land use tends to lead increase in the ridership between station and station.