## Slide 1
Research on Determinants of Rail Transit Ridership
 Taking Fukuoka, Japan as a Study Case 
CHEN Qi
Graduate School of Human-Environment Studies,
Kyushu University, Japan
January 30, 2019
Notes: Good morning everyone, I’m Chen Qi, from Zhao laboratory. Thanks for everyone coming to my dissertation defense.
let me begin my presentation. The title of my dissertation is Research on Determinants of Rail Transit Ridership, taking Fukuoka, Japan as a Study Case.

## Slide 2
Agenda (dissertation overview)
0.0
Introduction
Background
Research questions
Empirical Work
Willingness of Walking Duration to Transit Stations
Characteristics of Transit Ridership and Land Use
Influencing Factors on Transit Ridership at Station Level
Influencing Factors on Transit Ridership at Station-to-Station Level
Conclusion
Findings
Recommendations
Notes: Here a little bit about the agenda for quickly running into the presentation. This dissertation is mainly constructed by 3 parts, the introduction, four empirical studies, and the conclusion.

## Slide 3
Introduction
Chapter 1
Notes: The first chapter, introduction

## Slide 4
Background
1.1
Beginning
Chapter 1 - Introduction
Notes: I‘d like to begin my topic with a photograph. We can see a quite serious traffic congestion in this slide. The express way is also blocked due to the snow. If you are blocked on the way home after work, how do you think about this situation? Of course, I think it should not be a good experience.

## Slide 5
Meet the increasing traffic demand
Promote urban development
Capacity
30,000~60,000
2000~5000
Speed
30-50
10-15
punctuality
On time
Not sensitive to the external environment
Not on time
sensitive to the external environment
Background
1.1
Person/h
Km/h
Rail transit VS Road transportation
Importance of rail transit
Chapter 1 - Introduction
Notes: Is there any way to deal with this congestion problem?
The rail transit seems to be a good choice, since it has the features of large capacity, high speed, and punctuality. Because of these advantages, rail transit now is playing a more and more important role in the urban transportation system

## Slide 6
Chapter 1 - Introduction
Background
1.1
Problems in Fukuoka
Reduction in share rate of public transit
1
Traffic congestion
2
Chart: Traffic mode share rate of Fukuoka
| 1972 | 1983 | 1993 | 2005 | 2025
rail transit | 0.066 | 0.098 | 0.134 | 0.141 | 0.133
bus | 0.173 | 0.118 | 0.08 | 0.083 | 0.096
texi | 0.033 | 0.02 | 0.015 | 0.011 | 0.012
pravite car | 0.306 | 0.308 | 0.378 | 0.422 | 0.481
bycicle | 0.049 | 0.155 | 0.151 | 0.156 | 0.116
walk | 0.373 | 0.301 | 0.241 | 0.185 | 0.162
Notes: Let’s take a look at Fukuoka, there is also some problems in the urban transit system.
One is the reduction in the share rate of public transit. As we can see from this chart, the share rate of rail transit tends to decrease in the future, while the share rate of private car keeps on increasing. It’s not a good phenomena.

## Slide 7
Chapter 1 - Introduction
Background
1.1
Problems in Fukuoka
Chart: Average travel speed during crowded time in major cities
| Tokyo | Saitama | Osaka | Kawasaki | Nagoya | Sakaishi | Fukuoka | Yokohama | Kyoto | Sagamihara | Chiba | Sapporo | Kitakyushu | Kobe | Shizuoka | Hiroshima | Okayama | Sendai | Hamamatsu | Niigata
speed | 16.8 | 17.8 | 18.6 | 18.6 | 18.9 | 19.4 | 20.4 | 20.7 | 22.7 | 23.6 | 24.4 | 26.7 | 27.3 | 28.1 | 29 | 29.9 | 29.9 | 30.2 | 30.8 | 32.6
Reduction in share rate of public transit
1
Traffic congestion
2
Notes: Another problem is the traffic congestion that we are now facing every day. We can see from this chart the average travel speed during the crowed time in Fukuoka now is at a very low level.

## Slide 8
Research purpose
1.2
Exploring the factors influencing rail transit ridership from multiple perspectives and estimating the influence.
Main purpose
Specific issues in research
1
Walking is the most important travel modes in accessing transit stations, also one of the most key determinants on the utilization of rail transit.
2
Rail transit ridership is considered to be mainly affected by the factors surrounding the station.
3
The rail transit station is in a network. When the ridership is affected by the environmental factors around the station, it is also influenced by the environmental factors around the other stations in the same network.
Chapter 1 - Introduction
Notes: So is there anything we can do to help Fukuoka to promote the utilization of rail transit and to improve the traffic condition?
To increase the utilization of rail transit, obviously, knowing the influencing factors of transit ridership should come the first.
So, the main purpose could be, to explore the factors influencing rail transit ridership.
Around this topic, 3 specific questions will be answered in this research.
1. The first one is what influence the walking duration to transit stations? Since walking is the most important access to rail transit stations, the walking duration should be one of the most important determinants of transit ridership.
2. The second is what factors influence transit ridership at station level? As we know, the environment around a station can affect the ridership of this station, so our aim is to find and estimate the influencing factors.
3. Based on the second question, because stations are in the network, if the ridership of a stations varied, the ridership of other stations must vary as well. So, the third question will be what factors influence the transit ridership between station and station.

## Slide 9
Chapter 1 - Introduction
Summary
1.3
Exploring the determinants on the utilization of rail transit
Reduction in share rate of public transit
Promoting the use of public rail transit
Problems
Demand
Purpose
Subtopic
Walking duration to rail transit stations
Transit ridership at station level
Passenger flow between station and station
Traffic congestion
Notes: I will give a summary of the introduction.
Now Fukuoka is facing the problem of reduction in share rate of public transit, and traffic congestion. So, promoting the use of public rail transit seems to be a good choice for Fukuoka.
With this background and demand, the purpose of exploring the determinants on the utilization of rail transit is proposed.
Around this main purpose, the research contents are extended to 3 subtopics
walking duration to rail transit stations, Transit ridership at station level, passenger flow between station and station.

## Slide 10
Chapter 1 - Introduction
Organization
1.4
Chapter 1
Introduction of the dissertation including background, purpose, literature review.
Chapter 2
Walking duration
Exploring the factors influencing walking duration to transit stations from the perspective of passengers’ attributes.
Chapter 3
Characteristics analysis. Preliminary research for chapter 4, 5
Clarify the characteristics of transit ridership and land use
Chapter 6
Summarizing the findings achieved in each chapter, and giving the conclusion for this dissertation
Chapter 4
Transit ridership at station level
Exploring the factors influencing transit ridership at station level
Chapter 5
Transit ridership at station-to-station level
Exploring the factors influencing transit ridership at station-to-station level
Notes: This research is organized into 6 chapters. Chapter 2, 4, 5 correspond to the three subtopics, chapter 3 is a preliminary study for supporting chapter 4 and 5.

## Slide 11
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Chapter 2
Notes: Chapter 2, Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics.

## Slide 12
distance to destinations is widely thought to be an important predictor of active travel
Introduction
2.1
Background
Exploring the factors influencing walking duration to transit stations from the perspective of passengers’ attributes.
Main purpose
Walking is the most important travel modes in accessing transit stations.
Walking duration to transit station is widely accepted to be an important determinants on the utilization of rail transit.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Notes: Walking is the most important travel modes of accessing transit stations. The Walking duration to transit station is also widely thought to be an important determinants on the use of rail transit.
With this background, the purpose of this study can be proposed. That is to explore the factors influencing walking duration to transit stations from the perspective of passengers’ attributes.

## Slide 13
 | Study | Type 1 | Type 2 | Type 3 | This
Research object | Walking distance | ● |  | ● | 
 | Walking duration |  | ● |  | ●
Method | Statistical description | ● |  |  | 
 | Regression |  | ● | ● | 
 | Nonlinear fitting |  |  |  | ●
Predictable | No | ● | ● | ● | 
 | Yes |  |  |  | ●
Result |  | Survey result description | Some factors were found, but prediction and verification were not given | No relationship found | Having relationship with travel purpose, travel time period, age, and occupation
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Review
Notes: Before running the analysis, let’s take a look at how this study differs from the others.
The research object in this study is the walking duration to transit stations.
As to the methods, studies based on statistical description account for the majority, while some studies tried to use regression model to find the relationship between walking duration and personal attributes, but they didn’t get an expected result.
This study uses the nonlinear fitting method to find the relationship of walking duration and personal attributes, then try to make a prediction for the walking duration.

## Slide 14
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Most studies use qualitative methods. Few quantitative analysis obtained the significant result on estimating walking duration. The reason of that may be in the data processing, the model constructing, also model estimating.
Research contents
Using probability but not the linear relationship to describe the walking duration preference of passengers with different attributes.
1
  Function of walking duration
Problem 1
Key points
Problems in previous studies
Notes: Ok, now let’s have a look at the research contents.
According to the review of previous studies, some existing problems are summarized. This study will focus on some key points based on these problems.
The first problem is few quantitative analyses obtained a significant result, it means they didn’t find a proper function to describe the relationship between walking duration and personal attributes.
For this problem, two key points will be addressed in this study. one, construct a proper function to describe the relationship of walking duration and the indicators. two, identify the effective indicators that indeed have influences on the preference to walking duration.

## Slide 15
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Although many studies have summarized some factors affecting the walking duration through qualitative methods, none of them quantitatively verified the effect of the influencing factors.
Research contents
Key points
Problems in previous studies
To estimate the relationship between identified influencing factors and walking duration. Then evaluating the prediction to judge the effectiveness of identified influencing factors.
2
  Estimation and evaluation
Problem 2
Notes: Another problem is the effect of indicators cannot be quantified. It means the result cannot be used for prediction.
So the third key point in this study is to estimate the relationship between identified influencing factors and walking duration. Then use this obtained relationship to make a prediction.

## Slide 16
Introduction
2.1
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Walking duration preference
Probability of walking the given duration or more
Identify valid feature
Verify the extracted features
Conclusion
Construct the indicator system
Random forest decision tree
Prediction
evaluation
Variance analysis
Dependent variable
Exploratory variable
Data cleaning
Passenger attributes
Valid travel chain info
Result of individual
Result of group
Key point
1
Key point
2
Key point
3
Notes: This is the flowchart of this study. It is organized into 6 parts. They are constructing the indicator system, cleaning data, identifying valid features, verifying the valid features, and estimating walking duration preference. The conclusion comes the last.
The key points of this studies are marked with yellow block.

## Slide 17
Give an example, for one person who has the attributes:
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Realistic issue
Reflected in survey
Problem description
I walked 6 minutes to the station
0 min
6 min
8 min
4 min
OK
I can accept a walking duration less than 8 minutes
0 min
Notes: Next, I will give a simple example to explain how I deal with the walking duration.
Think about a people who has the attributes like this, we assume this passenger can accept a walking duration less than 8 minutes for accessing transit stations.
But if it is reflected in a questionnaire, the answer may be like “I walked 6 minutes to the station”. Obviously, it cannot represent how long he is willing to walk to the station. This 6 minutes is just the distance between his starting point and the station.
Here the deviation appeared. The next slide, I will continue to explain how to deal with this problem.

## Slide 18
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Problem description
Distance
Actual walking duration
Attributes
Personal socio-demographic characteristics
Other personal attributes
Trip chain info
Willingness of walking duration
Notes: Here is a relation map of distance, attributes, willingness, and actual walking duration.
The actual walking duration is the original data that we can obtain from the questionnaires. As shown in this relation map, the actual walking duration should be directly determined by the distance between the starting point and the station.
We assume that people with different attributes should have different willingness of walking duration, and this willingness can affect the final actual walking duration as well. But, the attributes should never affect the actual walking duration directly.
So, what I want to do is to build a bridge between the attributes and actual walking duration through the willingness.

## Slide 19
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Model construction
I walked 3 minutes
Uncertainly
if 6 minutes can be accepted
If investigating the 6-minute walking duration
I walked 10 minutes
Certainly
6 minutes can be accepted
Certain
More than
6 minutes
Less than
6 minutes
Proportion
Uncertain
Actual
walking duration
Willingness
With a giving actual walking duration
Notes: And this is the bridge. I’d like to raise another example to explain it.
We can take the 6-minute walking duration as the investigation object, if the respondent answered that “I walked 10 minutes to the station”, it not only means this passenger walked 10 minutes, but also tells us the 6-minute walking duration is certain to be accepted by this passenger. While if someone said “I walked 3 minutes”, it means the 6-minute walking duration is not clear to be accepted or not.
Well, we can get a relationship between the actual walking duration and the willingness.
And obviously, the willingness of walking duration can be expressed as the function of personal attributes.
Here the bridge between personal attributes and the actual walking duration can be established.

## Slide 20
Walk longer than the given threshold of walking duration
Explanatory variables
Attributes
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data
2.3
Indicators
Dependent variable
Probability
Trip chain info
Other personal attributes
Personal socio-demographic characteristics
Notes: Then I will give a brief introduction for the indicators used in this study.
The definition of the dependent variable is the key point to bridge the actual walking duration and the personal attributes. Just as I interpreted in the last slide, here the dependent variable is defined as the probability of walking longer than the given threshold of walking duration.
The explanatory variables are passengers’ attributes including socio-demographic characteristics, some other personal attributes, and the trip chain information.

## Slide 21
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data
2.3
Distribution of the transit stations
Data in this study
Study case: Fukuoka
Notes: The study case and data source.
This study uses the rail transit stations of Fukuoka, including 78 stations in total.
The main data source is the person trip survey, it mainly includes the information about trip chaining behavior and some socio-demographic attributes.

## Slide 22
Data
2.3
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
The age distribution of passengers
Distribution of walking duration
The passengers aged between 25-55 who are still at production age account for the majority
People tend to reply a looser answer when they are being asked some questions about details.
Peak values at 5, 10, 15 min
Distribution characteristics
Notes: A brief description for the data. The left part is the age distribution of passengers.
As we can see in this figure, the passengers aged between 25-55 who are still at production age account for the majority. The right part is the distribution of walking duration, we can clearly see 3 peak values in this figure, they are 5, 10, 15 minutes.
Here I want to have a try to give some explanations to it. It can be easily imagined that if people were asked some questions about details like how much did you spend, how long did you take, for such kinds of questions, people tend to reply a looser answer, some general numbers like 5, 10, or something. Maybe this is the reason that the peak values appeared at 5, 10, 15 minutes.
These peak values may be one of the reasons that the previous studies didn't get the expected result. But these peak values are considered not to lead deviation in this study. Because the walking duration that passengers answered in the questionnaires represents this walking duration has already been accepted by the passengers, even it is not accurate.

## Slide 23
Female
Age from 25 to 44
Peak hour
Purpose of work
Purpose of business
Purpose of entertainment
Purpose of going home
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Selection of valid features
2.4
The thresholds selected in this study is 5, 8, 13 minutes.
According to the distribution of walking duration in Fukuoka, the acceptable walking duration mainly range from 5 – 13 minutes.
In this study, the average walking duration is about 8 minutes.
Selection of thresholds
Identification of valid features (analysis of variance)
Age over 65
Peak hour
No occupation
purpose of work
purpose of business
purpose of entertainment
purpose of going home
5 minutes
8 minutes
13 minutes
Age from 45-64
Peak hour
purpose of work
purpose of entertainment
Notes: For the threshold of walking duration we are going to investigate, according to the distribution of walking duration in Fukuoka, the 5, 8, 13 minutes are selected as the threshold to be investigated.
Then I use the analysis of variance to extract the valid features at each threshold of walking duration. We can see that the features vary from different walking duration.

## Slide 24
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Prediction and evaluation
2.5
Decision tree and random forest
Reason for choosing decision tree
Reason for adding forest random
Used as an exploratory method for the dataset with unknown feature distribution
Reduce the possibility of over-fitting of data which is easily occurred in the decision tree model.
50% training set
50% testing set
Train the model
Get the rule
Verify the model
Input
Flow
Notes: Now we have got the valid features, the next step is to estimate the model to find the relationship between walking duration and the indicators.
With the consideration of the dataset and the research purpose, the random forest decision tree model is introduced to this study.
The procedure has two steps, training the model, and verifying the model. The dataset is split into the training set and testing set, for 50 percent respectively.

## Slide 25
Prediction and evaluation
2.6
Predictive power of group trends
Predictive power of individual
Object: Individual
Index: Kappa indicator
-1
1
Worse
Better
Range
Predictive power
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Object: Group of 200 individuals
Index: Coefficient of determination
0
1
Worse
Better
Range
Predictive power
……
Notes: The prediction is evaluated from two ways, for the individual and group.
The predictive power of individual is evaluated by the Kappa index. This index ranges from minus one to one, the higher value means a better predictive power.
The predictive power of group is evaluated by the coefficient of determination, it ranges from 0 to 1. Higher value represent a better predictive power.

## Slide 26
Prediction and evaluation
2.6
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Coefficient of determination
0.843
0.221
0.426
Kappa index
0.142
0.016
0.060
5 minutes
8 minutes
13 minutes
Predictive power of individual
Predictive power of group trends
Notes: Let’s take a look at the result.
We can see that the result of 5-minute walking duration is better than the other two walking duration. The prediction at 8 minutes is not well.
Here I give some speculation to the results. For the 5 minute threshold, because the 5 minutes walking duration can be easily accepted, some passengers who cannot accept this walking duration should have some significant characteristics. For this reason, the 5-minute walking duration has a higher predictive power. The same reason can be used to explain the result at 13-minute threshold.
For the 8 minute threshold, because the 8-minute walking duration is ambiguous in passenger’s behaviors, there is randomness in accepting whether to walk 8-minute. For this reason, the 8-minute walking duration is difficult to predict.

## Slide 27
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Findings
Walk less
Walk more
Peak hour
Commuting to work
Business purpose
Private purpose
Going home purpose
Older than 65
No occupation
5 minutes threshold
Individual: 0.142
Group trend: 0.843
Age between 25-44
Female
Peak hour
Commuting to work
Business purpose
Private purpose
Going home purpose
8 minutes threshold
Individual: 0.016
Group trend: 0.221
Age between 45-64
Peak hour
Commuting to work
Private purpose
13 minutes threshold
Individual: 0.060
Group trend: 0.426
Prediction
Notes: I will give a summary of the results.
In this table, the left column is the predictive power, the right part is the personal attributes identified at each threshold of walking duration. The column of walk more means passengers with these attributes tend to walk longer than the given walking duration, the attributes in the column of walk less means passengers tend to walk less than the given walking duration.
We can see from it, passengers with the private travel purpose tend to accept the longest walking duration. Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.

## Slide 28
The effect of influencing factors is predicted, the results are evaluated from the view of both individual and group.
Describe passengers' walking duration preferences using the probability of walking longer than a given threshold.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Summary
Problems
Little quantitative relationship between walking duration and passengers’ attributes was found.
Few of the existing studies quantitative verified the effect of influencing factors
1
2
Achievements
Notes: To the summary, the main achievements of this study:
1. This study described passengers' walking duration preferences using the probability of walking longer than a given threshold.
2. The effect of influencing factors is predicted, the results are evaluated from the view of both individual and group.

## Slide 29
Analysis on the Characteristics of Transit Ridership and Land Use
Chapter 3
Notes: This is the chapter 2. Next, chapter 3, Analysis on the Characteristics of Transit Ridership and Land Use

## Slide 30
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Research position
Purpose
To grasp the characteristics of transit stations in terms of both transit ridership and land use in Fukuoka.
Preliminary study
Characteristics
Relationship
Chapter 3
Land use
Ridership
Ridership Estimation
Chapter 4
Station-to-station
Chapter 5
Station level
Notes: This chapter is a preliminary study for estimating the influence of transit ridership, it mainly focus on the characteristics of transit ridership and land use, also give an exploration on the relationship between them.
The purposes of chapter 3 is to grasp the characteristics in terms of both transit ridership and land use.

## Slide 31
Summary the characteristics of rail transit ridership in spatial and temporal distribution
Introduction
3.1
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Problem 1
The characteristics of rail transit ridership and land use in Fukuoka needs to be clarified.
Key points
Problems
1
  Characteristics of transit ridership
Analyze the characteristics of land use around the subway in terms of the type of land use
2
  Characteristics of land use
Preliminary explore the relationship between rail transit ridership and land use
3
  Relationship between rail transit ridership and land use
Notes: To make a detailed understanding of the rail transit system in Fukuoka, this chapter mainly focused on three key points. 1. to summarize the characteristics of rail transit ridership. 2. To analyze the characteristics of land use around the subway stations. 3. To make a preliminary exploration on the relationship between rail transit ridership and land use.

## Slide 32
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
Study case
Fukuoka subway
35 subway stations
3 operating subway lines
29.8 km operating mileage
20% share of motorized travel
Data source
Notes: This is the overview of study case and data source.
The study case is Fukuoka subway.
The main data source in this study is the subway transit ridership, the statistics of population and land use.

## Slide 33
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership characteristics
Growth trend.
More than 600,000 passengers per day.
Significant difference in ridership among the three lines.
Trends of variation in transit ridership
Chart: Transit ridership of subway in Fukuoka
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
line 1 | 408641 | 420811 | 424076 | 427402 | 417222 | 426908 | 442126 | 454504 | 471578 | 491838
line 2 | 38887 | 39429 | 39145 | 40394 | 40015 | 41347 | 42583 | 43727 | 45848 | 47704
line 3 | 77007 | 88969 | 95886 | 100822 | 98519 | 102808 | 107775 | 110471 | 115163 | 120410
total | 524535 | 549209 | 559107 | 568618 | 555756 | 571063 | 592484 | 608702 | 632589 | 659952
Notes: This is the trends of variation in transit ridership.
The ridership keeps a growth trend. Currently, the Fukuoka subway system carries about 6 hundred thousands passengers per day.
And the three lines showed significant difference in ridership. The first line has a much larger transit ridership than the second line and the third line.

## Slide 34
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Line 3 had a much higher growth rate at the first few years of the opening
The growth rate of three lines tend to be stable after the year of 2009
Transit ridership characteristics
Annual growth rate of transit ridership
Chart: Annual change rate of transit ridership
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
line 1 | 0.029782 | 0.0077588 | 0.0078429 | -0.023818 | 0.023215 | 0.035647 | 0.027997 | 0.037566 | 0.042962
line 2 | 0.013938 | -0.0072028 | 0.031907 | -0.0093826 | 0.033288 | 0.029893 | 0.026865 | 0.048506 | 0.040482
line 3 | 0.15534 | 0.077746 | 0.051478 | -0.022842 | 0.043535 | 0.048313 | 0.025015 | 0.042473 | 0.045562
total | 0.04704 | 0.018022 | 0.017011 | -0.02262 | 0.027543 | 0.037511 | 0.027373 | 0.039243 | 0.043256
Notes: The annual growth rate of transit ridership.
We can see from the figure that the third line had a much higher growth rate at the first few years of the new opening.
The growth rate of three lines tend to be stable after the year of 2009.

## Slide 35
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership characteristics
Terminal
Terminal
Hub
Airport
Hub
Newly opened
Spatial distribution of transit ridership
Notes: This is the spatial distribution of transit ridership.
Fukuoka subway has two terminal stations, two hub stations, and one station serving for the airport.
We can see that, most stations located in the central area have larger transit ridership.

## Slide 36
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Transit ridership | Total | Line 1 | Line 2 | Line 3
Hub | 2 | 2 | 0 | 0
Large | 4 | 3 | 0 | 1
Medium | 11 | 8 | 1 | 2
Small | 18 | 0 | 4 | 4
Growth rate | Total | Line 1 | Line 2 | Line 3
0-2.5 | 12 | 8 | 4 | 0
2.5-4.5 | 11 | 5 | 2 | 4
4.5-6.0 | 6 | 0 | 0 | 6
6.0- | 6 | 0 | 0 | 6
Transit ridership characteristics
Small scale
High growth rate
Line 3
Small scale
Low growth rate
Line 2
Large scale
Low growth rate
Line 1
Classification based on transit ridership
Notes: Two cross tables about the transit ridership and the growth rate are given to help to understand the characteristics.
Both the first line and the second line have low growth rates, the first line has a larger transit ridership. For the third line, although the scale of transit ridership is still small, it keeps on a high growth rate.

## Slide 37
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
High correlation ( >0.7)
Correlation analysis for indicators
Notes: Next, the land use characteristics.
Because there are so many types of land use, we need to master the relationship among all the kinds of land use at first.
This table is the result of correlation analysis, the cells marked with grey color means there is a strong linear correlation between the two indicators.

## Slide 38
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
Component Matrix
Factor extraction
Factor 1: Ofﬁce & commerce
Office
Hotel
Commerce
Entertainment
Dwelling with shop
Culture
Factor 2: Residence
Apartment house
Residence
Culture
Factor 3: Education
Education
Government
Notes: To deal with this linear correlation, the factor analysis is conducted to make a in-depth exploration on the internal relationship.
As a result, three factors are extracted, they are office & commerce, Residence, and education.

## Slide 39
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.4
Land use characteristics
Station classification based on land use
99
Chart: 
| Low-density residence | High-density residence | Education | Downtown commerce | Office
Office | 0.028504 | 0.05432 | 0.060316 | 0.38084 | 0.27482
Commerce | 0.0799 | 0.040303 | 0.050842 | 0.25757 | 0.14201
Residence | 0.69225 | 0.59665 | 0.40217 | 0.13678 | 0.27095
Education | 0.044717 | 0.074697 | 0.20709 | 0.012363 | 0.030956
Other | 0.15463 | 0.23403 | 0.27958 | 0.21244 | 0.28127
114
74
62
151
Population Density
Person/Ha
Notes: According to the analysis of land use indicators, all the 35 stations are classified into 5 types.
They are office type, downtown commerce type, education type, high-density residence type, and low-density residence type.
This is the summary for each type of stations.

## Slide 40
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
General relationship
Large differences in different types
Low density = Low ridership
Commercial center = High ridership
Transit ridership
Land use
Characteristics
Notes: Combining with the cross table of land use and transit ridership, we can get some informations.
They are, different land use characteristics have different scales in transit ridership.
The density of both population and land use have significant influence on transit ridership.
Commercial land use produces more ridership than other land use types

## Slide 41
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
Statistical relationship - quantiﬁcation method I
Transit ridership per day
Dependent variable
Population density
Commerce & office
Residence
Education
Explanatory variables
0.513
Coefficient of determination
Commerce area
Office area
Key factors
Part 1
Notes: After a general understanding of the relationship between ridership and land use, the quantification method one is used to make a deeper exploration.
In the first part of quantification method one, the dependent variable is transit ridership per day.
Among the indicators, commercial and office area have the greatest impact on transit ridership.
But the estimation did not show a good fitness.

## Slide 42
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Exploration the influence on transit ridership
3.4
Statistical relationship - quantiﬁcation method I
Part 2
Growth rate of transit ridership
Dependent variable
Population density
Commerce & office
Residence
Government
Education
Explanatory variables
0.537
Coefficient of determination
Population density
Key factors
Notes: In part 2, the same indicators are used for estimating the growth rate of transit ridership.
The same with part 1, the result did not show a good fitness as well.

## Slide 43
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Conclusion
3.5
Through the summary and analysis, we got a comprehensive understanding of rail transit utilization and land use status in the case of Fukuoka City.
Provided foundation and references for the further exploration on the determinants on transit ridership
Pedestrian area should be considered.
Explanatory variables should be enriched.
Model should be improved.
The approach of dealing with small sample case should be considered.
Summary
Implications
Notes: This is the contents of chapter 3.
Through this study, we got a comprehensive understanding of transit ridership and land use status in the case of Fukuoka City.
This study also provided the foundation and references for the next exploration of the determinants on transit ridership
Some implications can be got from this chapter.
1. Pedestrian area should be considered in depicting the catchment area.
2. Explanatory variables should be enriched.
3. The Model should be improved.
4. The approach of dealing with small sample case should be considered.

## Slide 44
Influencing Factors on Transit Ridership at Station Level
Chapter 4
Notes: On the base of chapter 3, chapter 4 aims to make a deeper exploration on factors influencing subway ridership at station level.

## Slide 45
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Background
Rail transit ridership is considered to be mainly affected by the environmental factors surrounding the station.
The influencing factors are different in cities with different urban form and travel preference. Few studies focus on such a city like Fukuoka with only tens rail transit stations.
Explore and explain the factors influencing subway ridership at station level using a small sample case
Main purpose
Notes: As we know, rail transit ridership is considered to be mainly affected by the environmental factors around the station.
The influencing factors are different in cities with different urban form and travel preference. There is a problem in the existing studies that few studies focus on such a city like Fukuoka with only tens stations.
This chapter aims to answer the question that what factors explain transit ridership at station level in a small sample case?

## Slide 46
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Study type |  | Type 1 | Type 2 | Type 3 | This
Sample size | Tens |  |  |  | ●
 | Hundreds | ● | ● | ● | 
Method | Linear regression | ● | ● | ● | 
 | Spatial regression |  |  |  | ●
Catchment area | Circle buffer | ● | ● |  | 
 | Walking distance |  |  | ● | ●
Indicators | Land use |  | ● | ● | ●
 | Transit-relation | ● | ● | ● | ●
 | Demographic-relation | ● |  |  | ●
Review
Notes: At first, let’s take a look at how this study differs from the others. The biggest difference in this study is the sample size. Few studies deal with a case just having tens of the samples. Because this kind of studies is commonly based on statistics, a sufficient sample size is necessary.
Moreover, with the consideration of the spatial distribution of stations, the spatial regression will be introduced to this study. Also, to define the catchment area more accurately, the walking distance along the real road network is used to determine the catchment area.

## Slide 47
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Research contents
Problem 1
Problem 2
Few studies work on the selection of valid indicators using small sample case.
The consideration of spatial correlation among the explanatory variables is inadequate.
Problem 3
Index system need to be enriched
1
  Improve index system
Propose and reconstruct indicators to improve the index system
Identify valid indicators
2
Propose effective index screening method for small samples
Improve accuracy in estimation
3
Consider the different spatial distribution of indicators in the spatial regression model by identifying global/local variables.
Key points
Problems in previous studies
Notes: According to the review, this study will focus on three points to deal with the problems existing in the previous studies.
1. Reconstruct indicators to improve the index system.
2. Select the effective indicators for explaining transit ridership in a small sample case.
3. Identify the global/local indicators in the estimation of the spatial regression.

## Slide 48
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Determine the catchment area
Construct the indicator system
Select valid indicators on explaining ridership
MGWR
Determine local/global variables in MGWR
Estimate MGWR
Residual analysis
Conclusion
Extract indicator from the catchment area
Select valid indicators
Select optimal combination of valid indicators
Explanatory variables
Dependent variable
800m pedestrian area
Key point
1
Key point
2
Key point
3
Notes: This is the organization of this study.
It is constructed by 5 parts, constructing the indicator system, determining the catchment area, selecting the valid indicators, estimating the model, and drawing the conclusion.
The parts marked with yellow blocks are the key points in this study.

## Slide 49
Indicators
4.2
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Expected sign | Min Value | Max Value | Average | Unit
Built environment | Commerce | + | 2,921 | 811,281 | 114,353 | m2
 | Office | + | 2,614 | 839,956 | 167,088 | m2
 | Residence | + | 110,748 | 1,067,523 | 528,533 | m2
 | Education | + | 294 | 305,559 | 59,691 | m2
 | Government | + | - | 128,471 | 20,878 | m2
 | Transportation Facility Area | + | 197 | 132,777 | 21,204 | m2
 | Land use Aggregation | + | 0.09 | 0.75 | 0.31 | -
Transportation Accessibility | Transfer Dummy | + | 1 | 4 | 1.34 | -
 | Bicycle Parking | Unknown | 64 | 4,375 | 778 | -
 | Bus Capacity | Unknown | 3 | 260 | 58.48 | -
 | Bus Accessibility | Unknown | 4 | 455 | 89.71 | -
 | Road Density | - | 191 | 479 | 299 | m/ha2
Demographic and Socioeconomic Environment | Population | + | 1,908 | 19,393 | 9,813 | -
 | House Member | - | 1.86 | 2.79 | 2.18 | -
 | Population/Job Balance | Unknown | 1.27 | 2.61 | 1.80 | -
 | Tenant Proportion | - | 0.15 | 0.65 | 0.43 | %
Dependent variable: average daily subway ridership
Variable summary
Notes: The introduction of the indicator system.
In this study, the dependent variable is the average daily transit ridership.
The candidate independent variables are summarized into 3 categories: 1. built environment; 2. transportation accessibility; 3. demographic and socioeconomic environment.
In the column of expected sign, plus sign means the increase in this indicator is expected to cause an increase in transit ridership, while the minus sign is expected to have an opposite effect.

## Slide 50
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Land-use Aggregation
0
1
Range
Higher variety
Much daily activity can be finished within the catchment area
Lower variety
Have to go further places to complete some daily activities
Reduce
travel demand
Raise
travel demand
Speculation of impact
Notes: Then I will introduce some of the indicators in details.
First one is the indicator of land-use aggregation.
This indicator is used to describe the variety of land use.
The land use aggregation ranges from 0 to 1. A higher variety of land use infers much daily activity can be finished within the catchment area, it is supposed to lead a reduction in transit ridership. On the contrary, a lower variety of land use is thought to increase the transit ridership

## Slide 51
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Bus capacity
Share passengers from rail transit. Negative effect on rail transit ridership
Bus Accessibility
Bring passengers to rail transit. Positive effect on rail transit ridership
Indicators of bus system
Bus system has both positive and negative effect on rail transit ridership
Speculation of impact
Share ridership from rail transit
Bring ridership to rail transit
VS
Notes: Another one is about the bus system.
In this study, the indicator of bus system is considered from two aspects.
As shown in the figure, bus is supposed to have double effects on the rail transit, one is sharing passengers from rail transit, another one is bringing passengers to rail transit.
The indicator of bus capacity represent the ability of sharing passengers from rail transit, it is supposed to have negative effect on rail transit ridership.
The indicator of bus accessibility represent the ability of bringing passengers to rail transit, it is supposed to have positive effect on the rail transit ridership.

## Slide 52
Catchment area
4.3
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Catchment area: walking distance accessing the subway station. (Pedestrian Catchment Area, PCA)
Pedestrian area range: 400m ~ 1000m
Most adopted: 800m
Walking speed: about 4.8km/h
Average walking distance: about 600m
85% of passengers walk to stations
Use 800m pedestrian area as the catchment area of rail transit.
In general
Walking distance
In the case of Fukuoka
Notes: As to the catchment area, this study uses the 800 meters pedestrian area.
Summarized from the previous studies, the catchment area ranges from 400 meters to 1 kilometer in general, and the most accepted pedestrian area is 800 meters.
Back to our study case Fukuoka, according to the subway survey report, the average walking distance in Fukuoka will be about 600 meters.
We can think that 800 meters covers most of the passengers in Fukuoka.
Based on the above, it can be viewed that 800 meters pedestrian area is reasonable in this study.

## Slide 53
Catchment area
4.3
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Separated along the river
The walking distances along the real road network are equal from any point on the boundary line to both the station on both sides.
Notes: The catchment area is depicted as shown in this figure.
Any point on the boundary between two stations has the equivalent distance to both the stations.
Here, there is a river between the two stations that the river separated the road network. In this case, the two catchment areas are split along this river.

## Slide 54
Identification of valid factors
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Flowchart of screening valid factors with small sample
Candidate indicators
Valid indicators
Optimal combination
16
10
9
Multicollinearity
Validity
Stability
Judgement
Number of
indicators
Flow
Model estimation
Test indicators for linear regression
Notes: This part is identifying the valid factors in the small sample case.
This is the flowchart of screening valid factors. The procedure has two steps.
The first step is to identify the valid variables, using the judgement of multicollinearity, validity, and stability.
In the second step, the linear regression is conducted to select an optimal combination of valid explanatory variables.

## Slide 55
Pattern | Type
Random | Global
Clustered | Local
Random | Global
Random | Global
Random | Global
Clustered | Local
Clustered | Local
Clustered | Local
Clustered | Local
Model estimation
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Moran's Index | P-value*
Government Area | 0.04 | 0.51
Transportation Facility | 0.29 | 0.00
Land use Aggregation | -0.01 | 0.84
Transfer Dummy | 0.13 | 0.12
Bicycle Parking | -0.12 | 0.36
Bus Capacity | 0.70 | 0.00
Bus Accessibility | 0.45 | 0.00
Population/Job Balance | 0.77 | 0.00
Tenant Proportion | 0.24 | 0.01
Identification for global/local variable
P > 0.05
P ≤ 0.05
Pattern: Random
Type: Global
Pattern: Clustered
Type: Local
Notes: Now we have got the valid explanatory variables.
Before estimating the model, we should determine whether the indicator is a local or global indicator.
This procedure is conducted by using Moran’s index to examine if the variable is spatial autocorrelation or not.
As the result, the indicators of clustered pattern are selected as the local variable, while the random pattern are judged as the global variable.

## Slide 56
Model estimation
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Unit | Type |  | MGWR model | 
 |  |  |  | B | t
Government Area | m2 | Global |  | 0.05 | 2.59
Land Use Aggregation | coef (0-1) | Global |  | 13,384.34 | 2.48
Transfer Dummy | dummy | Global |  | 5,968.65 | 4.98
Bicycle Parking | count | Global |  | 7.72 | 8.59
Transport Area | m2 | Local |  | 0.10 | -
Bus Capacity | coef | Local |  | -55.14 | -
Bus Accessibility | coef | Local |  | 48.61 | -
Population/Job Balance | coef | Local |  | -2,411.17 | -
Tenant Proportion | % | Local |  | -10,304.66 | -
Estimation of Mix Geographically Weighted Regression
Notes: This is the result of estimation.
As a result, the indicators of building area have a positive effect on the transit ridership.
The indicator of land-use aggregation shows land use variety can lead to decrease in transit ridership.
As the expectation, the indicator of bus capacity has a negative effect on the subway ridership, and the bus accessibility has a positive effect.
The factor of resident/job balance and tenant proportion shows that working people and tenants are more willing to use subway.

## Slide 57
Reorganized the indicator system. Proposed the indicators of land use variety, bus capacity and bus accessibility.
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Summary
Identified global/local indicator in MGWR using the spatial autocorrelation of indicators.
Problems
Indicator system need to be enriched
1
Selection of effective indicators under small sample
2
Achievements
Insufficient consideration of spatial relevance of indicators
3
To reduce the first and second type of statistical error in small sample case, use exploratory regression to screen effective indicators and the most metric combinations.
Summary
Notes: The main achievements of this study can be summarized as following
This study reorganized the indicator system.
To reduce the first and second type of statistical error in small samples case, this study used exploratory regression to screen the effective indicators.
Identified global/local indicator in Mix Geographically Weighted Regression.

## Slide 58
Impact of Land Use Types on Transit Ridership between Stations and Stations
Chapter 5
Notes: Chapter 5, Impact of Land Use Types on Transit Ridership between Stations and Stations

## Slide 59
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
Background
Main purpose
Explore the impact of land use on the choice of destination station.
The rail transit station is in a network. When the ridership is affected by the environmental factors around the station, it is also influenced by the environmental factors around the other stations in the same network.
Land use determines travel purpose in some extent. The variation in the land use of departure station can affect the choice of travel destination.
Notes: We know that the rail transit stations are in a network. The transit ridership is not only affected by the elements around the station, but also be affected by the other stations in the same network.
On the other hand, because land use is one of the most important determinants on travel purpose. The variation in the land use of departure station is considered to have influence on the choice of travel destination.
Therefore, the main purpose of this study is to explore the impact of land use on the choice of destination.

## Slide 60
Downtown area
Office gathering area
The increased ridership will be transferred to the other stations
Question: How the land use type of a station influence the choice of destination?
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
Background
Notes: I’d like to give a brief introduction for what I want to do in this study.
As shown in this slide, if the transit ridership increased in this station, the increased part will be transferred to the other stations in the network, Due to different travel purpose, this part of increased passengers will choose different stations as the destinations.

## Slide 61
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
 | Type 1 | Type 2 | This
Scale | Station-level | Station-to-station level | Station-to-station level
Research object | Transit ridership of a single station | Transit ridership between station and station | Probability of choosing the a specific station as the destination
Functional relationship | Linear relationship | Linear relationship | Probability relationship (Binary choice)
Review
Differences with station-level
Notes: Then I will give a brief review to make clear the differences from previous studies.
For the research object, differ from station-level, the research object is not the passenger volume of a single station but the passenger flow between station and station.
Although some studies have paid attention to the station-to-station level, they just simply changed the research object to the passenger flow between station and station, but the functional relationship they examined is still the linear relationship.
This study uses the probability of choosing a specific station as the destination to describe the passenger flow between station and station.

## Slide 62
How to describe and define the passenger flow between station and station?
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Research contents
Problem 1
Describe the passenger flow between station and station using the probability of choosing a specific station as the destination.
1
Key points
Problems in previous studies
How to establish the functional relationship between the passenger flow and land use?
Problem 2
  Convert the problem of passenger flow to a binary choice problem, then estimate the influence of land use on the choice of destination.
2
Notes: According to the review, this study will focus on 2 points to deal with the problems existing in the previous studies.
For the problem of how to describe and define the passenger flow between station and station? This studies describes it using the probability of choosing a specific station as the destination
For the second problem of how to establish the functional relationship between the passenger flow and land use? This study converts this issue to a binary choice problem, then use logistic regression to estimate the influence of land use on the choice of destination.

## Slide 63
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Flowchart
Indicator system
Model construction
Convert into a binary choice problem
Model estimation
Conclusion
Research object
Land use
Independent variable
impedance
Dependent variable
Probability of getting off at a specific destination station
Logistic regression
Key point
1
Key point
2
Notes: This is the general flow of this study. It contains 5 main parts. Defining the research object. Establishing the indicator system. Building the model, then estimating the model. Finally drawing the conclusion. The key points of this study is marked with yellow blocks.

## Slide 64
Research object
5.2
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Dependent variable
Probability of choosing the destination
If Investigating the relationship between station a and station k
a
Boarding
Station
Passenger Volume
Passenger Volume
k
b
c
d
e
……
Station k
Other
Stations
Destination
Station
Expression
Notes: This is the definition of the dependent variable. It is defined as the probability of choosing a specific destination station. I will use a simple example to explain it.
If investigating the relationship between station a and station k, the passenger flow between station a and station k can be described as the following formula. The probability of choosing station k as the destination can be expressed as pak. This study supposes this probability should relate to the land use of both departure station a and destination station k.

## Slide 65
Indicator system
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Operation distance of subway
Bus capacity
Bus accessibility
Residence proportion
Office proportion
Land-use aggregation
Commerce proportion
Education proportion
Explanatory variables
Land use
Impedance
Notes: After defining the dependent variable, let’s take a look at the explanatory variables. The indicator system is constructed by two categories, the land-use, and impedance.

## Slide 66
Method
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Mathematical problems
Passenger flow
Binary choice model
Logistic regression model
Explanatory variable for making the choice of whether getting off
Probability of getting off at the specific station
Notes: Now we have prepared the dependent and explanatory variables, we need a model to establish the functional relationship between them.
Because the dependent variable is the probability of getting off at a specific station, this issue can be viewed as a binary choice problem. This is the abstract function, it can be estimated using logistic regression model.

## Slide 67
Method
5.4
Selection of sample station
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Chart: Land use proportion of each sample station
| 賀茂 | 藤崎 | 箱崎九大前 | 呉服町 | 天神
Commerce | 0.04 | 0.05 | 0.05 | 0.08 | 0.34
Office | 0.03 | 0.07 | 0.06 | 0.31 | 0.32
Residence | 0.83 | 0.76 | 0.51 | 0.49 | 0.24
Education | 0.04 | 0.06 | 0.22 | 0.03 | 0.01
Other | 0.06 | 0.06 | 0.16 | 0.09 | 0.09
Downtown
Office
Education
High-density residence
Low-density residence
Land use type
98
173
83
135
69
Population density
Person/ha
Notes: Because what we want to know is how land use affect the choice of destination, here I select some typical stations as the destination to estimate this influence.
According to the classification in the chapter 3, we select 5 stations from 5 types respectively.
They are Tenjin station of downtown type, Gofukumachi station of office type, Hakozakikyudaimae station of education type, Fujisaki station of high-density residence type, Kamo station of low-density residence type.
We can see the five stations have significant features in land use composition.

## Slide 68
Estimation
5.5
Chart: Low-density residence
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Low-density residence 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 | 1.07 | 1.01 | 1
Chart: High-density residence
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
High-density residence 藤崎 | 1.01 | 0.99 | 1.01 | 0.98 | 0.95 | 1 | 1
Chart: Education
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Education 箱崎九大前 | 1.02 | 1.02 | 1.03 | 0.99 | 0.88 | 1 | 1
Commerce land use
Office land use
Residence land use
Education land use
Land use aggregation
Distance
Bus capacity
Bus accessibility
Factors of the departure stations
Chart: Office
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Office 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 | 1 | 1
Chart: Downtown
| Commerce | Office | Residence | Education | Land use aggregation | Distance | Bus capacity | Bus accessibility
Commerce 天神 | 1 | 0.99 | 1.01 | 1.03 | 1.02 | 1.06 | 1
Commerce land use
Office land use
Residence land use
Education land use
Land use aggregation
Distance
Bus capacity
Bus accessibility
Factors of the departure stations
Increase in probability
Decrease in probability
Odd ratio
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
賀茂
藤崎
箱崎九大前
呉服町
天神
Probability of choosing the station as the destination
Notes: Now let’s check how the land use of departure station can influence the probability of choosing these 5 stations as the destination.
The solid square means the corresponding indicator of the departure stations can lead an increase in the probability of choosing this target station as the destination, while the hollow square represents a decrease in this probability.

## Slide 69
Conclusion
5.6
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Findings
Passengers are not inclined to choose a destination station which has a similar land use type with that of the departure station.
A station belongs to low-density residence type has a low probability being chosen as the destination no matter how the land use of departure station varies.
For any type of stations, the increase in the education land use of the departure station can lead to an increase in the probability of choosing the target station as the destination.
Notes: According to the result of estimation, we got some findings. They can be summarized as following:
1. Passengers are not inclined to choose a destination which has a similar land use type with that of the departure station.
2. A station belongs to low-density residence type has a low probability being chosen as the destination no matter how the land use of departure station varies.
3. For any type of stations, the increase in the education land use of the departure station can lead to an increase in the probability of choosing the target station as the destination.

## Slide 70
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Summary
Described the passenger flow using the probability of choosing a specific destination station.
Problems
Description for the process of passenger flow needs to be clear.
1
The model should be able to reflect the influence extent of the indicators.
2
Achievements
The problem is converted into a binary choice question. Logistic regression is used to estimate the influence of land use on the choice of destination
Notes: The summary for the main achievements.
First one, this study described the passenger flow using the probability of choosing a specific destination.
Secondly, converted this issue into a binary choice question, then estimated the influence of land use on the choice of destination using logistic regression model.

## Slide 71
Conclusion
Chapter 6
Notes: This is the contents of chapter 5. Finally, chapter 6, the conclusion.

## Slide 72
Chapter 1 - Introduction
Conclusion
6.0
Exploring the determinants on the utilization of rail transit
Reduction in share rate of public transit
Promoting the use of public rail transit
Problems
Demand
Purpose
Subtopic
Walking duration to rail transit stations
Ridership of a single station
Ridership flow between station and station
Traffic congestion
Review of the subtopics
Notes: Centering the main purpose of exploring the determinants on the utilization of rail transit, this research focused on 3 subtopics, walking duration to rail transit stations, transit ridership of single station, passenger flow between station and station.

## Slide 73
Conclusion
6.0
Chapter 6 - Conclusion
Walking duration to transit stations
Described passengers' walking duration preferences by examining the probability of certainly accepting a given threshold of walking duration to transit stations.
The effect of influencing factors is predicted, the results are evaluated from the view of both individual and group.
Notes: In the topic of walking duration to transit stations,
This research described passengers' walking duration preferences by examining the probability of certainly accepting a given threshold of walking duration to transit stations;
Then the preference of walking duration was predicted, and the results are evaluated in both individual and group.

## Slide 74
Conclusion
6.0
Chapter 6 - Conclusion
Reorganized the indicator system. Proposed the indicators of land use variety, bus capacity and bus accessibility.
To reduce first and second type of statistical error in small samples, use exploratory regression to screen effective indicators.
Identified global/local indicator in MGWR using the spatial autocorrelation of indicators.
Influencing factors of transit ridership (station level)
Notes: In the topic of Influencing factors of transit ridership at station level,
Firstly, this study redefined the indicators of land use variety and the indicators of bus system.
Secondly, To reduce first and second type of statistical error in small samples, use exploratory regression to screen effective indicators.
Thirdly, proposed an approach to identify the global/local indicator in the Mix Geographically Weighted Regression.

## Slide 75
Conclusion
6.0
Chapter 6 - Conclusion
Described the passenger flow using the probability of choosing a specific destination station.
The problem is converted into a binary choice question. Logistic regression is used to estimate the influence of land use on the choice of destination station.
Influencing factors of transit ridership (station-to-station level)
Notes: In the topic of Influencing factors of transit ridership at station-to-station level,
this research described the passenger flow using the probability of choosing a specific destination station.
Then constructed a binary choice model to describe the passenger flow between station and station, and estimated the influence of land use on the choice of destination station.

## Slide 76
Thanks
Notes: That’s all for my presentation, thanks for paying attention.

## Slide 77
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Data
3.2
1. Matching the region of data.
2. Matching the time points of data.
3. Extracting the data within the catchment area.
Data extraction
Notes: This is the procedure of data extraction.
1. Matching the region of data.
2. Matching the time points of data.
3. Extracting the data within the catchment area.

## Slide 78
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
800m-radius region
Extracting data
ArcGIS
Business
Commerce
Hotel
Entertainment
Residence
Apartment house
Dwelling with shop
Government
Education
Culture
Main land use
Data extraction
Notes: Then I will give an analysis on the land use characteristics.
The data of land use is extracted using an 800 meters radius region around the stations. The land use mainly includes the following types.

## Slide 79
Data
2.3
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Data Source: Person Trip Survey
Data processing
Notes: This is the data processing. The original data covers all the main cities in Kitakyushu area with more than four hundred thousands records.
I set the filter with city area of Fukuoka, rail transit trip chain, without null records, the remaining valid dataset has 4000 records.

## Slide 80
Assuming the distribution of walking duration of the passengers with the same attributions subject to the normal distribution.
If the survey result obtained from the questionnaire showed one group of passengers with specific attributes tend to walk longer, it means this group of passengers can accept a longer walking duration.
In this graph it can be considered that Group 1 can accept a longer walking duration than Group 2.
6 min
If considering the threshold of 6 minutes
Group 1
Group 2
All Samples
minute
Probability
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Methods
2.2
Important assumption
Notes: Then I’m going to explain the methods.
Firstly, An important assumption is necessary in this research.
Think about an example, as shown in this figure, we assume two groups of passengers, the passengers in each group have the same characteristics in personal characteristics, but group 1 is different from group 2.
The passengers in the two groups may have different preference of walking duration.
Now we give the assumption that the distribution of walking duration with the same personal attributes should subject to the normal distribution.
If the survey result obtained from the questionnaire showed group 1 tend to walk longer, it means this group of passengers can accept a longer walking duration.
As expressed in this figure, if investigating the threshold of 6 minutes, Group 1 can accept a longer walking duration than Group 2.

## Slide 81
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Evaluation of features
2.5
Individual Value |  | Group Trend | 
Actual | Prediction | Actual | Prediction
1 | 1.000 | 0.654 | 0.637
1 | 0.897 | 0.653 | 0.636
1 | 0.897 | 0.651 | 0.635
… | … | … | …
0 | 0.621 | 0.581 | 0.580
1 | 0.621 | 0.581 | 0.579
1 | 0.621 | 0.580 | 0.579
… | … | … | …
0 | 0.498 | 0.435 | 0.411
1 | 0.496 | 0.437 | 0.411
1 | 0.496 | 0.434 | 0.410
… | … | … | …
The predicted result is probabilities of accepting the giving threshold of walking duration.
The accuracy of results are evaluated by using the method of simple moving average.
Simple moving average
Prediction
200 records
Average
Notes: The result of decision tree is as shown in the figure. Here I just give a summary of the result to show.
As shown in the table on the right part, column of actual is the actual choice of individual, the prediction column is the value obtained from the estimation of decision tree.
The results are evaluated by using the method of simple moving average.
Sort the result by probability in descending order, the group trend is expressed by the average value of 200 samples.
So the trends between practice and prediction can be compared.

## Slide 82
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Estimation of Features
2.5
Forest random model is constructed by random selection of features and samples based on decision tree model.
The result is obtained by the average value of multiple decision trees.
Decision tree and forest random
Notes: Now we have got the valid features, the next step is to estimate the model to obtain the influence of the features on the acceptable walking duration.
I used the forest random decision tree model in this study.
Forest random model is constructed by random selection of features and samples based on decision tree model.
The result is obtained by the average value of multiple decision trees.

## Slide 83
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Conclusion
2.7
Recommendations
Encourage office buildings to move close to stations
Results from the factors of business purpose and going home purpose. Office staff tend to access rail transit station in a shorter time.
The individual prediction is still not accurate enough for predicting individual behavior. But the group prediction can be used for mastering the overall trend of rail transit utilization in a block.
Results from the evaluation of prediction
Notes: With the goal of increasing rail transit ridership, some recommendations are proposed based on the result. First, it is recommended to encouraging office building to move close to stations, because office staff tends to access rail transit station in a shorter time. Second, even the individual prediction is still not accurate enough for predicting individual behavior, the prediction of group trends can be used for mastering the overall trend of rail transit utilization in a block level.

## Slide 84
Land use
Facilities
Social-economic
……
Impact on the transit ridership
Catchment area
Influencing factors
Extraction
Introduction
4.1
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Notes: The transit ridership is affected by the elements around the station. To estimate the influences on transit ridership, at first we have to define this “around”, that is the catchment area. With a certain catchment area, the influencing factors can be extracted, and then use these factors to estimate the influence.
The problem in this procedure is how to define the catchment. I will show another slide to explain how can use the walking duration to determine the catchment area.

## Slide 85
Identification of valid factors
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Category | Variable | Statistical Information |  |  |  |  | 
 |  | VIF | Validity | stability | times | + | -
 | Total |  |  |  | 367 | 253 | 114
Built environment | Commerce Area | 8.8 | 32.1% | 100.0% | 25 | 25 | 0
 | Office Area | 10.4 | 9.0% | 71.4% | 7 | 5 | 2
 | Residence Area | 27.5 | 12.8% | 70.0% | 10 | 7 | 3
 | Education Area | 1.8 | 7.7% | 100.0% | 6 | 6 | 0
 | Government Area | 1.8 | 42.3% | 100.0% | 33 | 33 | 0
 | Transportation Facility | 3.0 | 67.9% | 100.0% | 53 | 53 | 0
 | Land use Aggregation | 2.5 | 50.0% | 100.0% | 39 | 39 | 0
Transportation Accessibility | Transfer Dummy | 3.0 | 34.6% | 100.0% | 27 | 27 | 0
 | Bicycle Parking | 4.5 | 44.9% | 100.0% | 35 | 35 | 0
 | Bus Capacity | 6.6 | 37.2% | 96.6% | 29 | 1 | 28
 | Bus Accessibility | 6.8 | 19.2% | 100.0% | 15 | 15 | 0
 | Road Density | 2.3 | 1.3% | 100.0% | 1 | 1 | 0
Demographic Socioeconomic Environment | Population | 23.9 | 12.8% | 60.0% | 10 | 6 | 4
 | Household Members | 3.0 | 39.7% | 100.0% | 31 | 0 | 31
 | Population/Job Balance | 3.0 | 37.2% | 100.0% | 29 | 0 | 29
 | Tenant Proportion | 2.2 | 21.8% | 100.0% | 17 | 0 | 17
The cell marked with dark color means that it doesn’t meet the judgment.
Valid factors
Suggested value
VIF< 7.5; Validity > 10%; Stability >90%
Valid Variable
Notes: This procedure is conducted by the exploratory regression.
The exploratory regression is to attempt all the combinations of explanatory variables by running the ordinary regression.
In this study, the exploratory regression ran 367 times in total, each variable entered in the models 78 times.
The validity is the proportion of showing statistical significance in all the models.
The stability means the proportion of showing positive or negative effects on the transit ridership.
The variables which have the VIF value less than 7.5, validity more than 10%, stability more than 90% are judged as the valid variable.

## Slide 86
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Identification of effective factors
4.4
Independent variables | Test model |  | 
 | Beta | Sig | VIF
Government Area | 0.10 | 0.02 | 1.36
Transportation Facility Area | 0.20 | 0.00 | 2.31
Land use Aggregation | 0.10 | 0.03 | 1.42
Bicycle Parking | 0.46 | 0.00 | 2.60
Bus Capacity | -0.20 | 0.01 | 3.56
Bus Accessibility | 0.26 | 0.00 | 4.71
Transfer Dummy | 0.26 | 0.00 | 2.79
Population/Job Balance | -0.10 | 0.05 | 1.94
Tenant Proportion | -0.09 | 0.03 | 1.32
Household Members | - | - | -
Residual sum of squares | 337744990 |  | 
Adjusted R2 | 0.96 |  | 
AICc | 694.39 |  | 
Jarque-Bera test (Sig) | 0.61 |  | 
Koenker (BP) test (Sig) | 0.85 |  | 
SA test (Sig) | 0.27 |  | 
No biased standard errors due to heteroscedasticity
Optimal combination of factors
Not deviating from a normal theoretical distribution
Not spatial autocorrelated
Notes: In the second step, the linear regression is conducted again to select an optimal combination of valid explanatory variables.
The judgement is the statistical test for regression.
As shown in this table, there are 9 valid variables entering the model at last.

## Slide 87
Government Area
Transport Area
Land Use Aggregation
Transfer Dummy
Bicycle Parking
Bus Accessibility
Bus Capacity
Population/Job Balance
Tenant Proportion
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Findings
Factors increasing ridership
Factors decreasing ridership
Notes: The main findings of this study can be summarized as following.
High diversity of land use can lead to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit.

## Slide 88
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Conclusion
4.6
Recommendation
Add bicycle parking
- Results from the indicator of bicycle parking
As to the bus lines and frequency, reduce the overlap rate between bus lines and rail transit lines, improve the transfer function of bus system
- Results from the indicator of bus accessibility and bus capacity
Encourage new construction of apartments around the rail transit station
- Results from the indicator of tenant proportion
Notes: Some recommendations are given according to the result. To increase the utilization of rail transit, it is recommended to adding bicycle parking to attract more passengers who ride bicycles. Reducing the overlap rate of bus lines and rail transit lines can help increase rail transit ridership. And, building apartments around the rail transit station can help increase the utilization of rail transit.

## Slide 89
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
Background
Station level
Station-to-station level
Notes: At the beginning, I want to repeat it once again that why I focus on the ridership between station and station.
There is a station A, if the ridership of station A varied because of the variation in the elements within the catchment area of station A, it is obvious, the transit ridership of station B will also vary, because station A is connecting with station B, the variation of transit ridership in Station A must bring new variation in Station B.
With this issues, the purpose of this study is proposed, Exploring how the factors of land-use influence the choice of destination station for passengers from the perspective of TOD

## Slide 90
Conclusion
5.6
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Recommendations
It is recommended paying more attention to the location of rail transit stations while judging the site selection of a newly planned school.
- Results from finding 3
For low-density residence type stations, it is recommended that promoting the utilization of rail transit could start with other measures, such as fare adjustment.
  - Results from finding 2
Notes: Based on the findings in this study, some recommendations can be raised for future planning.
It is recommended paying more attention to the location of rail transit stations while judging the site selection of a newly planned school.
For low-density residence type stations, it is recommended that promoting the utilization of rail transit could start with other measures, such as fare adjustment.

## Slide 91
Passenger flow between two stations is determined by the transit ridership of both the two stations.
Passenger flow will not increase with the increase of transit ridership in station B.
Introduction
5.1
Passenger flow
Station A
Station B
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Transit ridership
Station B >> Station A
Notes: Because the passenger flow between two stations is not only determined by one station, it is affected by the transit ridership of both two stations.
I’d like to show an example to help explain it.
Now if we investigate two stations, A and B. Station A has a small scale of transit ridership, but the transit ridership of station B is much larger than that of station A. Limited by the transit ridership of station A, the passenger flow will not always increase with the increase of transit ridership in station B.

## Slide 92
Conclusion
6.0
Chapter 6 - Conclusion
Summary
Chapter 2 discussed how the walking duration to rail transit station is affected by passenger attributes. Centering with this topic, 3 specific research questions are proposed according to the previous studies, then the answers to each question were given.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
One

## Slide 93
Conclusion
6.0
Chapter 6 - Conclusion
Summary
Chapter 3 summarized the characteristics of rail transit ridership and land use in the case of Fukuoka, which helped to make a comprehensive understanding of the research object in this dissertation. This chapter also gave some important reference and implication for the next research.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Two

## Slide 94
Conclusion
6.0
Chapter 6 - Conclusion
Summary
Chapter 4 explored and estimated the influencing factors on rail transit ridership at the station level. With the focus on the case of Fukuoka with small sample size, this chapter proposed improved approach from indicator system, valid indicator selection, and model estimation three aspects, and the results are proved effective and improved.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Three

## Slide 95
Conclusion
6.0
Chapter 6 - Conclusion
Summary
Chapter 5 gave a description for the passenger flow between station and station that use the land use type around a station to explain the probability of choosing that station as the destination station. Then ran logistic regression to estimate the influence of land use on the probability of getting off at the destination station. The influence of land use on the transfer of ridership between station and station is confirmed in this chapter.
Based on the theme of exploring the determinants on rail transit utilization in Fukuoka City, this study discussed 4 major issues.
Four

## Slide 96
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Recommendations
6.2
Station
A
C
B
11 min
7 min
5 min
Block
Estimation of catchment area
Prediction of transit ridership
Using the estimated catchment area to make prediction of transit ridership
Using the results of ridership transfer between station and station to correct the prediction of ridership at single station
Application of the achievements
Model
The trend (probability) of using this station in the blocks can be mastered.
PSDC data in the blocks
input
output
Estimating the catchment area
Notes: Now we get the conclusion of this study.
In summary, this study estimated the probability of accepting the given threshold of waling duration to rail transit stations.
Well, what can we do with this achievement?
I will give an example. We have a station in the center, and three blocks around this station, the distances to this station are different. Now if we have the data of personal attributes in each block, we can input this dataset to the model we have got in chapter 2, and then get the trends of using this station in each block.
With this output, obviously, the catchment area of the station can be estimated.
This is the contents of chapter 2.

## Slide 97
Organization
0.0
Introduction
Chapter 1
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Analysis on the characteristics of transit ridership and land use
Influencing Factors on Transit Ridership at Station Level
Influencing Factors on Transit Ridership at Station-to-Station Level
Conclusion
Chapter 6
Chapter 5
Chapter 4
Chapter 3
Chapter 2
Notes: At the first, I want to give an overview for the organization.
This dissertation is organized by 6 chapters.
Chapter 1 is introduction….

## Slide 98
Chapter 1 - Introduction
Research contents
1.3
Exploring the factors influencing rail transit ridership from multiple perspectives and estimating the influence.
Utilization of rail transit
Main purpose
Exploring the factors influencing the ridership at station level
Question
Chapter 4
Exploring the factors influencing the ridership transfer between station and station
Question
Chapter 5
Clarifying the characteristics of ridership and land use
Question
Chapter 3
Research questions
Exploring the factors influencing Walking duration
Question
Chapter 2
Notes: With these transportation problems, it’s clear that we have the demand to promote the use of public transit.
And that is what I want to talk about in this dissertation.
The theme is to explore the influencing factors of rail transit ridership.

## Slide 99
Chapter 1 - Introduction
Background
1.1
Problems
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3
Chart: Population estimation of Fukuoka
| 1985 | 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
0-14 years old | 252 | 231 | 205 | 191 | 188 | 192 | 201 | 204 | 201 | 189 | 176 | 168 | 165 | 164
15-64 years old | 816 | 886 | 933 | 968 | 984 | 998 | 1002 | 996 | 996 | 993 | 975 | 937 | 901 | 870
65 and older | 91 | 113 | 142 | 178 | 213 | 254 | 322 | 367 | 395 | 422 | 454 | 497 | 524 | 539
unknown | 1 | 7 | 5 | 4 | 16 | 20 | 0 | 1 | 0 | 0 | 1 | -1 | 0 | 0
sum | 1160 | 1237 | 1285 | 1341 | 1401 | 1464 | 1525 | 1568 | 1592 | 1604 | 1606 | 1601 | 1590 | 1573
Notes: This research uses the Fukuoka public rail transit as the study case to examine the influencing factors on ridership.
At the very beginning, I’d like to give an introduction of the background in Fukuoka.
Nowadays, even though Fukuoka is still in a rapid growth, there are also many social problems that Fukuoka is facing now.
One of that is the aging population, this figure gives the prediction of Fukuoka’s population in tens years. As we can see, The population of that in production age has reached the peak recently, and the total population will reach the peak in ten years. The population structure is not optimistic in Fukuoka.

## Slide 100
Aged society
Low birthrate
Fiscal burden
Urbanization
Congestion, pollution
Lack of resources
Chapter 1 - Introduction
Background
1.1
Developed Countries
Developing Countries
sustainability
Increasing supply
Improving financial situation
Exploring the determinants of rail transit ridership
Increase public transportation utilization
How is the research topic proposed ?
Status quo
Demand
Measure
Topic
Notes: As we know, nowadays, most of the cities either in developing countries or developed countries, are facing somewhat social problems. I can give a familiar and obvious instance, my country, China, now is still at the period of rapid urbanization, many problems like traffic congestion, air pollution, are not solved yet, while Japan, where now I’m living in, has totally different social problems, like serious aged society, low birthrate, heavy fiscal burden. Therefore, the developing countries like China have more demands on resource and environment protection, while developed countries like Japan need to improve financial situation. However, the demands of both developing and developed country can be viewed as sustainability. For this common demand, promoting public transportation is widely accepted as one of the most important measures.
With the goal of increasing public transportation utilization, the topic was proposed, that is exploring the determinants of rail transit ridership.

## Slide 101
Chapter 1 - Introduction
Research purpose
1.2
Primary questions
What influence the walking duration to transit stations?
1
What factors explain transit ridership at station level?
2
What factors influence the transit ridership between station and station?
3
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: 0. Around this topic, there are 3 primary questions to answer.
1. The first one is what influence the walking duration to transit stations? Since most travel accessing the transit station is walking, the walking duration should be one of the most important factors influencing the ridership.
2. The second is what factors explain transit ridership at station level? As we know, the environment around a station of cause can affect the ridership of this station, so our aim is to find and estimate the influencing factors.
3. Based on the second question, because stations are in the network, the ridership in one of the stations varied, the ridership in other stations must vary as well. Here the third question is proposed, that is what factors influence the transit ridership between station and station.
00. These are the primary questions in this dissertation

## Slide 102
Year |  | 2004 | 2004 | 2009 | 2010 | 2011 | 2012 | 2013 | 2013 | 2015
Author |  | Chu | Kuby et al. | Taylor et al. | Sohn and Shim | Gutiérrez et al. | Cardozo et al. | Chakraborty et al. | Zhao et al. | Jun et al.
Catchment (walking distance) |  | 400m walking distance | 800m walking distance | N/A | N/A | Distance-decay 800m buffer | 800m walking distance | N/A | 800m radius | 300m,600m,900m radius
Method |  | Poisson Regression | WLS | 2SLS | OLS/SEM | OLS | OLS/GWR | OLS/SEM | OLS | OLS/MGWR
Sample Size |  | 2568 | 268 | 265 | 251 | 158 | 190 | 900 | 55 | 442
Number of Valid Indicator |  | 15 | 11 | 8 | 7 | 9 | 4 | 9 | 11 | 11
Coefficient of determination (Adjusted R2) |  | 0.54 | 0.71 | 0.91 | 0.60 | 0.73 | 0.56 | 0.69 | 0.95 | 0.77
Building environment | Built environment |  |  |  | ● | ● |  | ● | ● | ●
 | Hospital |  |  |  |  |  |  |  | ● | 
 | School/University |  |  |  | ● |  |  |  | ● | 
 | CBD |  | ● |  |  |  |  |  | ● | 
 | Land use mix |  |  |  | ● | ● | ● |  |  | ●
 | Other infrastructures |  | ● |  |  |  |  |  | ● | ●
Transportation Accessibility | Accessibility of pedestrian | ● |  |  |  |  |  | ● |  | 
 | Accessibility of transfer |  | ● |  | ● | ● | ● | ● | ● | ●
 | Road coverage |  |  | ● | ● |  |  |  | ● | 
 | Parking |  | ● |  |  |  |  |  | ● | 
 | Service level of public transit | ● | ● | ● |  | ● | ● |  | ● | ●
 | Locational factor |  | ● |  | ● |  |  |  | ● | 
Demographic and Socioeconomic Environment | Population |  | ● | ● | ● |  | ● | ● | ● | ●
 | Employment | ● | ● | ● | ● | ● | ● | ● | ● | ●
 | Age | ● |  | ● |  |  |  |  |  | ●
 | Tenant proportion |  | ● |  |  |  |  |  |  | ●
 | Race | ● | ● | ● |  | ● |  |  |  | 
 | Income | ● |  |  |  |  |  | ● |  | 
 | Vehicles holdings | ● |  |  |  |  | ● | ● |  | 
 | Fare |  |  | ● |  |  |  |  |  | 
Chapter 1 - Introduction
Literature review
1.3
Points discussed in previous studies
Catchment area
Model
Indicator system
Lack of consideration
Small sample case
The ridership between station and station
Notes: With the primary questions, I will give an overview of the previous studies.
Most studies paid the concentration on catchment area, model construction and estimation, and the indicator system.
But very few studies focus on the small sample case and the ridership transfer between station and station.

## Slide 103
Chapter 1 - Introduction
Research contents
1.4
Specific research topic
Exploring the willingness of walking duration to transit stations regarding passengers’ personal attributes.
Chapter 2
Analyzing the characteristics in the variation of transit ridership.
Chapter 3
Exploring the approach of screening effective influencing factors in small sample case
Chapter 4
Shifting the research perspective, trying to describing the variation of ridership between stations and stations.
Chapter 5
1
2
3
4
Notes: Based on the research purpose and previous studies, 4 specific research topics are proposed, corresponding to the chapters from 2 to 5.
Chapter 2 is Exploring the willingness of walking duration to transit stations regarding passengers’ personal attributes.
Chapter 3 is Analyzing the characteristics in the variation of transit ridership.
Chapter 4 is Exploring the approach of screening effective influencing factors in small sample case
Chapter 5 is Shifting the research perspective, trying to describing the variation of ridership between stations and stations.
This is the introduction of my dissertation.

## Slide 104
Chapter 1 - Introduction
Research purpose
1.2
Explore the determinants of rail transit ridership
Giving reference for increasing the rail transit ridership
What factors influence transit ridership among stations?
Main purpose
Subject topics
What determines catchment area?
What factors explain transit ridership at station level?
Notes: With this topic, I will interpreter the research purpose in details. The main purpose of this research can be briefed to exploring the determinants of rail transit ridership, thus giving reference for increasing the rail transit ridership.
In details, the subject topics discussed in this research mainly have 3 parts. They are, what determines catchment area, what factors explain transit ridership at station level, what factors influence transit ridership among stations.

## Slide 105
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Catchment area
Influencing factor
Research Point
(This Study)
Environment
Behaviors
Personal Socio-Demographic Characteristics
(abbreviated as PSDC)
Walking duration to transit stations
Relationship
The area passengers can accept to walk to the station
Research position
Notes: Before I introduce this research, I want to give a brief position for it. As we know, obviously, the catchment area is a basic determinants for the use of transit station. According to the previous research, catchment area should be determined by various factors, like built-environment, facilities, also people’s behaviors. In this research, we chose the perspective of people’s behaviors to investigate how the catchment area is determined. The walking duration and personal socio-demographic characteristics are used to represent the catchment area and people’s behaviors, respectively.

## Slide 106
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Research position
Behaviors
Acceptable walking duration to rail transit stations
Catchment area
Determine
Walk to the station
How the socio-demographic characteristics influence the acceptable walking duration
Research purpose
Personal attributes
Socio-demographic characteristics
(abbreviated as PSDC)
Walking duration to transit stations
Notes: Since pedestrian accounts most rail transit users, the walking distance and duration can determine the catchment area to a large extent. And the walking duration is thought to be affected by the behavior preference, which should be affected by personal attributes like socio-demographic characteristics.
Now we can carry out the main research purpose, How the socio-demographic characteristics influence the acceptable walking duration?

## Slide 107
Threshold of walking duration
Continuous value of Walking duration
Research object
Examine the probability of accepting the given threshold of walking duration
Explore how the PSDC can affect the acceptable walking duration to transit stations using the data of person trip survey.
Research purpose
Entry point
Try to explain the acceptable walking duration using probability.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
The work of this study
Notes: With the interpretation of the existing problems in previous studies, here the research purpose is proposed, that is to explore how the personal socio-demographic characteristics can affect the acceptable walking duration to transit stations using the data of person trip survey.
And different from the existing studies, I investigate the walking duration by some specific threshold value rather than the continuous value. Moreover, the estimation of relationship is not from the perspective of regression but the probability.
That is to say, I will check the probability of choosing walking to transit stations at some specific threshold.

## Slide 108
Threshold of walking duration
Continuous value of Walking duration
Examine the probability of accepting the given threshold of walking duration
Entry point
Try to explain the acceptable walking duration using probability.
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
Research object
Acceptable walking duration
Where the is the acceptable walking duration for the people with those factors
Notes: With the interpretation of the existing problems in previous studies, here the research purpose is proposed, that is to explore how the personal socio-demographic characteristics can affect the acceptable walking duration to transit stations using the data of person trip survey.
And different from the existing studies, I investigate the walking duration by some specific threshold value rather than the continuous value. Moreover, the estimation of relationship is not from the perspective of regression but the probability.
That is to say, I will check the probability of choosing walking to transit stations at some specific threshold.

## Slide 109
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Selection of valid features
2.4
The thresholds selected in this study is 5, 8, 13 minutes.
According to the existing studies, the acceptable walking duration mainly range from 5 – 13 minutes.
In this study, the average walking duration is about 8 minutes.
L : tend to spend Less than the threshold
M: tend to spend more than the threshold
Valid Features at each threshold
Selection of thresholds
Analysis of variance
Notes: It has been said in the former slides, the research objects are some specific threshold of walking durations.
According to the previous research and the investigation of Fukuoka, the acceptable walking duration mainly range from 5-13 minutes, and the average duration is about 8 minutes in Fukuoka.
Therefore, the threshold of walking duration to be investigated are set to 5, 8. 13 minutes.
Regarding the three thresholds, I picked the valid factors at each threshold, by using the analysis of variance.
For this table, in the column of effect, the cell marked with L means people with this attributes tend to accept a longer time than this threshold, M is the opposite.
For example, at the 5 minutes threshold, we can see that passengers who has the attributes of peak hour, and purpose of commuting to work tend to walk a less time than the given threshold of 5 minutes.

## Slide 110
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Evaluation of features
2.5
Individual Value |  | Group Trend | 
Actual | Prediction | Actual | Prediction
1 | 1.000 | 0.654 | 0.637
1 | 0.897 | 0.653 | 0.636
1 | 0.897 | 0.651 | 0.635
… | … | … | …
0 | 0.621 | 0.581 | 0.580
1 | 0.621 | 0.581 | 0.579
1 | 0.621 | 0.580 | 0.579
… | … | … | …
0 | 0.498 | 0.435 | 0.411
1 | 0.496 | 0.437 | 0.411
1 | 0.496 | 0.434 | 0.410
… | … | … | …
The predicted result is probabilities of accepting the giving threshold of walking duration.
The accuracy of results are evaluated by using the method of simple moving average.
Simple moving average
Prediction
200 records
Average
Notes: The result of decision tree is as shown in the figure. Here I just give a summary of the result to show.
As shown in the table on the right part, column of actual is the actual choice of individual, the prediction column is the value obtained from the estimation of decision tree.
The results are evaluated by using the method of simple moving average.
Sort the result by probability in descending order, the group trend is expressed by the average value of 200 samples.
So the trends between practice and prediction can be compared.

## Slide 111
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of prediction
Evaluation of 13 minutes threshold
Slightly high precision
The threshold of 13 minute is not a commonly acceptable walking duration
Some one who can accept this threshold can be considered to have some specific characteristics.
The features are significant at this threshold.
Notes: Next is the evaluation at 13minutes threshold.
We can see the precision is neither good not bad.
A little like the result at 5 minutes threshold, because the threshold of 13 minute is not a commonly acceptable walking duration. Some one who can accept this threshold can be considered to have some specific characteristics. This significant difference from the other passengers explains this fitness at 13 minutes threshold.

## Slide 112
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 5 minutes threshold
The features are significant at 5 minutes threshold.
The threshold of 5 minute is a commonly acceptable walking duration.
Good fitness
Evaluation of prediction
Notes: Continuously, I will show the trend line of prediction at each threshold of walking duration.
First is the 5 minutes threshold.
As we can see, the prediction trend line fit the actual trend line quite well, the features are significant at this threshold.
The threshold of 5 minute is a commonly acceptable walking duration

## Slide 113
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 8 minutes threshold
The features are not significant at 8 minutes threshold.
There is randomness in choosing whether accepting the 8 minutes walking duration or not.
Low fitness
Evaluation of prediction
Notes: Next is the 8 minutes threshold.
The fitness at 8 minutes is not well, the features are not significant at this threshold.
There is randomness in choosing whether accepting the 8 minutes walking duration or not.

## Slide 114
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Result and Discussion
2.6
Evaluation of 13 minutes threshold
The features are significant at 13 minutes threshold.
The threshold of 13 minute is not a commonly acceptable walking duration
Good fitness
Evaluation of prediction
Notes: The fitness at 13 minutes is not bad.
From the probability we can know the 13 minutes is not a commonly accepted walking duration.

## Slide 115
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 116
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 117
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3

## Slide 118
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Land use characteristics
Factor analysis
Purpose
To deal with the strong collinearity among indicators
Further explore the internal relationship
Test for factor analysis
Suggested value
> 0.7
Suggested value
< 0.05
KMO and Bartlett’s Test
PASSED the test
Notes: To deal with this linear correlation, the factor analysis is conducted to make a further exploration on the internal relationship.
According to the test for factor analysis, this dataset is thought to be suitable to do factor analysis.

## Slide 119
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Introduction
3.1
Problems
Background
Reduction in share rate of public transit
1
  Aging population
2
Traffic congestion
3
Demands
Promoting the use of rail transit
Alleviating the pressure on government finances

## Slide 120
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Type | Station No. | Population-density | Office | Commerce | Residence | Education
Low-density residence | 30 | 33 | 1.70% | 41.50% | 44.95% | 0.18%
 | 26 | 54 | 2.81% | 1.23% | 58.26% | 2.85%
 | 29 | 78 | 3.02% | 5.40% | 75.86% | 6.94%
 | 27 | 79 | 4.30% | 4.24% | 75.87% | 0.77%
 | 28 | 81 | 3.55% | 3.42% | 73.46% | 6.24%
 | 3 | 91 | 4.01% | 8.58% | 59.97% | 6.25%
 | 33 | 101 | 1.74% | 2.10% | 81.71% | 7.84%
 | 24 | 103 | 2.14% | 2.17% | 66.82% | 8.30%
 | 34 | 109 | 2.38% | 3.28% | 86.12% | 0.86%
Land use characteristics
Station classification based on land use
Low-density residence
Low population-density
High proportion of residence
Notes: According to the analysis of land use indicators, all the 35 stations are classified into several types.
The first is low-density residence, with Low population-density, and High proportion of residence

## Slide 121
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
High-density residence
High population density
High proportion of residence
Type | Station No. | Population-density | Business | Commerce | Residence | Education
High-density residence | 19 | 121 | 2.17% | 3.15% | 76.63% | 0.12%
 | 13 | 125 | 11.11% | 6.48% | 46.08% | 4.51%
 | 16 | 142 | 4.59% | 5.03% | 72.75% | 2.68%
 | 18 | 142 | 2.27% | 1.96% | 64.58% | 6.80%
 | 31 | 143 | 4.14% | 2.26% | 54.17% | 18.28%
 | 17 | 144 | 6.02% | 7.28% | 55.45% | 10.60%
 | 12 | 145 | 4.16% | 1.77% | 66.22% | 4.39%
 | 32 | 170 | 1.17% | 1.28% | 73.54% | 9.93%
 | 23 | 193 | 10.00% | 6.18% | 44.52% | 2.56%
Notes: The second is high-density residence, with high population-density, and High proportion of residence

## Slide 122
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Education
High proportion of education
Type | Station | Population-density | Business | Commerce | Residence | Education
Education | 25 | 35 | 1.38% | 2.31% | 30.04% | 39.83%
 | 1 | 56 | 8.70% | 1.91% | 48.01% | 17.89%
 | 35 | 58 | 5.63% | 3.78% | 55.18% | 21.37%
 | 4 | 67 | 4.93% | 3.49% | 33.52% | 14.63%
 | 2 | 77 | 4.03% | 11.75% | 44.03% | 23.24%
 | 5 | 89 | 11.53% | 7.26% | 30.51% | 7.30%
Notes: The third is education, with high proportion education

## Slide 123
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Downtown commerce
High proportion of business
High proportion of commerce
Type | Station | Population-density | Business | Commerce | Residence | Education
Downtown commerce | 9 | 64 | 44.97% | 20.55% | 10.62% | 0.70%
 | 20 | 67 | 34.60% | 36.74% | 11.34% | 1.26%
 | 8 | 67 | 42.97% | 27.86% | 12.23% | 0.59%
 | 11 | 79 | 37.12% | 17.38% | 18.47% | 1.89%
 | 10 | 92 | 30.76% | 26.26% | 15.72% | 1.74%
Notes: Then is downtown commerce, with high proportion in both business and commerce.

## Slide 124
Land use characteristics
Station classification based on land use
Chapter 3 - Analysis on the characteristics of transit ridership and land use
Characteristics of transit ridership and land use
3.3
Office
High proportion of business
Type | Station | Population-density | Business | Commerce | Residence | Education
Office | 15 | 64 | 31.63% | 7.80% | 25.80% | 5.73%
 | 6 | 96 | 34.56% | 17.29% | 21.61% | 1.75%
 | 14 | 105 | 26.97% | 17.27% | 17.61% | 2.80%
 | 21 | 136 | 22.86% | 16.12% | 33.66% | 2.70%
 | 22 | 167 | 21.38% | 12.53% | 36.79% | 2.50%
Notes: Next is the office type, with high proportion in business.

## Slide 125
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Introduction
4.1
Purpose
Explore and explain the factors influencing subway ridership at station level using a small sample case
1
  Improve index system
Propose and reconstruct indicators to improve the index system
Identify valid indicators
2
Propose effective index screening method for small samples
Improve accuracy in estimation
3
Consider the different spatial distribution of indicators in the spatial regression model
Research questions
Notes: The main purpose of chapter 4 is to explore and explain the factors influencing subway ridership at station level using a small sample case.
Around this purpose, this study focuses on three specific topics.
The first one is to propose and reconstruct indicators to improve the index system
Second is to find an approach of identifying the valid indicators for small sample case.
The third one is to consider the different spatial distribution of indicators in the spatial regression model to improve accuracy in estimation.

## Slide 126
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Bus capacity
Bus Accessibility
: is the number of bus lines passing through the th bus station.
: the number of bus stations within catchment area of subway station
: the number of lines in one bus station and
: is the frequency of NO. line at NO. station.
Notes: There are the two indicators about bus system. In this study, I considered the effect of bus system from two opposite parts, one is the bus capacity, and the other one is bus accessibility.
The indicator of bus capacity represents the ability of how many passengers the bus system can transfer, it relates to the number of bus stops, bus lines and the frequency of bus within the catchment area. It is expected to have negative effect on rail transit ridership, since the large bus capacity may share parts of the passengers from rail transit.
The indicator of bus accessibility represents the areas connecting to the bus system within the catchment area. It only relates to the number of bus lines. This indicator is expected to have positive effect on rail transit ridership, since a better accessibility of bus may take more rail transit passengers.

## Slide 127
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
: the average proportion of type land use.
: the type of land use (respectively government, commercial, residence and education)
: the floor area of land use type within catchment area of subway station
The indicator of land-use mix is re-defined into the aggregation of land-use.
Indicators
4.2
Variable interpretation
Land-use Aggregation
Range of PCA | Residence | Office | Commerce | Education | Total
600 | 51.8% | 19.3% | 13.8% | 5.5% | 90.5%
800 | 55.3% | 17.5% | 12.0% | 6.2% | 90.9%
1000 | 57.6% | 16.5% | 10.8% | 6.0% | 90.9%
1200 | 59.2% | 15.5% | 10.2% | 5.9% | 90.8%
Ave | 62.8% | 10.1% | 7.5% | 5.3% | 85.7%
Average
Notes: Let me go on to interpret some of the indicators. Firstly, the variable of land-use aggregation. This indicator is used to describe the variety of land use. Maybe we usually hear about the word of land-use mix, but not aggregation. Here I redefined it. Look at this formula, it represents the spatial distance between the uppercase P and lowercase p, where the uppercase P means the average proportion of each kind of land use, and the lowercase p represents the proportion in the observing station. The higher the indicator A is, the function of land use is more aggregative, which means the land use variety is lower. The reference value of uppercase P is calculated from the average of all the stations in Fukuoka, using the catchment area of 800 meters walking distance.

## Slide 128
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Indicators
4.2
Variable interpretation
Bus capacity
Share passengers from rail transit. Negative effect on rail transit ridership
Bus Accessibility
Bring passengers to rail transit. Positive effect on rail transit ridership
Departure
Departure
Destination
Share passengers from rail transit
Bring passengers to rail transit
Indicators of bus system
Notes: In this study, the indicator of bus system is considered from two aspects.
Like shown in the figure, bus should have two effect on the rail transit, one is bringing passengers to rail transit, and another one is share passengers from rail transit.
The indicator of bus capacity is expected to share passengers from rail transit, having negative effect on rail transit.
The indicator of bus accessibility is expected to bring passengers to rail transit, having positive effect on rail transit.

## Slide 129
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Moran's Index | Z-score | P-value* | Pattern | DIFF of Criterion** | Type
Government Area | 0.04 | 0.66 | 0.51 | Random | - | Global
Transportation Facility | 0.29 | 3.33 | 0.00 | Clustered | -1.95 | Local
Land use Aggregation | -0.01 | 0.20 | 0.84 | Random | - | Global
Transfer Dummy | 0.13 | 1.58 | 0.12 | Random | - | Global
Bicycle Parking | -0.12 | -0.92 | 0.36 | Random | - | Global
Bus Capacity | 0.70 | 7.57 | 0.00 | Clustered | 0.18 | Local
Bus Accessibility | 0.45 | 5.04 | 0.00 | Clustered | 0.04 | Local
Population/Job Balance | 0.77 | 7.61 | 0.00 | Clustered | -0.17 | Local
Tenant Proportion | 0.24 | 2.54 | 0.01 | Clustered | 1.02 | Local
* Statistical significance means autocorrelation
** More than or equal to 2.00, means the local term is better to be assumed as global
Identification for global/local variable
Notes: Before estimating the model, we should determine whether the indicator is a local or global indicator.
This procedure is conducted by using Moran’s index to examine if the variable is spatial autocorrelation or not.
The indicators with clustered pattern are selected as the local variable.

## Slide 130
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Fixed Gaussian kernel function
Chart: AICc
5.7km
Golden-section search
MGRW parameter
Kernel Type
Bandwidth selection method
Ordinary regression
MGRW model
means the weight at the coordinate of
Notes: With these screened indicators, I’m going to estimate the influence on transit ridership quantitively. The transit ridership is not like the common sampling data, it also depends on spatial distribution. Therefore the mix geographically weighted regression is used to deal with the spatial relationship. As we can see the difference between the two formula, beta means the weight at the coordinate of (u, v). The two important parameters in MGRW is set as shown. The bandwidth is set to 5.7 kilometers, which is selected by golden-section search.

## Slide 131
Residual Analysis
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Transportation Facility Area
Bus Capacity
Bus Accessibility
Population Job Balance
Tenant Proportion
Significance Map
Significance Map
Not Significance
P = 0.01
P = 0.05
P = 0.1
Notes: The spatial distribution of significance for each local variable are mapped in Figure 4.4. For the variables of building area of transportation, bus capacity, bus accessibility, job-resident balance and tenant proportion, there are 33, 34, 35, 24 and 32 data points having statistical significance at confidence level 95% respectively. As in the figures, the two indicators for bus that proposed in this study have good performance in terms of significance and stability, while the variable of ‘tenant proportion’ has a little worse stability.

## Slide 132
Model estimation
4.4
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Variable | Type | OLS model |  |  |  | MGWR model |  | 
 |  | B | SE | t |  | B | SE | t
Government Area | Global | 0.05 | 0.02 | 2.41 |  | 0.05 | 0.02 | 2.59
Land Use Aggregation | Global | 11,832.53 | 5323.15 | 2.22 |  | 13,384.34 | 5,408.81 | 2.48
Transfer Dummy | Global | 6,578.09 | 1216.82 | 5.41 |  | 5,968.65 | 1,198.72 | 4.98
Bicycle Parking | Global | 7.51 | 0.93 | 8.11 |  | 7.72 | 0.90 | 8.59
Transport Area | Local | 0.11 | 0.03 | 3.58 |  | 0.10 | 0.02 | -
Bus Capacity | Local | -59.21 | 20.71 | -2.86 |  | -55.14 | 5.94 | -
Bus Accessibility | Local | 50.71 | 14.64 | 3.46 |  | 48.61 | 2.43 | -
Population/Job Balance | Local | -2,762.24 | 1,079.33 | -2.56 |  | -2,411.17 | 364.44 | -
Tenant Proportion | Local | -9,987.81 | 4,380.30 | -2.28 |  | -10,304.66 | 756.09 | -
Best bandwidth |  |  |  |  |  | 5.7km |  | 
AICc |  | 694.39 |  |  |  | 690.60 |  | 
Residual sum of squares |  | 337,744,989 |  |  |  | 296,311,499 |  | 
Estimation of Mix Geographically Weighted Regression
Notes: This is the result of estimation.
As a result, the indicators of building area have a positive effect on the subway ridership.
The indicator of land-use aggregation shows land use variety can lead to decrease in ridership.
As the expectation, the indicator of bus capacity has a negative effect on the subway ridership, and the bus accessibility has a positive effect.
The factor of resident/job balance and tenant proportion tells that working people and tenants are more willing to use subway.

## Slide 133
Model estimation
4.5
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Z-score in MGWR is lower than that in OLS
Moran’s index in MGWR is closer to the expected index than that in OLS
Indicator | OLS | MGWR
Moran’s index | 0.08 | 0.03
Expected index | -0.03 | -0.03
Variance | 0.01 | 0.01
z-score | 1.09 | 0.61
p-value | 0.27 | 0.54
Distribution of residuals
Closer to the expected value is better
Less is better
Notes: This part is the residual analysis.
From the residual distribution, Moran’s index in MGWR is closer to the expected index than that in OLS, Z-score is also lower than that in OLS.
We can say the result of MGWR is better than that of OLS.
The lower part is the distribution of residuals of both linear regression and geographically weighted regression, to have a look if the accuracy increased. The Moran’s index in MGWR is closer to the expected index than that in OLS, and the Z-score in MGWR is less than that in OLS, the accuracy did increase.

## Slide 134
Conclusion
4.6
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Reclassified and reorganized the indicator framework.
Proposed the approach of selecting variables from candidates using the tool of exploratory regression in ArcGIS.
Provided a method for judging whether a variable is global or local used in estimating the MGWR model.
Main works
Main findings
The higher diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.
Notes: For a conclusion, this study reorganized the indicator framework, and proposed a method for selecting valid variables. Also, provided a way for judging whether a variable is global or local in the mix geographically weighted regression model.
Also there are some interesting finding from this study.
The higher diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 135
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
5.1
Background
Station level
Station-to-station level
Notes: At the beginning, I want to repeat it once again that why I focus on the ridership between station and station.
There is a station A, if the ridership of station A varied because of the variation in the elements within the catchment area of station A, it is obvious, the transit ridership of station B will also vary, because station A is connecting with station B, the variation of transit ridership in Station A must bring new variation in Station B.
With this issues, the purpose of this study is proposed, Exploring how the factors of land-use influence the choice of destination station for passengers from the perspective of TOD

## Slide 136
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
 | Scale | Objective
Station-Level | single station | OD pair of stations
Station-to-Station-Level | station network | OD transit ridership
To describe the connectivity between different stations using OD ridership.
To explain how the connectivity is determined by land-use factors.
Description for the research
Differences with station-level
Research contents
Notes: This study is at the station-to-station level, but not station-level. Different from station-level, the research scale shift to station network but not a sing station, the research objective is changed to OD passenger volume but not the passenger volume of single station. The emphasis of station-to-station level is not only the prediction of ridership, but also the connectivity between the station and station.
The research contents mainly have two parts, to describe the connectivity between different stations using OD ridership, and to explain how the connectivity is determined by land-use factors.

## Slide 137
The transit ridership is generated at the origin station, and then transferred to the destination station. But few studies focused on the procedure of passenger transfer between the departure and destination stations.
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Research contents
Problem 1
Using the probability of choosing a specific destination station to describe the transit ridership between station and station.
1
  Describe the transit ridership transfer between station and station
Key points
Problems in previous studies
Notes: According to the review, some problems not well addressed are summarized. Based on which, the key points of this study are proposed. The first one is to find an indicator to describe the passenger transfer between station and station.

## Slide 138
In terms of the methods, the linear regression is not proper to describe and estimate the passenger transfer between stations and stations
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Research contents
Problem 2
2
  Find a proper function to estimate the influencing factors of the passenger transfer of ridership between stations and stations
Convert this issue into the mathematical problem, then estimate the effect of influencing factors.
Key points
Problems in previous studies
Notes: The second key point is about the method. Because the linear regression is not proper to describe and estimate the passenger transfer between stations and stations, this study will try to find a proper method to estimate the influencing factors of the passenger transfer of ridership between stations and stations

## Slide 139
Previous study |  | Type 1 | Type 2 | Type 3 | This
Perspective | Station | ● |  |  | 
 | Station-to-station |  | ● | ● | ●
Research object | Dependent variable | Transit ridership | Transit ridership | Transportation Impedance | Destination selection probability
 | Explanatory variable | Single station | Origin and destination stations | Origin and destination stations | Origin and destination stations
Method | Linear Regression | ● | ● |  | 
 | Gravity model |  |  | ● | 
 | Logistic regression |  |  |  | ●
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Review
Notes: Before the analysis, I want to give a brief review of previous studies to show how this study differs from the others.
This study focused on the relationship between station and station. For the research object, not like the other studies using transit ridership as b

## Slide 140
Introduction
5.1
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Flowchart
Index framework
Dependent variable
Independent variable
Conversion of realistic issue
Discrete choice issue
Logistic regression
Model estimation
Result and Discussion
Probability of getting off at a specific destination station
Notes: This is the research flow of this study.
First, I will construct the index framework, and then convert this realistic issue into a mathematical problem.
Finally, estimate the logistic regression model, and give discussion for the result.

## Slide 141
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Boarding
Alighting
……
Other
Stations
Station 1
……
Station 2
Station k
Choice of whether to get off at station k
Affect
Independent variable
Dependent variable
Description for the research question
land-use feature of boarding station
Impedance between boarding and alighting station
Notes: Before constructing the mathematical model, I am going to explain how to convert this realistic problem into a mathematical problem. If we examine the case of alighting station k, this probability of getting off at station k is affected by the land-use and impedance of boarding station. Here we can convert this problem into a discrete choice problem. And it can be expressed using logistic regression. In this logistic regression, if we take the alighting station k as an example, the dependent variable is the connectivity between all the boarding stations and alighting station k, it is the probability of getting off at station k. The independent variables are the land-use of departure stations and the impedance between boarding stations and the alighting station k.

## Slide 142
Method
5.3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Station type | Station name | Population density | Commerce proportion | Office proportion | Residence proportion | Education proportion
Low-density residence | 賀茂 | 98 Person/Ha | 4% | 3% | 83% | 4%
High-density residence | 藤崎 | 173 Person/Ha | 5% | 7% | 76% | 6%
Education | 箱崎九大前 | 83 Person/Ha | 5% | 6% | 51% | 22%
Office | 呉服町 | 135 Person/Ha | 8% | 31% | 49% | 3%
Commerce | 天神 | 69 Person/Ha | 34% | 32% | 24% | 1%
Note:
The highlighted cells refer to the representative values that having much higher proportion than other land-use types.
Selecting sample station
Notes: In this problem, what we want to know is how the independent variables determine the choice of where to get off.
To master the significant features of choosing destination regarding different type of land-use, I will select some typical stations as research objective.
I chose one station from each of the land use type.
The six stations are Kamo station of medium-density residence
Fujisaki station of high-density residence
Hakozakikyudai station of education
Gofukumachi station of office
Tenjin station of commerce
and airport station.

## Slide 143
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | 0.88 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Result of estimation
Full name of the abbreviation
B-C: Bus Capacity
B-A: Bus Accessibility
L-A: Land-use Aggregation
D: Distance
R: Residence
E: Education
C: Commerce
O: Office
Increase in this type of land use will lead to an increase in the probability of choosing this station as the destination
Increase in this type of land use will lead to a decrease in the probability of choosing this station as the destination
Note
Meaning of the coefficients
1% increase in the proportion of land use will lead to a corresponding variation in the probability of getting off at the destination
Notes: This is the result of estimation.
In this table, the values less than 1 means Increase in this type of land use will lead to a decrease in the probability of choosing this station as the destination
The values larger than 1 means Increase in this type of land use will lead to an increase in the probability of choosing this station as the destination
For the meaning of the coefficients, 1% increase in the proportion of land use will lead to a corresponding variation in the probability of getting off at the destination
. The blank means this value does not pass the statistical significance test.

## Slide 144
Chart: 
| Commerce | Office | Residence | Education | Land use aggregation
Low-density residence 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97
High-density residence 藤崎 | 1.01 | 0.99 | 1.01 | 0.98
Education 箱崎九大前 | 1.02 | 1.02 | 1.03 | 0.99
Office 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99
Commerce 天神 | 1 | 0.99 | 1.01 | 1.03 | 1.02
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Discussion for results
Commerce
Land use aggregation
Education
Residence
Gray areas represent negative effects
All in the white area
All in the gray area
Office
Notes: Then I will give some details for the results.
Look at the values marked with frame.
It means the any type of Land use increased in departure station
The Probability of choosing the destination station belong to low-density residence type will decrease

## Slide 145
Conclusion
5.5
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Main works
In the future
Defined the “connectivity” between station and station
The influence of land use on the connectivity was estimated
The indicator system should be further enriched
The share of different transportation modes should be considered
The indicators belong to impedance should be improved
The influence of bus system also should be considered at the station-to-station level
Notes: This is the chapter 5, the main work of this study includes two parts, Defined the “connectivity” between station and station. The influence of land use on the connectivity was estimated.
Also we got some implications for the future, Further enrich the indicator system. The share of different transportation modes should be considered. The indicators belong to impedance should be improved. The influence of bus system also should be considered at the station-to-station level

## Slide 146
Contributions
6.2
Chapter 6 - Conclusion
Chapter 2
Reinterpreted the implication of surveyed walking distance/duration to transit stations. The surveyed walking distance/duration has no linear relation with people willingness but just the reﬂection of the distance between departures and stations.
Described the correlation between surveyed walking duration and people’s individual characteristics from the view of probability, which can be further applied to the estimation of catchment area of rail transit stations.

## Slide 147
Contributions
6.2
Chapter 6 - Conclusion
Chapter 3
Analyzed the trend of variations in transit ridership, and classiﬁed the sub-way stations of Fukuoka into 5 types in terms of land use. Conﬁrmed the correlations between transit ridership and land use.

## Slide 148
Contributions
6.2
Chapter 6 - Conclusion
Chapter 4
Considered the inﬂuence of bus on rail transit ridership from both the sides of bus capacity and bus accessibility, and veriﬁed that the effect of bus capacity is positive to rail transit ridership, while the effect of bus accessibility is negative.
Proposed the approach of screening valid indicators by introducing the exploratory regression, and conﬁrmed its effectiveness in a small sample case.
Distinguished the local and global variables in MGWR model by examining the spatial distribution of each variable, and the effectiveness was conﬁrmed in the estimation of MGWR model

## Slide 149
Contributions
6.2
Chapter 6 - Conclusion
Chapter 5
By examining the probability of selecting the destination station from all the stations, established a logistic regression model for describing the correlation between stations and stations.
Quantitatively validated the impact of land use types on the selection of destination stations.

## Slide 150
Summary
6.1
Chapter 6 - Conclusion
Analyzed the inﬂuence of various factors on rail transit ridership from station level and station-to-station level respectively.
Provided new explanations for the catchment area of rail transit stations.
Provided an approach for selecting the valid indicators
Proposed a ridership forecasting method with the consideration of interaction among stations and stations
Main findings

## Slide 151
Recommendations
6.2
Chapter 6 - Conclusion
How to increase the use of rail transit
People’s walking preferences have signiﬁcant inﬂuence on the use of rail transit. It is suggested that the design for pedestrian accessibility should also consider the individual characteristics of resident, thus helping increase the use of rail transit.
With the development of rail transit, if viewing from the whole transit system, the positioning of bus system is gradually inclining to be the connection between departures and rail transit. Rather than planning higher capacity for bus transport, it is suggested to plan more accessible bus routes which can help people use rail transit more convenient.
According to the ﬁndings, the more aggregation in land use functions the more demand in rail transit. Thus suggesting to connect more functional regions as possible when making rail transit planning.

## Slide 152
Recommendations
6.2
Chapter 6 - Conclusion
The further research
Enrich indicator system
Combine the estimation of catchment area and the prediction of transit ridership.
Explore how the rail transit affect land use.
Explore the balance condition among various elements in the catchment area of transit stations, including human, resource, land use, transportation etc., providing reference to create the compact city.

## Slide 153
Chapter 1
Introduction
Background
Research contents
Primary research questions
Research purpose
Notes: The chapter 1 is a brief introduction for the whole dissertation

## Slide 154
Chapter 2
Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
Methods
Data description
Selection for Valid Features
Estimation of Features
Result and Discussion
Conclusion
Notes: The chapter 2, Analyzing Willingness of Walking Duration to Transit Stations Using passenger’s personal attributes

## Slide 155
Chapter 3
Analysis on the characteristics of transit ridership and land use
Introduction
Data
Characteristics of transit ridership and land use
Exploration the influence on transit ridership
Conclusion
Notes: Next, Chapter 3, Analysis on the characteristics of transit ridership and land use.

## Slide 156
Chapter 4
Influencing Factors on Transit Ridership at Station Level
Introduction
Indicators
Identification of valid factors
Model estimation
Residual analysis
Conclusion
Notes: Next, chapter 4, Influencing Factors on Transit Ridership at Station Level.

## Slide 157
Chapter 5
Influencing Factors on Transit Ridership at Station-to-Station Level
Introduction
Research object
Method
Results and Discussion
Conclusion
Notes: Chapter 5, Influencing Factors on Transit Ridership at Station-to-Station Level

## Slide 158
Chapter 6
Conclusion
Findings
Recommendations

## Slide 159
Chapter 2 - Analyzing Willingness of Walking Duration to Transit Stations Using Socio-Demographic Characteristics
Introduction
2.1
The question to answer
What influence the walking duration to transit stations?
1
What factors explain transit ridership at station level?
2
What factors influence transit ridership between station and station?
3
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: This study aims to answer the first primary question that I proposed at the very beginning.
That is, what influence the walking duration to transit stations.

## Slide 160
What factors influence transit ridership between station and station?
3
What influence the walking duration to transit stations?
1
Introduction
4.1
The question to answer
What factors explain transit ridership at station level?
2
Chapter 4 - Influencing Factors on Transit Ridership at Station Level
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: Chapter 4 aims to answer the second question that I proposed at the very beginning
it is What factors explain transit ridership at station level?

## Slide 161
What influence the walking duration to transit stations?
1
Introduction
5.1
The question to answer
What factors explain transit ridership at station level?
2
What factors influence transit ridership between station and station?
3
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Station
Station
2
Ridership
Ridership
3
Walking duration
1
Notes: This chapter aims to answer the third question that I proposed at the very beginning, that is What factors influence transit ridership between station and station?

## Slide 162
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: All types
Probability of choosing the destination station belong to low-density residence type: decrease
画成雷达图
Notes: Then I will give some details for the results.
Look at the values marked with frame.
It means the any type of Land use increased in departure station
The Probability of choosing the destination station belong to low-density residence type will decrease

## Slide 163
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: increase in education
Probability of choosing the destination station: increase
Notes: Look at the column of education
It means the Increase in the education land use tends to lead increase in the ridership between station and station.

## Slide 164
Results and discussion
5.4
Chapter 5 - Influencing Factors on Transit Ridership at Station-to-Station Level
Destination Station |  | Variables in Departure Station |  |  |  |  |  |  |  | 
Station Type | Station Name | Land-use |  |  |  |  |  | Impedance |  | 
 |  | C | O | R | E | L-A |  | D | B-C | B-A
Low-density residence | 賀茂 | 0.95 | 0.94 | 0.94 | 0.93 | 0.97 |  | 1.07 | 1.01 | 1.00
High-density residence | 藤崎 | 1.01 |  | 0.99 | 1.01 | 0.98 |  | 0.95 | 1.00 | 1.00
Education | 箱崎九大前 | 1.02 |  | 1.02 | 1.03 | 0.99 |  | -0.13 | 0.00 | 0.00
Office | 呉服町 | 1.02 | 0.98 | 1.02 | 1.06 | 0.99 |  |  | 1.00 | 1.00
Commerce | 天神 | 1.00 | 0.99 | 1.01 | 1.03 | 1.02 |  | 1.06 |  | 1.00
Airport | 空港 | 0.97 | 1.03 | 0.99 | 0.99 | 1.03 |  | 0.92 | 1.00 | 1.00
Discussion for results
Result
Land use increased in departure station: The same type with the that of the destination station
Probability of choosing the destination station: decrease
Notes: Look at the values with frames.
This represent, the probability of choosing a destination has a trend of decreasing between the same type of land use.

## Slide 165
Conclusion
6.1
Chapter 6 - Conclusion
Walking duration
5 minutes is a widely accepted walking duration to rail transit.
Whether accepting the 8 minutes walking duration is ambiguous in passenger’s practical behaviors.
Passengers with the private travel purpose tend to accept the longest walking duration.
Passengers with the commuting travel purpose and during the peak hour tend to arrive at transit station as soon as possible.

## Slide 166
Findings
6.1
Chapter 6 - Conclusion
Valid factors selection in small sample case
Approach of screening valid indicator in small sample case is confirmed to be effective.
High diversity of land use leads to decrease in transit ridership.
The bus system has both positive and negative effects on rail transit ridership.
The tenants are more willing to use rail transit in the case of Fukuoka.

## Slide 167
Findings
6.1
Chapter 6 - Conclusion
Choice of destination regarding land use
Confirmed the influence of land use on the choice of destination.
The probability of choosing a destination has a trend of decreasing between the same type of land use.
The probability of choosing a destination belong to low-density residence type never increase regarding to the variation of land use in the departure station.
Increase in the education land use tends to lead increase in the ridership between station and station.